## Slide 1: JVET-AB0145 EE2-2.6-related: On Decoder-side Affine Model Refinement (DAMR)
J. Chen, R.-L. Liao, X. Li, Y. Ye (Alibaba)

## Slide 2: Problem statement
In last meeting, JVET-AA0144 proposed to refine the motion of affine coded blocks in decoder-side without signaling
  Simply extend DMVR to affine coded blocks
  Only base MV is refined
  Tested as EE2-2.6 and was adopted
Affine model
Non-translation parameters are not refined in EE test.
Base MV
Non-translation parameters

## Slide 3: Proposed method
It is proposed to refine both base MV and non-translation parameters of affine model for affine coded blocks
Proposed algorithm
  The 1st step: base MV refinement, which is exactly the same as EE2-2.6
  The 2nd step: non-translation parameters refinement
    Fix the base MV and search non-translation parameters in the parameter space around the original parameter point
    The parameters with minimum bilateral matching cost (SAD between L0/L1 predictors of the CU) are output as the refined parameters
    Three stages
      Fix top-left CPMV as base MV, do parameter search
      Fix refined top-right CPMV as base MV, do parameter search
      Fix refined bottom-left CPMV as base MV, do parameter search

## Slide 4: Experimental Results
Simulation is conducted under CTC
RA results are shown below
 | Random Access Main 10 |  |  |  | 
 | Over EE2-2.6 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.17% | -0.08% | -0.02% |  | 
Class A2 | -0.20% | -0.19% | -0.16% |  | 
Class B | -0.07% | -0.09% | -0.09% | 108% | 107%
Class C | -0.05% | -0.06% | -0.03% | 102% | 102%
Class E |  |  |  |  | 
Overall | -0.11% | -0.10% | -0.07% |  | 
Class D | -0.09% | -0.21% | -0.05% | 101% | 101%
Class F | -0.02% | 0.03% | -0.07% | 103% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.36% | -0.25% | -0.19% | 121% | 118%
Class A2 | -0.50% | -0.38% | -0.35% | 117% | 121%
Class B | -0.18% | -0.03% | -0.17% | 109% | 109%
Class C | -0.09% | -0.08% | -0.09% | 104% | 103%
Class E |  |  |  |  | 
Overall | -0.26% | -0.16% | -0.19% | 112% | 111%
Class D | -0.11% | -0.18% | -0.10% | 102% | 102%
Class F | -0.04% | 0.00% | -0.07% | 105% | 104%
Anchor: ECM-6.0
Anchor: EE2-2.6

## Slide 5: Conclusion
On top of EE2-2.6, it is proposed to additionally refine the non-translation parameter of affine model for affine coded blocks.
Over ECM-6.0
  Overall, -0.26% luma coding gain with 112%/111% Enc/Dec time
  Higher gain in 4K sequences (-0.50% for class A2)
Over EE2-2.6
  Overall, -0.11% additional coding gain
  Higher additional gain in 4K sequences( -0.17%/-0.20% for class A1/A2)
It is suggested to further study the proposed method in the next round of EE