## Slide 1
JVET-AB0180
Non-EE2: CCCM using non-downsampled luma samples
Hong-Jheng Jhu, Che-Wei Kuo, Xiaoyu Xiu, Wei Chen, Ning Yan, Changyue Ma, Xianglin Wang (Kwai)
Vadim Seregin, Yao-Jen Chang, Bappaditya Ray, Marta Karczewicz (Qualcomm)

## Slide 2: Introduction
In ECM-6.0, besides cross-component linear model (CCLM) and gradient linear model (GLM), convolutional cross-component model (CCCM) is applied to predict the chroma samples from reconstructed luma samples
  The CCCM extends the 2-parameter linear model in the CCLM to 7-tap non-linear model
  One downsampling filter is applied to the reconstructed luma samples to align with the resolution of chroma samples in the CU before the CCCM being applied

## Slide 3: CCCM using non-downsampled luma samples
Chroma samples are directly predicted from the original reconstructed luma samples
For signaling, when the CCCM is selected, one single flag is signaled and used for both two chroma components
C
to-be-predicted chroma sample
-th reconstructed luma sample surround the chroma sample
-th coefficient
offset

## Slide 4: Simulation Results
 | All Intra Main10 |  |  |  | 
 | Over ECM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.40% | -0.32% | 101% | 99%
Class A2 | -0.17% | -0.56% | -0.62% | 102% | 102%
Class B | 0.01% | -0.32% | -0.30% | 101% | 99%
Class C | 0.00% | -0.29% | -0.26% | 102% | 100%
Class E | 0.01% | 0.02% | -0.05% | 101% | 99%
Overall | -0.02% | -0.31% | -0.31% | 101% | 100%
Class D | 0.01% | -0.26% | -0.28% | 102% | 99%
Class F | -0.35% | -1.74% | -1.06% | 101% | 99%
Class TGM | -1.89% | -3.62% | -3.36% | 101% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over ECM6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.01% | -0.08% | 100% | 98%
Class A2 | -0.28% | -0.40% | -0.69% | 100% | 99%
Class B | 0.00% | -0.04% | -0.31% | 100% | 99%
Class C | 0.01% | -0.11% | 0.00% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.05% | -0.13% | -0.26% | 100% | 99%
Class D | 0.03% | -0.32% | -0.16% | 100% | 100%
Class F | -0.51% | -1.52% | -1.11% | 100% | 100%
Class TGM | -0.70% | -1.83% | -1.52% | 100% | 100%

## Slide 5: Conclusion
CCCM using non-downsampled luma samples is proposed where the chroma sample is directly predicted based on the original reconstructed luma samples
Significant luma/chroma gains on screen content sequences with negligible encoding/decoding impacts
Suggest to adopt the proposed method into ECM
Thanks to Alibaba for the crosschecking!