## Slide 1: JVET-AD0134 Non-EE2: Bi-predictive IBC
Y. Kidani, H. Kato, and K. Kawamura (KDDI Corp./KDDI Research, Inc.)

## Slide 2: Summary
Motivation / Background
  Improve the coding performance of IBC
  Currently, IBC generates prediction samples with only one BV, i.e., uni-predictive IBC.
Proposal: Bi-predictive IBCs
  Method 1: IBC BVP-merge mode
  Method 2: Bi-predictive IBC merge mode
Results (Overall of AI)
  Test 1: Method 1 + Method 2 over EE2-1.8a
  Test 2: Method 1 + Method 2 over EE2-1.8c
  Test 3: Method 1 over EE2-1.8a
  Test 4: Method 1 over EE2-1.8c
  Test 5: Test 2 + encoder opt. over EE2-1.8c
 | Y | U | V | EncT | DecT
Test 1 | -0.51% | -0.59% | -0.62% | 109% | 100%
Test 2 | Not completed |  |  |  | 
Test 3 | -0.21% | -0.30% | -0.28% | 101% | 100%
Test 4 | Not completed |  |  |  | 
Test 5 | Not completed |  |  |  | 
Adopted in this mtg.

## Slide 3: Proposal
Overview
  Method 1: IBC BVP-merge mode
    Derivation of BVs: IBC BVP and IBC merge, similar to AMVP-merge
  Method 2: Bi-predictive IBC merge mode
    Derivation of BVs: IBC merge candidate list with two merge indices
    Target of Bi-pred.: IBC regular merge, IBC-MBVD (all sequences) and IBC-GPM (only SCC)
Details
  Merge list construction: Reuse existing IBC merge list
  BV refinement: Enable IBC-TM
  Compensation: Simple (1:1) average
  Signalling: Slice-level control flag in I-slice
BV1
BV2
Bi-predictive IBC-GPM

## Slide 4: Results
 | All Intra Main 10 |  |  |  | 
 | Over EE2-1.8a |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | -0.14% | -0.15% | 107% | 100%
Class A2 | -0.77% | -0.81% | -0.89% | 107% | 100%
Class B | -0.60% | -0.72% | -0.65% | 110% | 100%
Class C | -0.22% | -0.16% | -0.29% | 109% | 100%
Class E | -0.96% | -1.16% | -1.23% | 109% | 101%
Overall | -0.51% | -0.59% | -0.62% | 109% | 100%
Class D | -0.20% | -0.28% | -0.24% | 109% | 100%
Class F | -0.24% | -0.46% | -0.51% | 104% | 100%
Class TGM | -0.51% | -0.19% | -0.17% | 103% | 98%
 | All Intra Main 10 |  |  |  | 
 | Over EE2-1.8a |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.10% | -0.09% | 101% | 100%
Class A2 | -0.37% | -0.46% | -0.46% | 100% | 100%
Class B | -0.26% | -0.36% | -0.29% | 101% | 100%
Class C | -0.08% | -0.11% | -0.14% | 100% | 100%
Class E | -0.37% | -0.49% | -0.47% | 100% | 100%
Overall | -0.21% | -0.30% | -0.28% | 101% | 100%
Class D | -0.06% | -0.18% | -0.07% | 100% | 100%
Class F |  |  |  |  | 
Class TGM |  |  |  |  | 
 | All Intra Main 10 |  |  |  | 
 | Over EE2-1.8c |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.06% | 0.01% | -0.16% | 101% | 100%
Class E | -0.21% | -0.19% | -0.26% | 100% | 100%
Overall |  |  |  |  | 
Class D | -0.05% | -0.07% | -0.07% | 101% | 100%
Class F |  |  |  |  | 
Class TGM |  |  |  |  | 
 | All Intra Main 10 |  |  |  | 
 | Over EE2-1.8c |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.22% | -0.23% | -0.36% | 113% | 102%
Class E | -0.73% | -0.76% | -0.75% | 112% | 103%
Overall |  |  |  |  | 
Class D | -0.19% | -0.33% | -0.29% | 112% | 101%
Class F |  |  |  |  | 
Class TGM | -0.33% | -0.09% | -0.10% | 103% | 98%
Test 3: Method 1 over EE2-1.8a
Test 1: Method 1 + Method 2 over EE2-1.8a
Test 2: Method 1 + Method 2 over EE2-1.8c
Test 4: Method 1 over EE2-1.8c
 | All Intra Main 10 |  |  |  | 
 | Over EE2-1.8c |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.17% | -0.13% | -0.21% | 105% | 101%
Class E | -0.58% | -0.68% | -0.67% | 104% | 102%
Overall |  |  |  |  | 
Class D | -0.15% | -0.28% | -0.25% | 105% | 102%
Class F |  |  |  |  | 
Class TGM | -0.33% | -0.09% | -0.10% | 103% | 98%
Test 5: Test 2 + encoder optimization over EE2-1.8c

## Slide 5: Conclusion
Bi-predictive IBC is proposed to improve coding performance.
Additional coding gains are confirmed over EE2-1.8c adopted in this mtg..
Encoder runtime increase can be reduced with encoder optimization.
It is recommended to study the proposal in the next EE.
Thanks Qualcomm for cross-checking (JVET-AD0313).