## Slide 1: JVET-AD0220: Non-EE2: Improved fixed filters for ALF
Marta Karczewicz, Nan Hu, Vadim Seregin (Qualcomm)

## Slide 2: ALF filtering in ECM-8.0
Taps #0-#19: neighboring reconstructed samples
Taps #20-#27: outputs from two fixed filters f0 and f1
Taps #28-#30: samples before deblocking filters
Taps #31,#32: residual samples

## Slide 3: Fixed filters in ECM-8.0
Laplacian-based classifier
  class index with =0,1 is derived based on activity and directionality
Filters are selected based on
Filters are applied to ALF input samples

## Slide 4: Proposed method
Filters are also applied to samples before deblocking filter
Extended classifier:
  Calculate the variance
  Quantize the variance by a scaling factor based on activity
  Proposed class index
    Combination of activity, directionality and quantized variance
Apply f1 to f0 outputs and samples before deblocking filter

## Slide 5: Results
Filters applied to samples before deblocking filter + extended classifier
Filters applied to samples before deblocking filter + extended classifier + apply f1 to f0 outputs
 | All Intra Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.16% | -0.02% | -0.03% | 98% | 101%
Class A2 | -0.19% | -0.02% | -0.02% | 98% | 102%
Class B | -0.16% | -0.02% | -0.02% | 97% | 101%
Class C | -0.28% | -0.03% | -0.03% | 99% | 101%
Class E | -0.37% | -0.08% | -0.07% | 95% | 101%
Overall | -0.22% | -0.03% | -0.03% | 98% | 101%
Class D | -0.31% | -0.01% | -0.01% | 99% | 100%
Class F | -0.12% | -0.02% | -0.02% | 96% | 100%
Random access Main 10 |  |  |  | 
Over ECM-8.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.25% | 0.10% | -0.07% | 99% | 101%
-0.31% | -0.01% | -0.01% | 100% | 101%
-0.24% | 0.06% | -0.01% | 98% | 100%
-0.47% | -0.03% | -0.10% | 101% | 100%
-0.31% | 0.03% | -0.05% | 99% | 101%
-0.49% | 0.27% | 0.02% | 100% | 101%
-0.23% | 0.03% | -0.07% | 98% | 101%
Low delay B Main 10 |  |  |  | 
Over ECM-8.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.21% | -0.31% | -0.09% | 99% | 104%
-0.44% | 0.30% | 0.07% | 99% | 100%
-0.61% | 0.48% | -0.70% | 98% | 101%
-0.39% | 0.09% | -0.19% | 99% | 102%
-0.57% | -0.72% | -0.40% | 100% | 102%
-0.04% | 0.20% | 0.84% | 100% | 101%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.29% | -0.03% | -0.03% |  | 
Class A2 | -0.20% | -0.02% | -0.02% |  | 
Class B | -0.24% | -0.02% | -0.03% |  | 
Class C | -0.42% | -0.03% | -0.03% |  | 
Class E | -0.45% | -0.07% | -0.07% |  | 
Overall | -0.32% | -0.03% | -0.03% |  | 
Class D | -0.32% | -0.04% | -0.03% |  | 
Class F | -0.25% | -0.03% | -0.03% |  | 
Random access Main 10 |  |  |  | 
Over ECM-8.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.39% | 0.06% | -0.20% |  | 
-0.72% | -0.07% | -0.03% |  | 
-0.81% | 0.29% | 0.17% |  | 
-0.36% | -0.08% | -0.14% |  |