## Slide 1: JVET-AF0166 Non-EE2: Intra TMP fusion probing
Jian-Liang Lin, Po-Han Lin, Hongtao Wang, Yao-Jen Chang,
Zhi Zhang, Vadim Seregin, Marta Karczewicz (Qualcomm)

## Slide 2: Introduction
        In ECM10, Intra TMP candidate list is constructed based on the template matching search.
        In Intra TMP fusion mode, multiple Intra TMP candidates are linear combined:
        Cost-based weighting: (1-5), (6-10), (11-15)
        MSE-based weighting: (1-5), (6-10), (11-15)
        Signalled by intra_tmp_fusion_weight_type and intra_tmp_fusion_idx

## Slide 3: Proposal
        Apply a probing line to select a fusion mode with minimum probing cost from a fusion list.
        An additional flag is signalled to indicate this probing mode.
probing line
Reference block
Template
Fused probing line
Current block
Template

## Slide 4: Simulation Results
 | All Intra Main 10 |  |  |  | 
 | Over ECM-10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.12% | -0.10% | 103.2% | 99.2%
Class A2 | -0.10% | -0.07% | -0.16% | 102.1% | 100.2%
Class B | -0.10% | -0.09% | -0.14% | 102.3% | 102.7%
Class C | -0.09% | 0.06% | 0.07% | 101.9% | 102.6%
Class E | -0.10% | 0.05% | -0.26% | 101.0% | 101.8%
Overall | -0.09% | -0.04% | -0.11% | 102.1% | 101.5%
Class D | -0.03% | -0.01% | 0.05% | 102.2% | 100.2%
Class F | -0.05% | 0.08% | 0.27% | 100.8% | 102.8%
Class TGM | -0.04% | -0.09% | -0.08% | 100.5% | 100.8%