## Slide 1: JVET-AG0233: EE2-related: Adaptive precision for CCALF coefficients
Nan Hu, Marta Karczewicz, Vadim Seregin, Hongtao Wang
Qualcomm

## Slide 2: JVET-AG0233
Luma ALF coefficient in EE2-4.3
  Fractional part of a coefficient
    adaptive with 5, 6, 7 and 8-bit
Proposal: CCALF coefficient
  Reuse the mothed in EE2-4.3
    Fractional part of a coefficient
      adaptive with 7, 8, 9 and 10-bit
 | All Intra Main 10 |  |  |  | 
 | Over ECM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.19% | -0.03% | 99.9% | 100.1%
Class A2 | 0.00% | -0.13% | -0.11% | 99.8% | 100.0%
Class B | -0.01% | -0.22% | -0.37% | 100.0% | 99.6%
Class C | 0.00% | -0.34% | -0.34% | 100.4% | 99.8%
Class E | -0.01% | -0.33% | -0.61% | 99.8% | 99.8%
Overall | 0.00% | -0.25% | -0.30% | 100.0% | 99.9%
Class D | 0.03% | -1.04% | -0.94% | 100.9% | 99.6%
Class F | 0.01% | -0.52% | -0.54% | 99.9% | 99.2%
Class TGM |  |  |  |  | 
Random Access Main 10 |  |  |  | 
Over ECM-11.0 |  |  |  | 
Y | U | V | EncT | DecT
0.01% | -0.18% | -0.52% | 99.8% | 100.6%
0.02% | -0.47% | -0.46% | 99.9% | 99.2%
-0.03% | -0.70% | -1.16% | 100.0% | 99.0%
0.04% | -0.55% | -0.67% | 99.9% | 99.7%
Low delay B Main 10 |  |  |  | 
Over ECM-11.0 |  |  |  | 
Y | U | V | EncT | DecT
0.05% | -0.35% | -0.69% | 100.0% | 99.7%
-0.07% | 0.48% | -0.76% | 99.4% | 100.1%
0.00% | -1.19% | -1.35% | 100.6% | 100.0%