## Slide 1: Non-EE2: On residual adjustments for adaptive loop filters JVET-AH0060
Z. Dai, N. Song, Y. Yu, H. Yu, D. Wang (OPPO)

## Slide 2
In the current ECM-12.0 design, the adaptive loop filters (including ALF and CCALF) are used in the in-loop filter module to improve the coding performance. The in-loop filtering module is shown in Fig. 1. The SAO’s output will be further filtered by the ALF and CCALF.
In EE1, when a NN filter is being applied to reconstructed pictures, a residual offset value is selected and signaled for each color component in the slice header. The offset value candidates are {1, 2}. The residual of NNLF’s output is adjusted by reducing the magnitude of the residual at each pixel by this small offset value before being added to input samples.
Fig. 1: The process of the in-loop filtering module
Introduction
LMCS
DBF
SAO
ALF
CCALF

## Slide 3: Proposed
The process of the proposed method is shown in Fig. 2. A frame level offset can be applied to the output of the adaptive loop filters to reduce the output residual magnitude.
Firstly, the residual image is simply extracted by subtracting the adaptive loop filters’ input from its output. Then the residual is adjusted by reducing the magnitude of the residual with a pixel-wise small offset whose absolute value is larger than 1. Three frame level flags are signaled to indicate whether the residual adjustment method is enabled for Y, U and V components, respectively.
An example of the residual adjustment with offset value 1 is shown in Fig. 3, all the positive residual values larger than 1 are decremented by 1, while all the negative residual values smaller than -1 are incremented by 1.
Fig. 2: The process of the proposed method
Fig. 3: An example of the proposed residual offset adjustment
ALF
CCALF
residual
Residual
Adjustment
residual offset
+1 / -1
-2 | 0 | 3 | 6
1 | 4 | -1 | -5
-1 | 0 | 2 | 5
1 | 3 | -1 | -4

## Slide 4
proposed method over ECM-12.0
 | Random access Main10 |  |  |  | 
 | Over ECM-12.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.01% | -0.10% | 100.3% | 100.8%
Class A2 | 0.02% | -0.03% | -0.03% | 100.4% | 100.9%
Class B | -0.01% | -0.11% | -0.13% | 100.1% | 100.8%
Class C | -0.05% | -0.27% | -0.34% | 100.0% | 100.8%
Class E |  |  |  |  | 
Overall | -0.01% | -0.12% | -0.16% | 100.2% | 100.8%
Class D | -0.09% | -0.15% | -0.22% | 100.2% | 100.6%
Class F | -0.02% | -0.05% | -0.13% | 100.1% | 102.6%
 | Low Delay B Main10 |  |  |  | 
 | Over ECM-12.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.38% | -0.20% | 99.9% | 101.1%
Class C | -0.07% | -0.42% | -0.15% | 99.7% | 100.9%
Class E | 0.03% | -0.32% | -0.37% | 99.6% | 100.2%
Overall | -0.03% | -0.38% | -0.22% | 99.8% | 100.8%
Class D | -0.29% | -0.08% | -1.16% | 99.8% | 101.0%
Class F | -0.10% | -0.14% | -0.66% | 100.1% | 101.7%
Simulation results

## Slide 5
This contribution proposes a residual offset adjustment method for adaptive loop filters. Simulation results show that the proposed method can improve the coding efficiency of ECM with minor complexity increases.
It is suggested to further study this method in EE2.
Thanks to InterDigital for cross-checking!
Conclusions