## Slide 1: JVET-AH0195 EE1-related: Complexity reduction of NN in-loop filters through early cropping
J. Ström, M. Damghanian, D. Liu, P. Wennersten (Ericsson)

## Slide 2: Background
Current LOP.2 structure
picture
144x144
128x128
Neural network
144x144
128x128
Crop to
128x128
128x128
+
128x128
final output
NN output

## Slide 3: Background
Current LOP.2 structure
picture
144x144
128x128
Neural network
144x144
128x128
Crop to
128x128
128x128
+
128x128
final output
NN output
Calculated but
never used

## Slide 4: Proposed structure in JVET-AH0195
picture
144x144
128x128
Neural network
128x128
+
128x128
NN output
final output

## Slide 5: Proposed structure in JVET-AH0195
picture
144x144
128x128
Neural network
128x128
+
128x128
NN output
final output
Neural network outputs the correct size from the start

## Slide 6
36x36
(a) 144x144
(b) 72x72
(c) 72x72
(d) 72x36
(e) 36x36
(f) 36x36
(i) 36x36
(j) 72x72
(k) 144x144
(l) 128x128
Current EE1-1.2 (and EE1-1.3) architecture

## Slide 7
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
CONV 3x3 using padding=(1,1)
CONV 3x3 using padding=(0,0)
Current
Proposed
In: 36x36 samples Out: 36x36 samples
In: 36x36 samples Out: 34x34 samples

## Slide 8
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
CONV 3x3 using padding=(1,1)
CONV 3x3 using padding=(0,0)
Current
Proposed
In: 36x36 samples Out: 36x36 samples
In: 36x36 samples Out: 34x34 samples
Same 3x3 weights and biases can be used.

## Slide 9
(a) 144x144
(b) 72x72
(c) 72x72
(d) 72x36
(e) 36x36
(f) 36x36
(g) 36x34
(h) 34x34
(i) 32x32
(j) 64x64
(k) 128x128
(l) 128x128
crop
crop
Proposed architecture

## Slide 10
(a) 144x144
(b) 72x72
(c) 72x72
(d) 72x36
(e) 36x36
(f) 36x36
(g) 36x34
(h) 34x34
(i) 32x32
(j) 64x64
(k) 128x128
(l) 128x128
crop
crop
Proposed architecture

## Slide 11: Changes done
We converted existing checkpoints for LOP.2 and EE1-1.3 to new SADL-int16 models
  Exactly the same weight- and bias values
  Padding (1,1) exchanged with (0,0) in strategic places
We changed the NNVC software so that it does not do cropping of the NN output
We changed SADL so that it can handle padding=(0,0)

## Slide 12: Results
Bit exact results
  Matching md5sums when decoding bitstreams created using the original EE1-1.3 or LOP.2 models.
Some lowered decoder runtime in the LOP.2 case
Proposed on top of EE1-1.3 over EE1-1.3
 | All Intra Main10 |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-1.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 99%
Class B | 0.00% | 0.00% | 0.00% | 100% | 99%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E | 0.00% | 0.00% | 0.00% | 100% | 101%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 99%
Class F | 0.00% | 0.00% | 0.00% | 100% | 99%
 | Random access Main10 |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-1.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class B | 0.00% | 0.00% | 0.00% | 100% | 99%
Class C | 0.00% | 0.00% | 0.00% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 100% | 99%
Class D | 0.00% | 0.00% | 0.00% | 100% | 99%
Class F | 0.00% | 0.00% | 0.00% | 100% | 98%
 | Random access Main10 |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-1.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 93%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 93%
Class B | 0.00% | 0.00% | 0.00% | 100% | 96%
Class C | 0.00% | 0.00% | 0.00% | 100% | 97%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 100% | 95%
Class D | 0.00% | 0.00% | 0.00% | 100% | 98%
Class F | 0.00% | 0.00% | 0.00% | 100% | 97%
Proposed on top of LOP.2 over NNVC8.0
 | All Intra Main10 |  |  |  | 
 | BD-rate Over VTM-11.0_nnvc-1.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 96%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 97%
Class B | 0.00% | 0.00% | 0.00% | 100% | 98%
Class C | 0.00% | 0.00% | 0.00% | 100% | 98%
Class E | 0.00% | 0.00% | 0.00% | 100% | 95%
Overall | 0.00% | 0.00% | 0.00% | 100% | 97%
Class D | 0.00% | 0.00% | 0.00% | 100% | 97%
Class F | 0.00% | 0.00% | 0.00% | 100% | 98%

## Slide 13: Results
Complexity in kMAC/pixel
  EE1-1.3-version: 16.76 kMAC/pixel, (down from 16.90 kMAC/pixel): -0.8%
  LOP.2 version: 16.86 kMAC/pixel, (down from 17.80 kMAC/pixel): -1.1%

## Slide 14: Summary
Uses padding = (0,0) to avoid unnecessary calculations
Weights from existing models can be reused – no retraining needed.
Bit-exact identical results obtained
Complexity reduction in kMAC/sample:
  A reduction of 0.8% (when applied on top of EE1-1.2 or EE1-1.3 model)
  A reduction of 1.1% (when applied on top of LOP.2 model)
We propose to adopt this into LOP.3.
Thanks to Interdigital for crosschecking (JVET-AH0334)