## Slide 1: Film grain synthesis demos
JVET 34th meeting / MPEG146

## Slide 2: Contents
Introduction
  What is film grain, encoding issues, grain synthesis
VFGS
  A hardware-friendly film grain synthesizer
  Low HW cost, reference model in C
  Supports different grain models
Demos
  Grain model and tuning tool
  VVC web player (live decode) with grain synthesis
    Rate savings by using grain synthesis instead of attempting to code the grain natively: ~90% off !
    Includes hiding some coding defects

## Slide 3: Introduction
What is film grain
Is is hard to compress
Film grain synthesis
Stakes and current actions

## Slide 4: What is film grain ?
4000 dpi scanner output
1 pix = 6.4 μm
Fuji S400 film (still picture)
Raw negative
150x microscope view
1 pix = 0.6 μm
Raw negative
500x microscope view
1 pix = 0.16 μm
1mm
100 μm
10 μm

## Slide 5: What is film grain ?
Image formation (microscopic grains)  « film grain » macroscopic texture
Part of original look of films. Artists like it and now add synthetic grain to digital footage: that became an « artistic intent ».
1916 autochrome (13x18 cm glass plate), A. Samama, RMN-GP (France)
24x24 mm crop
2.2x2.2 mm crop

## Slide 6: Problem: encoding removes grain
Grain
Video

## Slide 7: Film grain synthesis
Film grain is removed before/by video compression and film grain characteristics are generated
  Grain / noise is spatially & temporally uncorrelated = costly to encode
  Recent codecs are very efficient denoisers, gains come at that price
Synthesis at decoder side (post-processing) helpful:
  To restore artistic intent, if grain was present in the source video
  To hide compression defects (blurring, blocks, etc)
 subjective quality improvement
  Synthesis follows a defined model, with parameters embedded in the bitstream (metadata = SEI message). Available since AVC

## Slide 8: System architecture
Denoise
Source video
Grain model fitting
Encode
Decode
Add grain
Output video
Bitstream with SEI
Model parameters =
Film Grain Characteristics SEI message
FGC

## Slide 9: System architecture (option 2)
Source video
Grain model fitting
Encode
Decode
Add grain
Output video
Bitstream with SEI
Model parameters =
Film Grain Characteristics SEI message
FGC

## Slide 10: Synthesis example #1
original
decoded
+ synthetic grain

## Slide 11: Synthesis example #2
original
decoded
+ synthetic grain

## Slide 12
Studies / specs in applicative standards
  3GPP: concluding (HEVC + SEI)
  DVB: starting(VVC + SEI)
  SCTE related discussions
Demos + Visual tests
  JVET: started formal visual test of VVC+SEI. Rate savings, grain similarity. Needs more test content.
  DVB: demos by InterDigital in ‘23 and ‘24
  NAB, IBC: demos and test reports by various companies
Publications
Technical report (ISO 23002-9)
  Explains how it works and how to use it
Synthesis implementation
  HW model more flexible + reduced cost vs RDD-5: VFGS (InterDigital)
  Android: libFGS (Ittiam/Dolby)
  Real-time SW needed (SIMD/GPU)
Interoperability
  Translate model parameters
  Graceful degradation (no shape adaptation)
Parameter estimation / tuning
  Should be easy and reliable, to quiclky assess to potential of the technology
Enablers & current actions

## Slide 13: VFGS
Film grain synthesis implementation
A hardware model in C
Interoperable
Good quality and low cost

## Slide 14: Synthesis architecture overview
Get a set of film grain patterns
Generate random block offset
Select pattern
Apply scaling factor
Deblock
Split image into blocks
Blend with target picture
cfg
Offline / firmware
Randomization
Content-adpatation
64x64
Need deblock

## Slide 15: VFGS
Firmware
Model parameters
(e.g. FGC SEI)
vfgs_fw.c / .h
Hardware
Pixel stream (in)
vfgs_hw.c / .h
Pat-terns
Gain LUT
Pattern LUT
Generic hardware interface, pixel-based process suitable for display pipeline (no line buffer)
https://github.com/InterDigitalInc/VersatileFilmGrain
https://vcgit.hhi.fraunhofer.de/jvet-ahg-fgt/vfgs

## Slide 16: Film grain demos
Grain model, tuning tool
Live VVC decode and grain synthesis.
  Savings at top quality: ~90% off !
Side-by-side comparisons

## Slide 17: Film grain experimentation framework
(green = work in progress)