## Slide 1: JVET-AL0220: AHG12: Reuse of ALF control information
Nan Hu, Hongtao Wang, Marta Karczewicz, Vadim Seregin

## Slide 2
ALF control information in ECM-16.1
  Picture level: on/off flags, APS indices
  CTU level: on/off flags, filter index
Proposal
  Reuse of CTU level chroma ALF/CCALF control information from previously encoded frames
  For each chroma component at picture level, flags are signalled for ALF and CCALF reusage decision
  Encoder decision is made independently for each frame
Result
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-16.1 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | 0.16% | 0.28% | 100.2% | 100.0% | 100.0% | 100.1%
Class A2 | -0.04% | -0.02% | 0.11% | 100.3% | 99.8% | 99.3% | 100.5%
Class B | -0.04% | -0.10% | -0.08% | 100.0% | 99.7% | 100.7% | 100.1%
Class C | -0.03% | -0.09% | 0.02% | 99.8% | 100.0% | 100.0% | 100.0%
Class E |  |  |  |  |  |  | 
Overall | -0.04% | -0.03% | 0.06% | 100.0% | 99.9% | 100.1% | 100.2%
Class D | -0.02% | -0.16% | -0.03% | 98.8% | 100.1% | 100.0% | 100.1%
Class F | -0.03% | -0.08% | -0.02% | 99.6% | 99.6% | 99.5% | 100.1%
Class TGM |  |  |  |  |  |  | 
Low delay B Main 10 |  |  |  |  |  | 
Over ECM-16.1 |  |  |  |  |  | 
Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
-0.11% | 0.82% | 0.28% | 99.5% | 99.8% | 100.0% | 99.7%
-0.06% | -0.10% | 0.27% | 99.7% | 100.2% | 100.0% | 100.2%
0.09% | 1.60% | 1.88% | 99.9% | 100.5% | 100.0% | 100.1%
-0.04% | 0.71% | 0.67% | 99.7% | 100.1% | 100.0% | 100.0%
0.05% | -0.74% | -0.29% | 99.7% | 100.0% | 100.0% | 99.8%
-0.05% | 0.07% | -0.05% | 100.4% | 100.0% | 100.1% | 100.3%