## Slide 1: JVET-AM0050 AHG 14: Work on NN-coded Base Layer in VTM / NNVC
F. Brand, T. Solovyev, E. Alshina (Huawei)
F. Urban, F. Galpin (Interdigital)

## Slide 2: Neural Network Coded Baselayer
Combination of NN-based and conventional video coding
Use NN-coded frame as reference
  Allows all coding tools of NNVC to act on top of NN-coded refPic
  Makes use of existing structures within VTM (RefPicList, ML coding)
Framework for ML coding was proposed in JVET-AL0243
  Pass externally NN coded YUV file to encoder and decoder
  Relies on external information for rate computation
  Introduced in AhG11/14 telco
  Just first step of integration, was not really decodable
Mandate during telco to integrate NN bitstream into main bitstream
P
b
B
b
P
Hybrid codec with AI coded RefPic
AI image codec

## Slide 3: Overview of Changes
Including the bitstream for NN coded refPic into the new NAL unit
Decoding AI-coded frame together with hybrid codec (runtime includes both processes)
Encoding AI-coded frame together with hybrid codec (runtime includes both processes)
No need for external reference frames as external yuv file
Normal encoding and decoding is possible
Decoder can be verified
Original functionalities (external yuv, csv,…) are also supported
Easy to link any NN image codec (encoder/decoder) for experiments

## Slide 4: Including bitstream in NAL unit
Turned on by “--IncludeExternalBitstream=1”
If turned on, no rate is added from csv file
Instead bitstream file is read and written into main bitstream with new NAL unit
  Path to bitstream file in csv or from encoder call (see later)
  Rate is taken into account automatically
Works still with additional yuv as input and csv files (if needed)
Only requirement: Individual bitstream files for each frame

## Slide 5: Decoding AI-coded frame at runtime
Only works if AI-Coder NAL unit is present
When NAL unit is encountered:
  Read bitstream from NAL unit
  Write bitstream in “tmp.bin”
  Call bash script “run_NN_decoder.sh “ which calls the neural decoder
  Read resulting yuv frame and copy it into the reconstructed picture buffer of Layer 0
External YUV path does not have to be passed to decoder
Ensures that bitstream is decodable!
To use different decoder: Modify “run_NN_decoder.sh”
Example script “run_AI_decoder.sh”

## Slide 6: Encoding AI-coded frame at runtime
Turned on by “--EncodeAIReference=1”
Write original frame into yuv file
Call bash script to run external encoder
Read reconstructed frame from resulting yuv and set it as reconstructed frame
Read bitstream file and include in the main bitstream
No need for external yuv sequence and csv files

## Slide 7: Results
Due to current restrictions of framework: Test only on first I frame of sequence with LMCS off (both test and anchor)
NN-based coder: DCVC-FM intra coder
Results similar to results obtained in previous contributions (JVET-AL0196, JVET-AK0177, JVET-AJ0208)
Bug: Rare decoding mismatch for two Class A sequences
Further work is planned in the next meeting circle
 | All Intra Main10 |  |  |  |  |  |  | 
 | BD-rate Over VTM 23.9 |  |  |  |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-MSIM | U-MSIM | V-MSIM | EncT | PSNR Overlap
Class A1 | 2.88% | 13.99% | 0.72% | -1.53% | 5.22% | -5.08% | 168% | 100%
Class A2 | -8.90% | -6.08% | 4.37% | -9.38% | -11.01% | -1.08% | 86% | 100%
Class B | -2.74% | -13.25% | -10.37% | -4.70% | -21.68% | -16.58% | 89% | 100%
Class C | -4.31% | -14.25% | -11.01% | -12.37% | -26.07% | -24.86% | 37% | 100%
Class E | -7.56% | -18.83% | -23.62% | -11.53% | -25.89% | -31.14% | 85% | 100%
Overall | -3.98% | -8.66% | -8.42% | -7.79% | -17.10% | -16.35% | 80% | 100%
Class D | -6.19% | -17.01% | -16.23% | -13.05% | -28.86% | -29.52% | 41% | 100%

## Slide 8: Summary
Added features to framework
  Including the bitstream in new NAL unit (fully decodable)
  Actual decoding AI-coded frame together with NNVC decoder
  Actual encoding AI-coded frame together with NNVC encoder
  Experiments with other AI image codec are possible
Preliminary results
  Roughly matches previously reported performance
To do during next meeting circle
  Bugfixes
  Extend to longer than single frame test (bug of a frame work)
  Align with LMSC