## Slide 1
JVET-AM0169: Non-EE2: Reducing Candidate Modes In DDCCP
Shuai Wan, Yujie Yin, Zhiwei Zhu (NWPU)
Shaowei Xie, Xing Zeng, Cheng Huang (ZTE)

## Slide 2
Introduction
In ECM17.0, Decoder-Derived Cross-Component Prediction (DDCCP) derives the best CCP mode by calculating and comparing the template costs of candidate modes.
In the current ECM version, Local-Boosting Cross-Component Prediction (LB-CCP) filterting is only applied to multi-model CCLM and CCCM, not to single-model CCCM.

## Slide 3
Proposed method
This contribution proposes to remove the modes of S-CCCM with LB-CCP and M-CCCM with LB-CCP from the DDCCP candidate list, i.e., to remove the filtering process of LB-CCP in DDCCP.
The CCP Mode list of DDCCP is changed from {S-CCLM, S-CCCM, S-CCCM with LB-CCP, M-CCCM, M-CCCM with LB-CCP, S-GLCCCM} to {S-CCLM, S-CCCM, M-CCCM, S-GLCCCM}. The fusion process in DDCCP remains unchanged.

## Slide 4
Proposed method
 | Number of non-Fusion modes | Number of Fusion modes | Total Number
Original DDCCP | 6 | 15 | 21
Proposed Method | 4 | 6 | 10
Reduction | 2 | 9 | 11
The proposed method simplifies the DDCCP derivation process:

## Slide 5
Experimental results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-17.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.01% | -0.12% | -0.03% | 99.4% | 99.3% | 100.0% | 99.9%
Class A2 | 0.00% | -0.11% | -0.10% | 99.2% | 99.5% | 100.0% | 100.0%
Class B | 0.01% | -0.20% | -0.11% | 99.8% | 98.8% | 100.0% | 100.0%
Class C | 0.02% | -0.11% | -0.08% | 100.0% | 99.0% | 100.0% | 100.0%
Class E | 0.04% | -0.06% | -0.25% | 100.3% | 100.0% | 100.0% | 100.0%
Overall | 0.02% | -0.13% | -0.11% | 99.7% | 99.3% | 100.0% | 100.0%
The reported decoding time is the mean value calculated from ten decoding trials.

## Slide 6
Conclusion
To reduce the complexity of the DDCCP derivation process and improve the codec efficiency, this contribution proposes to remove the filterting process of LB-CCP in the DDCCP.
On top of ECM-17.0
  AI(Y/U/V): 0.02% / -0.13% / -0.11%, EncT 99.7%, DecT 99.3%
It is suggested to investigate in EE.

## Slide 7
Thank you