## Slide 1: JVET-AM0285
Yaxian Bai, Menghu Jia, Weihong Niu, Shaowei Xie, Cheng Huang
AHG12: Reuse of TALF control information

## Slide 2: Introduction
In ECM-17.0, TALF operations are controlled at both the Slice-level and CTB-level.
Slice-level:
  talf_enabled_flag
  talf_use_new_filter_flag
  talf_aps_id
  talf_mode
CTB-level:
  talf_ctb_flag
  talf_aps_index
  talf_aps_filter_index

## Slide 3: Proposal
This contribution proposes a method to store TALF control information of the current frame for potential reuse in future frames.
Syntax changes
  One flag at slice level to indicate whether to reuse the TALF control information of the previously encoded frame.
Similarity comparison
  At the encoder side, the similarity between the current frame and the previously encoded frame is evaluated by comparing the ALF CTB on/off status. The similarity score is defined as the percentage of CTBs with identical statuses relative to the total number of CTBs.
  If the similarity score falls below 0.2, reuse of TALF control information will be disabled.

## Slide 4: Results
Over ECM17.0 |  |  |  |  |  |  |  |  |  |  | 
 | Random Access Main 10 |  |  |  |  | Low delay B Main 10 |  |  |  |  | 
 | Y | U | V | EncT | DecT |  | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  | Class A1 |  |  |  |  | 
Class A2 |  |  |  |  |  | Class A2 |  |  |  |  | 
Class B | 0.00% | -0.03% | 0.00% |  |  | Class B* | 0.00% | -0.04% | 0.05% |  | 
Class C | -0.02% | -0.02% | -0.01% |  |  | Class C | -0.02% | 0.04% | 0.20% |  | 
Class E |  |  |  |  |  | Class E | -0.05% | 0.44% | 0.30% |  | 
Overall |  |  |  |  |  | Overall | -0.02% | 0.11% | 0.16% |  | 
Class D | -0.01% | -0.01% | -0.03% |  |  | Class D | 0.04% | 0.62% | 0.73% |  | 

## Slide 5: Conclusion
This contribution introduces a method to reuse TALF control information from previously encoded frames, which has the potential to improve coding performance.
It is suggested to study in EE.
Thanks to OPPO and Nokia for cross-checking.

## Slide 6: Thank you