## Slide 1: A Bitstream Extension Mechanism for New Technologies Based on Video Coding
Yiyi Liao (Zhejiang University)
Lu Yu (Zhejiang University)
Xin Jin (Tsinghua SIGS)
Lili Zhao (China Mobile)

## Slide 2: Overview
Proposal: Utilize existing extension mechanisms in VVC/HEVC syntax to embed bitstreams of new technologies, e.g., LVC and GSC
Decoupled design: Decoding processes for new technologies do not change VVC/HEVC standards; they reside in respective LVC/GSC standards

## Slide 3: Motivation
Existing video-codec extensions (e.g., V-PCC, MIV, VCM) wrap the standard video bitstream inside their respective bitstreams
Requires extra design at the system level to manage and synchronize the various sub-components (e.g., geometry, attributes, or occupancy maps) alongside the video data
VVC/HECV
V-PCC, MIV, VCM, etc.

## Slide 4: Motivation
Proposed solution: Use internal syntax extension mechanisms
  Internal extension points exist in all modern standards (VPS, SPS, PPS, APS) originally for future version tools.
  Legacy decoders can safely discard extended data without crashing, ensuring backward compatibility.
  Maintains single-stream NAL unit structure, reducing coordination overhead at the system level.
VVC/HECV
LVC, GSC, etc.
VVC/HECV
V-PCC, MIV, VCM, etc.

## Slide 5: Existing Extension Mechanisms
video_parameter_set_rbsp( ) { | Descriptor
…… | 
vps_extension_flag | u(1)
if( vps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
vps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
seq_parameter_set_rbsp( ) { | Descriptor
sps_seq_parameter_set_id | u(4)
…… | 
sps_extension_flag | u(1)
if( sps_extension_flag ) { | 
sps_range_extension_flag | u(1)
sps_extension_7bits | u(7)
if( sps_range_extension_flag ) | 
sps_range_extension( ) | 
} | 
if( sps_extension_7bits ) | 
while( more_rbsp_data( ) ) | 
sps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
pic_parameter_set_rbsp( ) { | Descriptor
pps_pic_parameter_set_id | u(6)
…… | 
pps_picture_header_extension_present_flag | u(1)
pps_slice_header_extension_present_flag | u(1)
pps_extension_flag | u(1)
if( pps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
pps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 
adaptation_parameter_set_rbsp( ) { | Descriptor
aps_params_type | u(3)
aps_adaptation_parameter_set_id | u(5)
…… | 
aps_extension_flag | u(1)
if( aps_extension_flag ) | 
while( more_rbsp_data( ) ) | 
aps_extension_data_flag | u(1)
rbsp_trailing_bits( ) | 
} | 

## Slide 6: Suggested Extension Mechanism
Extension mechanism: Specify the syntax extension within different types of NAL units in a new standard
Set extension signaling: e.g., set sps_extension_nbits to non-zero
Leading bit definition: sps_leading_bits_of_extension_data
Pattern definition: if leading bit equals a specific value (e.g., ., '0001’) …
Payload Carriage: … parse sps_ext_data() according to specific standard

## Slide 7: Example: LVC based on latest VVC version
seq_parameter_set_rbsp( ) { | Descriptor
sps_seq_parameter_set_id | u(4)
…… | 
sps_extension_flag | u(1)
if( sps_extension_flag ) { | 
sps_range_extension_flag | u(1)
sps_extension_7bits | u(7)
if( sps_range_extension_flag ) | 
sps_range_extension( ) | 
} | 
if( sps_extension_7bit == '1000000' ) { | 
sps_leading_bits_of_extension_data | u(4)
if (sps_leading_bits_of_extension_data == '0001') | 
sps_lvc_data() // specified in the LVC standard | 
} | 
rbsp_trailing_bits( ) | 
} | 

## Slide 8: Example: LVC based on latest HECV version
seq_parameter_set_rbsp( ) { | Descriptor
sps_video_parameter_set_id | u(4)
…… | 
sps_extension_4bits | u(4)
} | 
if( sps_range_extension_flag ) | 
sps_range_extension( ) | 
if( sps_multilayer_extension_flag ) | 
sps_multilayer_extension( ) /* specified in Annex ‎F */ | 
if( sps_3d_extension_flag ) | 
sps_3d_extension( ) /* specified in Annex ‎I */ | 
if( sps_scc_extension_flag ) | 
sps_scc_extension( ) | 
if( sps_extension_4bits == '1000' ) { | 
sps_leading_bits_of_extension_data | u(4)
if (sps_leading_bits_of_extension_data == '0001') | 
sps_lvc_data() // specified in the LVC standard | 
} | 
rbsp_trailing_bits( ) | 
} | 

## Slide 9: Versioning and Forward Compatibility
The extension sub-bitstream can be inserted not only into the bitstreams of existing versions of VVC/HEVC but also into future versions
VVC/HECV
LVC, GSC, etc.
VVC/HECV
LVC, GSC, etc.
VVC/HECV extension

## Slide 10: Conflict Avoidance and Reservation
We suggest that WG 5 does not define internal extension data using the same leading bit patterns reserved for this mechanism in future versions of VVC or HEVC.

## Slide 11: Advantages
Easy deployment: Reduce coordination overhead at the system level
Decoupled design: HEVC/VVC versions and the new standard can evolve independently
Conformance point: Clearly defined in the new standard

## Slide 12: Recommendation
We recommend that WG 5 agrees to the proposed extension mechanism and establishes a policy to avoid conflicts with the reserved leading bit patterns in future versions of of the base video codec.