## Slide 1: AHG18: Random Access GOP4 Configuration for Live-streaming Applications evaluated in ULL test conditions
Sergey Ikonin, Ivan Gribushin, Maxim Sychev, Kirill Malyshev, Boris Shevchenko, Vyacheslav Khamidullin, Xiang Ma, Elena Alshina, Zhipin Deng
Huawei, Bytedance
JVET-AP0200

## Slide 2: Recap: RA GOP4 for Live Streaming applications
Contribution JVET-AM0238, Deajeon, July, 2025 from Bytedance, Google, Tencent, Disney, Alibaba
Emphasized importance of low latency for Live Streaming applications, such as real-time broadcasting, online events, e-commerce, and interactive services
Suggested Random Access GOP4 configuration as relevant to Live Streaming
Current contribution exercises RA GOP4 in ULL test conditions

## Slide 3: Structural delay and latency restriction
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
E2E Latency
1/fps
8
`
0
4
2
1
3
8
6
5
7
Structural delay: 3 frames (max buffering time of frame 1)
RA GOP4 additional structural delay: 3 frames
Depending of fps it is 50 or 60ms
Giving some reasonable time for transmission, e2e latency restriction was exercised at four points:
  70, 90, 110 and 130ms

## Slide 4: Video freeze under latency restriction
Some times freeze time is huge
However, temporal layer 0 is delivered in most of the cases
If L0 is delivered, the video is viewable, however FPS drop is noticeable and quite disturbing
 |  | Latency restriction, ms | Freeze time,
Class B | BasketballDrive | 70 | 78.6%
1080p |  | 90 | 55.8%
 |  | 110 | 29.0%
 |  | 130 | 17.8%
 | BQTerrace | 70 | 24.5%
 |  | 90 | 1.7%
 |  | 110 | 1.0%
 |  | 130 | 0.2%
Gaming | GTAVs090 | 70 | 39.2%
1080p |  | 90 | 11.0%
 |  | 110 | 1.8%
 |  | 130 | 1.0%
 | Minecraft | 70 | 52.3%
 |  | 90 | 44.0%
 |  | 110 | 23.7%
 |  | 130 | 3.3%

## Slide 5: Small and Big freeze
The freeze time separated on two categories
“Small” freeze, <= 60 ms (within 1 GOP), a kind of OK
“Big” freeze, > 60ms, obvious video stalling
 |  | Latency restriction, ms | Freeze time, | Small freeze (<= 60ms) | Big freeze (> 60ms)
Class B | BasketballDrive | 70 | 78.6% | 51.8% | 26.8%
1080p |  | 90 | 55.8% | 42.4% | 13.4%
 |  | 110 | 29.0% | 15.6% | 13.4%
 |  | 130 | 17.8% | 17.8% | 0.0%
 | BQTerrace | 70 | 24.5% | 24.5% | 0.0%
 |  | 90 | 1.7% | 1.7% | 0.0%
 |  | 110 | 1.0% | 1.0% | 0.0%
 |  | 130 | 0.2% | 0.2% | 0.0%
Gaming | GTAVs090 | 70 | 39.2% | 39.2% | 0.0%
1080p |  | 90 | 11.0% | 11.0% | 0.0%
 |  | 110 | 1.8% | 1.8% | 0.0%
 |  | 130 | 1.0% | 1.0% | 0.0%
 | Minecraft | 70 | 52.3% | 36.5% | 0.0%
 |  | 90 | 44.0% | 6.8% | 0.0%
 |  | 110 | 23.7% | 1.5% | 0.0%
 |  | 130 | 3.3% | 0.5% | 0.0%

## Slide 6: ULL CfE JVET-AN0080 evaluated in RA GOP4
BD-PSNR improvement
 | Broadcast w/o feedback, transmission priority Off, try #0-WiFi, QP 22 |  |  |  |  |  | 
PSNR vs Latency | ULL CfE JVET-AN0080 over VTM, BD-PSNR |  |  |  |  |  | 
at QP 22 | Y | U | V | Freeze | Delta Freeze | EncT | DecT
Class A | 2.1 | 1.2 | 1.1 | -11.6% | 40.1 -> 28.5% |  | 
Class B | 2.5 | 1.2 | 1.7 | -14.4% | 27.6 -> 13.2% |  | 
Gaming | 1.4 | 1.0 | 0.9 | -9.8% | 17.2 -> 7.4% |  | 
Overall | 2.1 dB | 1.2 dB | 1.3 dB | -12.4% | 28.2 -> 15.8% |  | 
Chart: 
| 70 | 90 | 110 | 130
VTM | 33.121 | 38.942 | 40.767 | 40.945
ULL CfE JVET-AN0080 | 38.704 | 40.416 | 41.003 | 41.053
Chart: 
| 70 | 90 | 110 | 130
VTM | 0.392 | 0.11 | 0.018 | 0.01
ULL CfE JVET-AN0080 | 0.02 | 0.007 | 0.002 | 0
Demo link: https://drive.google.com/drive/folders/1bpIa9dcRv-059TSuGVxlZP-5GdzlJNk7
Exemplary test case uploaded with contribution
More samples are available on the link

## Slide 7: Software modifications on top of AHG18 software
On top of JVET-AO0123 : Standalone network simulation application on top of ULL software
Fixes in NetworkLib to support to synchronize capture order and coding
Two queue buffers on sending and receiving side for correct latency modelling
JVET-AN0080

## Slide 8: Conclusion
Random Access GOP4 configuration is practically used in low latency Live-streaming applications
The solutions used for ULL CfE JVET-AN0080 demonstrates an evidence of potential improvement
It is suggested to study RA GOP4 configuration in context of AHG18 work, and include described software modification to AHG18 branch to support RA latency restricted tests
JVET-AN0080
Demo link: https://drive.google.com/drive/folders/1bpIa9dcRv-059TSuGVxlZP-5GdzlJNk7

## Slide 9
Thank you.

## Slide 10: Structural delay: Temporal Layer 0
0
1
2
3
4
5
6
7
8
`
0
4
8
no delay for TL0

## Slide 11: Structural delay: Temporal Layer 1
0
1
2
3
4
5
6
7
8
`
0
4
2
8
6
1 frame delay for TL1

## Slide 12: Structural delay: Temporal Layer 2
0
1
2
3
4
5
6
7
8
`
0
4
2
1
3
8
6
5
7
3 frames delay for TL2