## Slide 1
Hendry, Muhammed Coban, Geert Van der Auwera, Marta Karczewicz (Qualcomm)
AHG8: Adaptive QP for 360-degree video ERP projection (JVET-F0049)

## Slide 2: Introduction
Adaptive QP based ERP coding
  ERP WSPSNR weight based QP adaptation
  CTU level
QP adaptation
  QP = QP – 3 log2(w) , w: normalized WSPSNR weights
Use average w in a CTU row

## Slide 3: Results
BD-rates (RA) for adaptive QP comparison with ERP following common test conditions for 360-degree video (JVET-E1030)
Metric |  | Y | U | V
End-to-end | SPSNR-NN | -4.3% | -6.8% | -6.8%
 | SPSNR-I | -4.3% | -6.8% | -6.8%
 | CPP-PSNR | -4.3% | -6.8% | -6.9%
 | WS-PSNR | -4.3% | -6.9% | -6.9%
Cross Format | SPSNR-NN | -2.4% | -6.6% | -6.7%
 | SPSNR-I | -4.3% | -6.7% | -6.8%
 | CPP-PSNR | -4.4% | -6.8% | -6.8%
Dynamic Viewport | Viewport0 | -11.0% | -11.8% | -12.1%
 | Viewport1 | -4.4% | -6.3% | -6.4%

## Slide 4: Viewport Results
Adaptive QP ERP North and South pole 90-degree FOV viewport PSNR comparison vs ISP
ISP: approximately uniform quality distribution over the sphere
 | Avg. PSNR difference (dB) (0,90) |  |  | Avg. PSNR difference (dB) (0,-90) |  | 
Sequence | Y | U | V | Y | U | V
Trolley | 0.123 | -0.180 | -0.006 | -0.068 | -0.615 | -0.319
GasLamp | -0.327 | -0.269 | -0.158 | -0.411 | 0.084 | -0.341
Skateboarding_in_lot | -0.080 | -0.127 | -0.065 | -0.101 | -0.297 | 0.465
Chairlift | -0.054 | -0.311 | -0.231 | -0.079 | -0.399 | -0.214
KiteFlite | 0.002 | -0.355 | -0.153 | -0.428 | -0.353 | -0.270
Harbor | -0.456 | -0.186 | -0.150 | -0.310 | 0.001 | 0.120
PoleVault | -0.207 | -0.215 | -0.102 | -0.351 | -0.267 | -0.251
AerialCity | 0.739 | 1.259 | 0.956 | 1.180 | 0.883 | 0.792
DrivingInCity | -0.193 | -0.289 | -0.238 | -0.226 | -0.182 | -0.168
DrivingInCountry | -0.197 | -0.038 | 0.046 | -0.142 | -0.101 | -0.134
Overall | -0.065 | -0.071 | -0.010 | -0.094 | -0.125 | -0.032
PSNR difference: ISP anchor

## Slide 5: Conclusion
Adaptive QP based ERP coding is presented.
Reported coding gain is -4.3% (e2e WS-PSNR) compared with ERP for RA conditions
Request to replace ERP anchor with adaptive QP based ERP.