## Slide 1: CE11-related: CTU line buffer reduction for long filter deblocking (JVET-L0572)
A.M. Kotra, S. Esenlik, B. Wang, J. Chen (Huawei), W. Zhu, K. Misra, P. Cowan, A. Segall (Sharp)

## Slide 2: Proposal overview
Builds the following on top of using long filters for large blocks and using HEVC strong filter and control for chroma:
  Limited support long filters for large luma blocks for above CTU boundary (to reduce CTU line buffers)
  Samples beyond CTU line boundary are not used in deblocking control process (to reduce CTU line buffers)
  Subsampling of chroma gradient computation to reduce complexity
  Threshold change in strong deblocking condition for luma long filter deblocking for objective gain

## Slide 3: Limited support long filter at CTU boundary
Problem:
  Using a longer tap filter at CTU boundaries will require a increase in line buffer when compared to DBF present in VTM.
Current Proposal:
  At CTU boundaries for the top blocks
    Only “3” samples are modified
    Same as in VTM
Horizontal edge overlapping with CTU boundary
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
…
…
…
…
…
…
…
…
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Block Height =16
Block Height =16
…
…
…
…
…
…
…
…
x
Sample modified by filter

## Slide 4: Limited support long filter at CTU boundary
Output pixel | Filter coefficients {p7, p6, p5, p4, p3, p2, p1, p0, q0, q1, q2, q3, q4, q5, q6, q7} | Input pixels
p2 | {0, 0, 0, 0, 6, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0} | p3 ~ q4
p1 | {0, 0, 0, 0, 5, 1, 3, 1, 1, 1, 1, 1, 1, 1, 0, 0} | p3 ~ q5
p0 | {0, 0, 0, 0, 5, 1, 1, 2, 1, 1, 1, 1, 1, 1, 1, 0} | p3 ~ q6
q0 | {0, 0, 0, 0, 4, 1, 1, 1, 2, 1, 1, 1, 1, 1, 1, 1} | p3 ~ q7
q1 | {0, 0, 0, 0, 3, 1, 1, 1, 1, 3, 1, 1, 1, 1, 1, 1} | p3 ~ q7
q2 | {0, 0, 0, 0, 2, 1, 1, 1, 1, 1, 3, 1, 1, 1, 1, 2} | p3 ~ q7
q3 | {0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 1, 3} | p3 ~ q7
q4 | {0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 1, 4} | p2 ~ q7
q5 | {0, 0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 1, 5} | p1 ~ q7
q6 | {0, 0, 0, 0, 0, 0, 0, 1, 1, 1, 1, 1, 1, 1, 3, 6} | p0 ~ q7

## Slide 5: Deblocking control process at CTU boundary
…
ControlSamplesAccessible = p0 belongs to CTU above current CTU ? FALSE : TRUE
if ( LongTapDeblocking )
if (p side is greater than or equal to 32 && ControlSamplesAccessible )
dp0 = ( dp0 + Abs( p5,0 − 2 * p4,0 + p3,0 ) + 1 ) >> 1
dp3 = ( dp3 + Abs( p5,3 − 2 * p4,3 + p3,3 ) + 1 ) >> 1
…
if ( p side is greater than or equal to 32 && LongTapDeblocking && ControlSamplesAccessible )
sp3 = ( sp3 + Abs( p7 − p3 ) + 1) >> 1

## Slide 6: Chroma gradient computation when using HEVC strong filter
Strong deblocking decision in chroma are made very 2-sample segment (e.g. in CE11.1.7b)
Problem:
As a result, in worst-case gradient computations are carried out for every chroma line
dp0 = Abs( p2,0 − 2 * p1,0 + p0,0 )
dp1 = Abs( p2,1 − 2 * p1,1 + p0,1 )
dq0 = Abs( q2,0 − 2 * q1,0 + q0,0 )
dq1 = Abs( q2,1 − 2 * q1,1 + q0,1 )
dpq0 = dp0 + dq0
dpq1 = dp1 + dq1
d = dpq0 + dpq1

## Slide 7: Subsampling of chroma gradient computation
Proposal: Compute gradients for only one of the two lines
Reduction of worst case complexity
dp0 = Abs( p2,0 − 2 * p1,0 + p0,0 )
dp1 = Abs( p2,1 − 2 * p1,1 + p0,1 )
dq0 = Abs( q2,0 − 2 * q1,0 + q0,0 )
dq1 = Abs( q2,1 − 2 * q1,1 + q0,1 )
dpq0 = dp0 + dq0
dpq1 = dp1 + dq1
d = 2*dpq0 + dpq1

## Slide 8: Threshold change for long filter deblocking
The use of long filters with the same threshold as the original HEVC filters may lead to objective loss, e.g. CE11.1.7b:
0.01 (AI) / 0.16% (RA) / 0.42% (LDB) / 0.28% (LDP)
Proposal: Reduce the threshold for better objective gain
As in HEVC derive, StrongFilterCondition = (dpq is less than ( β >> 2 ), sp3 + sq3 is less than ( LongTapDeblocking ? ( 3*β >> 5 ) : ( β >> 3 ) ), and Abs( p0 − q0 ) is less than ( 5 * tC + 1 ) >> 1) ? TRUE : FALSE

## Slide 9: Results

## Slide 10: Conclusion
  Limited support long filters for large luma blocks for above CTU boundary (to reduce CTU line buffers)
  Samples beyond CTU line boundary are not used in deblocking control process (to reduce CTU line buffers)
  Subsampling of chroma gradient computation to reduce complexity
  Threshold change in strong deblocking condition for luma long filter deblocking for objective gain
We propose to adopt the above changes to VVC

## Slide 11: Backup Slides

## Slide 12: Luma long filter for large blocks
p6′= (7*p7+2*p6+p5+p4+p3+p2+ p1+p0+q0+ 8) >> 4
p5′= (6*p7+p6+2*p5+p4+p3+p2+p1+p0+q0+q1+ 8) >> 4
p4′= (5*p7+p6+p5+2*p4+p3+p2+p1+p0+q0+q1+q2+ 8) >> 4
p3′= (4*p7+p6+p5+p4+2*p3+p2+p1+p0+q0+q1+q2+q3+ 8) >> 4
p2′= (3*p7+p6+p5+p4+p3+2*p2+p1+p0+q0+q1+q2+q3+q4+8) >> 4
p1′= (2*p7+p6+p5+p4+p3+p2+2*p1+p0+q0+q1+q2+q3+q4+q5+8) >> 4
p0′= (p7+p6+p5+p4+p3+p2+p1+2*p0+q0+q1+q2+q3+q4+q5+q6+8) >> 4
q6′= (7*q7+2*q6+q5+q4+q3+q2+ q1+q0+p0+ 8) >> 4
q5′= (6*q7+q6+2*q5+q4+q3+q2+q1+q0+p0+p1+ 8) >> 4
q4′= (5*q7+q6+q5+2*q4+q3+q2+q1+q0+p0+p1+p2+ 8) >> 4
q3′= (4*q7+q6+q5+q4+2*q3+q2+q1+q0+p0+p1+p2+p3+ 8) >> 4
q2′= (3*q7+q6+q5+q4+q3+2*q2+q1+q0+p0+p1+p2+p3+p4+8) >> 4
q1′= (2*q7+q6+q5+q4+q3+q2+2*q1+q0+p0+p1+p2+p3+p4+p5+8) >> 4
q0′= (q7+q6+q5+q4+q3+q2+q1+2*q0+p0+p1+p2+p3+p4+p5+p6+8) >> 4

## Slide 13: Large blocks
Luma
LongTapDeblocking = ( ( p side >= 32 && q side >= 16 ) || ( p side >= 16 && q side >= 32 ) ) ) ? TRUE : FALSE
Chroma
P-side >= 8 (chroma samples) && Q-side >= 8 (chroma samples)