## Slide 1: JVET-M0255 AHG11: MMVD without Fractional Distances for SCC
Hongbin Liu, Li Zhang, Kai Zhang, Jizheng Xu Yue Wang, Pengwei Zhao, Dingkun Hong

## Slide 2: Summary
Motivation
  In MMVD, fractional MVD are always used, which is unreasonable for screen content coding.
Proposed solution
  Decide whether a picture is screen content or not, if yes, disable fractional MVD in MMVD.
  It can achieve -0.76/-1.66% for RA/LDB when CPR is on, and -1.58 and -2.74% when CPR is off.
Thanks Huawei for crosschecking

## Slide 3: Proposed Method
Determination whether a slice is screen content or not
  Check the ratio of the block which has identical hash value with another block.
  If the ratio is larger than a threshold, the slice is considered as a screen content slice.
Disabling fraction MVD in MMVD
  A flag is signaled to decoder to indicate whether fractional MVD is enabled or not
  If fractional MVD is enabled, the default distance table is used; otherwise, all elements in the default distance table are left shifted by 2.

## Slide 4: Simulation results (CPR on)
Anchor: VTM-3.0 + ticket#140
 | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.03% | -0.10% | 99% | 99% |  |  |  |  | 
Class A2 | 0.00% | 0.00% | 0.00% | 101% | 101% |  |  |  |  | 
Class B | 0.00% | -0.01% | -0.03% | 100% | 100% | -0.01% | -0.06% | -0.03% | 100% | 103%
Class C | 0.00% | 0.00% | 0.00% | 100% | 101% | 0.00% | 0.00% | 0.00% | 100% | 99%
Class E |  |  |  |  |  | 0.02% | 0.02% | 0.02% | 100% | 98%
Overall | 0.00% | -0.01% | -0.03% | 100% | 100% | 0.00% | -0.02% | -0.01% | 100% | 101%
Class D | 0.01% | 0.01% | 0.01% | 99% | 99% | 0.01% | 0.01% | 0.01% | 100% | 100%
Class F | -0.03% | -0.06% | -0.08% | 99% | 100% | -0.06% | -0.32% | 0.29% | 100% | 102%
Class SCC | -0.76% | -0.82% | -0.87% | 99% | 101% | -1.66% | -1.51% | -1.47% | 99% | 100%

## Slide 5: Simulation results (CPR off)
Anchor: VTM-3.0 + ticket#140
 | Random Access Main 10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class SCC | -1.58% | -1.56% | -1.55% | 98% | 99% | -2.74% | -2.77% | -2.80% | 99% | 99%

## Slide 6
Thanks！