## Slide 1: CE6-related: 32 point MTS based on skipping high frequency coefficients (JVET-M0297)
Moonmo Koo, Mehdi Salehifar, Jaehyun Kim, and Seung Hwan Kim

## Slide 2: Summary
Proposed method
  In VTM 3.0, coefficient region other than top-left 32x32 is skipped (zeroed-out).
  Skipping high frequency coefficients for 32-point MTS (RMTS32)
    If width (height) ≥ 32, left (top) half of coefficients are kept.
    RMTS32 was proposed in the previous CE (JVET-L0132).
  Residual coding can also be taken care of accordingly.
    sub-block flags for skipped region are not coded.
    last coefficient position is restricted within feasible region.
  Complexity reduction for 32-point MTS
    Half multiplication count (64 mult/pel  32 mult/pel for 32x32 TU)
    Half memory usage (2KB  1KB)
Experimental results (BD-rate / enc. time)
  Test 1: RMTS32 without residual coding change
    0.12% / 97% (AI), 0.03% / 99% (RA), and 0.02% / 100% (LD)
  Test 2: RMTS32 with residual coding change
    0.10% / 97% (AI), 0.00% / 99% (RA), and 0.05% / 99% (LD)
Thanks to Technicolor for cross-checking

## Slide 3: Conclusion
Reasonable trade-off between complexity reduction and performance
  The worst computational complexity is halved (64  32 mult/pel).
It is recommended that RMTS32 be adopted in next VTM or studied in next CE.

## Slide 4: Appendix – Experimental results [1/2]
Test 1: RMTS32 without residual coding change
  CTC
  Inter MTS on
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
AI | 0.12% | 0.05% | 0.02% | 97% | 94%
RA | 0.03% | 0.05% | 0.08% | 99% | 99%
LDB | 0.02% | 0.08% | 0.00% | 100% | 100%
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
RA | 0.05% | 0.01% | 0.10% | 96% | 99%
LDB | 0.14% | 0.10% | -0.05% | 96% | 99%

## Slide 5: Appendix – Experimental results [2/2]
Test 2: RMTS32 with residual coding change
  CTC
  Inter MTS on
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
AI | 0.10% | 0.01% | 0.00% | 97% | 94%
RA | 0.00% | 0.09% | 0.11% | 99% | 99%
LDB | 0.05% | 0.34% | 0.11% | 99% | 98%
Config. | BD-rate |  |  | EncT | DecT
 | Y | U | V |  | 
RA | 0.02% | 0.01% | 0.04% | 96% | 99%
LDB | 0.12% | 0.15% | -0.30% | 96% | 99%