## Slide 1: JVET-M0474 – CE8.1.3: Extended CPR reference with 1 buffer line
Luong Pham Van, Vadim Seregin
Wei-Jung Chien, Ted Hsieh, Marta Karczewicz
@qualcomm
01/2019
AV

## Slide 2: Proposed method – CE8.1.3
Adding 1 line buffer into the CPR search area
  No addition memory cost
 |  | x
x
CPR reference
Current PU
Line buffer

## Slide 3: Experimental results
Thank LGE for cross-checking
CPR on, PLT off
CPR on, PLT on
 | AI |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3 + CPR on + PLT off |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.05% | 0.06% | 127% | 103% | 0.00% | 0.06% | 0.00% | 101% | 103%
Class A2 | -0.49% | -0.55% | -0.55% | 134% | 102% | -0.01% | -0.04% | -0.01% | 102% | 101%
Class B | -0.31% | -0.40% | -0.35% | 138% | 102% | -0.01% | -0.01% | 0.00% | 101% | 101%
Class C | -0.10% | -0.17% | -0.28% | 142% | 103% | -0.01% | 0.08% | -0.03% | 101% | 99%
Class E | -0.67% | -0.76% | -0.61% | 145% | 104% | -0.04% | 0.05% | -0.02% | 102% | 101%
Overall | -0.29% | -0.37% | -0.34% | 137% | 103% | -0.01% | 0.02% | -0.01% | 101% | 101%
Class D | -0.13% | -0.26% | 0.11% | 138% | 100% | -0.03% | -0.03% | -0.10% | 102% | 102%
Class F | -12.21% | -12.14% | -12.19% | 159% | 104% | -0.17% | -0.14% | -0.14% | 102% | 104%
Class SCC | -37.14% | -36.32% | -36.57% | 144% | 97% | -0.37% | -0.33% | -0.35% | 102% | 103%
RA |  |  |  |  |  |  |  |  |  | 
Class A1 | 0.12% | -0.01% | 0.24% | 99% | 101% | -0.02% | 0.03% | 0.01% | 101% | 101%
Class A2 | -0.02% | 0.06% | 0.09% | 99% | 100% | -0.02% | -0.01% | -0.15% | 101% | 100%
Class B | 0.00% | 0.05% | -0.23% | 99% | 100% | -0.02% | 0.05% | -0.02% | 101% | 100%
Class C | 0.21% | -0.08% | 0.10% | 102% | 101% | 0.02% | -0.02% | 0.01% | 100% | 100%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.08% | 0.01% | 0.02% | 100% | 100% | -0.01% | 0.02% | -0.03% | 101% | 100%
Class D | 0.16% | -0.37% | 0.22% | 102% | 98% | 0.00% | -0.09% | 0.07% | 100% | 100%
Class F | -9.96% | -10.10% | -9.99% | 106% | 101% | -0.09% | -0.17% | -0.02% | 102% | 104%
Class SCC | -22.17% | -21.75% | -22.27% | 105% | 100% | -0.19% | -0.21% | -0.21% | 101% | 102%
LDB |  |  |  |  |  |  |  |  |  | 
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.08% | -0.15% | 0.08% | 108% | 103% | 0.01% | 0.17% | 0.21% | 102% | 100%
Class C | 0.12% | 0.16% | 0.37% | 111% | 104% | 0.00% | -0.23% | 0.04% | 102% | 103%
Class E | 0.24% | 1.11% | -0.69% | 106% | 98% | -0.04% | 0.05% | -0.50% | 101% | 99%
Overall | 0.13% | 0.27% | -0.02% | 109% | 102% | -0.01% | 0.01% | -0.02% | 102% | 101%
Class D | 0.15% | 0.21% | 0.98% | 110% | 92% | 0.01% | 0.37% | 0.26% | 98% | 92%
Class F | -5.18% | -5.41% | -5.56% | 108% | 99% | -0.05% | -0.05% | -0.09% | 100% | 98%
Class SCC | -13.03% | -13.23% | -13.55% | 108% | 95% | 0.07% | 0.15% | 0.09% | 100% | 100%
AI |  |  |  |  |  |  |  |  |  | 
Over VTM-3.0 |  |  |  |  |  | Over VTM-3 + CPR on + PLT on |  |  |  | 
Y | U | V | EncT | DecT | Y |  | U | V | EncT | DecT
0.11% | 0.06% | 0.13% | 135% | 101% | -0.01% |  | -0.02% | -0.01% | 99% | 96%
-0.39% | -0.43% | -0.44% | 142% | 101% | -0.01% |  | 0.01% | -0.01% | 101% | 102%
-0.21% | -0.34% | -0.28% | 144% | 102% | -0.01% |  | -0.03% | 0.02% | 100% | 97%
0.00% | -0.19% | -0.13% | 147% | 104% | 0.01% |  | -0.06% | 0.05% | 99% | 99%
-0.52% | -0.67% | -0.53% | 150% | 104% | -0.02% |  | -0.15% | 0.04% | 100% | 98%
-0.19% | -0.31% | -0.25% | 144% | 103% | -0.01% |  | -0.05% | 0.02% | 100% | 98%
-0.02% | -0.05% | 0.15% | 143% | 100% | 0.00% |  | -0.01% | -0.02% | 99% | 94%
-15.57% | -14.12% | -14.27% | 171% | 96% | -0.10% |  | -0.09% | -0.18% | 100% | 100%
-44.89% | -41.21% | -41.42% | 157% | 77% | -0.23% |  | -0.24% | -0.25% | 100% | 100%
RA |  |  |  |  |  |  |  |  |  | 
0.22% | 0.06% | 0.31% | 102% | 100% | 0.01% |  | -0.14% | -0.05% | 100% | 99%
0.13% | 0.14% | 0.20% | 102% | 101% | 0.02% |  | -0.01% | -0.08% | 99% | 104%
0.12% | 0.06% | -0.19% | 104% | 100% | 0.01% |  | 0.06% | -0.10% | 101% | 101%
0.36% | -0.06% | 0.46% | 107% | 100% | 0.01% |  | -0.04% | 0.08% | 99% | 97%
0.21% | 0.05% | 0.16% | 104% | 100% | 0.01% |  | -0.02% | -0.04% | 100% | 100%
0.41% | 0.00% | 0.06% | 108% | 98% | -0.01% |  | 0.04% | 0.10% | 98% | 97%
-12.00% | -11.84% | -12.07% | 112% | 97% | -0.12% |  | -0.05% | -0.06% | 100% | 98%
-25.74% | -24.58% | -24.94% | 107% | 95% | -0.10% |  | -0.12% | -0.17% | 100% | 100%
LDB |  |  |  |  |  |  |  |  |  | 
0.16% | 0.01% | 0.16% | 114% | 101% | -0.01% |  | 0.25% | 0.05% | 101% | 99%
0.26% | 0.32% | 0.68% | 119% | 105% | -0.03% |  | -0.21% | 0.31% | 100% | 103%
0.45% | 0.48% | -0.52% | 113% | 95% | -0.02% |  | -0.56% | -0.14% | 102% | 101%
0.27% | 0.23% | 0.16% | 115% | 101% | -0.02% |  | -0.11% | 0.09% | 101% | 100%
0.32% | 0.35% | 0.44% | 118% | 95% | -0.06% |  | -0.30% | -0.21% | 99% | 98%
-6.25% | -7.17% | -7.64% | 114% | 99% | -0.12% |  | -0.39% | -0.51% | 100% | 100%
-14.79% | -14.59% | -14.60% | 110% | 95% | 0.05% |  | 0.13% | 0.19% | 99% | 103%

## Slide 4: Supplemental results (1)
4 lines above and 4 columns to the left current CTU are added to CPR search
CPR on, PLT off
 | AI |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3 + CPR on + PLT off |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.09% | 0.02% | 125% | 102% | -0.01% | 0.01% | -0.04% | 99% | 102%
Class A2 | -0.51% | -0.49% | -0.58% | 131% | 95% | -0.03% | 0.01% | -0.04% | 100% | 94%
Class B | -0.32% | -0.42% | -0.36% | 136% | 103% | -0.02% | -0.03% | -0.01% | 100% | 101%
Class C | -0.09% | -0.23% | -0.34% | 139% | 101% | -0.01% | 0.02% | -0.10% | 100% | 97%
Class E | -0.73% | -0.86% | -0.63% | 142% | 104% | -0.09% | -0.05% | -0.04% | 100% | 101%
Overall | -0.30% | -0.41% | -0.38% | 135% | 101% | -0.03% | -0.01% | -0.04% | 100% | 99%
Class D | -0.11% | -0.19% | 0.09% | 136% | 98% | -0.01% | 0.04% | -0.13% | 100% | 100%
Class F | -12.69% | -12.62% | -12.62% | 157% | 100% | -0.81% | -0.79% | -0.72% | 101% | 100%
Class SCC | -38.56% | -37.53% | -37.80% | 141% | 90% | -2.78% | -2.35% | -2.41% | 99% | 99%
RA |  |  |  |  |  |  |  |  |  | 
Class A1 | 0.13% | 0.01% | 0.25% | 97% | 100% | -0.01% | 0.05% | 0.02% | 99% | 100%
Class A2 | -0.01% | 0.05% | 0.21% | 97% | 101% | -0.01% | -0.02% | -0.04% | 99% | 101%
Class B | 0.00% | -0.17% | -0.23% | 97% | 99% | -0.01% | -0.17% | -0.02% | 98% | 99%
Class C | 0.18% | -0.06% | 0.15% | 100% | 97% | -0.01% | 0.00% | 0.07% | 98% | 97%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.07% | -0.06% | 0.06% | 98% | 99% | -0.01% | -0.05% | 0.01% | 98% | 99%
Class D | 0.18% | -0.31% | 0.23% | 100% | 96% | 0.03% | -0.03% | 0.07% | 99% | 98%
Class F | -10.35% | -10.24% | -10.38% | 103% | 95% | -0.62% | -0.42% | -0.54% | 98% | 99%
Class SCC | -23.12% | -22.57% | -23.14% | 102% | 96% | -1.51% | -1.35% | -1.42% | 99% | 99%
LDB |  |  |  |  |  |  |  |  |  | 
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.08% | -0.11% | 0.27% | 106% | 103% | 0.01% | 0.20% | 0.40% | 100% | 100%
Class C | 0.13% | 0.38% | 0.29% | 108% | 103% | 0.00% | -0.01% | -0.04% | 99% | 102%
Class E | 0.17% | 1.01% | 0.14% | 104% | 96% | -0.11% | -0.06% | 0.34% | 98% | 96%
Overall | 0.12% | 0.33% | 0.24% | 106% | 101% | -0.02% | 0.07% | 0.24% | 99% | 100%
Class D | 0.19% | 0.21% | 0.10% | 110% | 97% | 0.05% | 0.37% | -0.58% | 98% | 97%
Class F | -5.42% | -5.69% | -5.35% | 107% | 97% | -0.34% | -0.37% | 0.08% | 99% | 96%
Class SCC | -13.71% | -14.02% | -14.29% | 108% | 93% | -0.74% | -0.78% | -0.79% | 99% | 98%

## Slide 5: Supplemental results (2) – CPR area = current 64x64 VDPU
CPR on, PLT off
CPR on, PLT on
 | AI |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3 + CPR on + PLT off |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | -0.06% | -0.18% | -0.14% | 127% | 102% | 0.21% | 0.22% | 0.19% | 94% | 100%
Class D | 0.07% | 0.10% | 0.28% | 128% | 104% | 0.17% | 0.33% | 0.07% | 94% | 106%
Class F | -8.42% | -8.52% | -8.49% | 143% | 106% | 4.96% | 4.72% | 4.84% | 92% | 105%
Class SCC | -26.37% | -25.67% | -25.84% | 142% | 104% | 17.70% | 17.26% | 17.44% | 101% | 106%
RA |  |  |  |  |  |  |  |  |  | 
Overall | 0.15% | 0.09% | 0.12% | 98% | 99% | 0.07% | 0.10% | 0.07% | 99% | 99%
Class D | 0.24% | -0.49% | 0.11% | 103% | 102% | 0.09% | -0.21% | -0.05% | 102% | 104%
Class F | -6.95% | -6.99% | -7.08% | 101% | 97% | 3.97% | 3.95% | 3.92% | 97% | 100%
Class SCC | -15.03% | -14.66% | -15.04% | 104% | 101% | 9.63% | 9.45% | 9.66% | 100% | 103%
LDB |  |  |  |  |  |  |  |  |  | 
Overall | 0.14% | 0.15% | 0.12% | 107% | 102% | 0.00% | -0.11% | 0.11% | 100% | 101%
Class D | 0.15% | 0.23% | 0.49% | 112% | 101% | 0.01% | 0.39% | -0.19% | 100% | 101%
Class F | -3.33% | -3.61% | -4.10% | 107% | 102% | 2.14% | 2.07% | 1.66% | 99% | 101%
Class SCC | -8.15% | -8.36% | -8.52% | 109% | 100% | 6.07% | 6.15% | 6.27% | 101% | 105%
AI |  |  |  |  |  |  |  |  |  | 
Over VTM-3.0 |  |  |  |  |  | Over VTM-3 + CPR on + PLT on |  |  |  | 
Y | U | V | EncT | DecT | Y |  | U | V | EncT | DecT
0.02% | -0.05% | -0.07% | 134% | 103% | 0.21% |  | 0.21% | 0.19% | 93% | 99%
0.17% | 0.17% | 0.29% | 134% | 106% | 0.19% |  | 0.21% | 0.12% | 93% | 99%
-13.25% | -11.48% | -11.57% | 158% | 95% | 3.31% |  | 3.57% | 3.55% | 92% | 99%
-38.52% | -34.16% | -34.31% | 162% | 75% | 11.76% |  | 12.06% | 12.18% | 103% | 99%
RA |  |  |  |  |  |  |  |  |  | 
0.28% | 0.15% | 0.24% | 104% | 100% | 0.09% |  | 0.08% | 0.04% | 100% | 100%
0.44% | 0.09% | 0.44% | 109% | 102% | 0.02% |  | 0.14% | 0.48% | 100% | 101%
-10.09% | -9.78% | -10.06% | 110% | 97% | 2.59% |  | 2.84% | 2.77% | 98% | 98%
-21.01% | -19.83% | -19.96% | 109% | 95% | 6.73% |  | 6.56% | 6.81% | 103% | 100%
LDB |  |  |  |  |  |  |  |  |  | 
0.28% | 0.37% | 0.20% | 113% | 100% | -0.01% |  | 0.03% | 0.12% | 99% | 100%
0.34% | 0.78% | 1.15% | 116% | 94% | -0.05% |  | 0.13% | 0.48% | 97% | 98%
-4.94% | -5.76% | -6.38% | 110% | 94% | 1.47% |  | 1.30% | 1.03% | 97% | 95%
-11.28% | -11.04% | -10.84% | 108% | 90% | 4.43% |  | 4.52% | 4.82% | 98% | 97%

## Slide 6: Supplemental results (3) – CPR area = current 64x64 VDPU
With 1 line above and 1 left column
CPR on, PLT off
CPR on, PLT on
 | AI |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3 + CPR on + PLT off |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | -0.08% | -0.20% | -0.17% | 128% | 105% | 0.20% | 0.20% | 0.17% | 95% | 103%
Class D | 0.05% | 0.09% | 0.25% | 129% | 105% | 0.16% | 0.32% | 0.04% | 95% | 107%
Class F | -8.65% | -8.75% | -8.74% | 144% | 105% | 4.64% | 4.42% | 4.50% | 93% | 105%
Class SCC | -26.79% | -26.08% | -26.26% | 143% | 104% | 17.00% | 16.60% | 16.75% | 101% | 106%
RA |  |  |  |  |  |  |  |  |  | 
Overall | 0.15% | 0.08% | 0.09% | 98% | 99% | 0.06% | 0.09% | 0.05% | 99% | 99%
Class D | 0.23% | -0.35% | 0.19% | 104% | 103% | 0.07% | -0.08% | 0.03% | 102% | 105%
Class F | -7.12% | -7.31% | -7.35% | 101% | 97% | 3.73% | 3.56% | 3.57% | 97% | 100%
Class SCC | -15.24% | -14.88% | -15.22% | 103% | 99% | 9.33% | 9.14% | 9.41% | 100% | 102%
LDB |  |  |  |  |  |  |  |  |  | 
Overall | 0.15% | 0.01% | 0.08% | 108% | 101% | 0.01% | -0.25% | 0.08% | 101% | 100%
Class D | 0.12% | 0.17% | 0.59% | 113% | 101% | -0.02% | 0.32% | -0.10% | 101% | 101%
Class F | -3.37% | -3.79% | -3.48% | 107% | 101% | 2.10% | 1.90% | 2.31% | 99% | 100%
Class SCC | -8.19% | -8.30% | -8.43% | 109% | 98% | 6.01% | 6.20% | 6.35% | 101% | 103%
AI |  |  |  |  |  |  |  |  |  | 
Over VTM-3.0 |  |  |  |  |  | Over VTM-3 + CPR on + PLT on |  |  |  | 
Y | U | V | EncT | DecT | Y |  | U | V | EncT | DecT
0.01% | -0.07% | -0.11% | 135% | 104% | 0.20% |  | 0.19% | 0.16% | 93% | 100%
0.15% | 0.19% | 0.32% | 135% | 106% | 0.17% |  | 0.23% | 0.15% | 93% | 100%
-13.37% | -11.48% | -11.59% | 159% | 98% | 3.14% |  | 3.53% | 3.50% | 93% | 101%
-38.67% | -34.37% | -34.51% | 163% | 76% | 11.49% |  | 11.72% | 11.86% | 104% | 101%
RA |  |  |  |  |  |  |  |  |  | 
0.28% | 0.13% | 0.23% | 104% | 99% | 0.08% |  | 0.06% | 0.03% | 99% | 99%
0.43% | -0.01% | 0.21% | 106% | 96% | 0.01% |  | 0.03% | 0.25% | 96% | 95%
-10.18% | -9.85% | -10.27% | 108% | 95% | 2.46% |  | 2.73% | 2.52% | 97% | 96%
-21.14% | -19.87% | -20.04% | 107% | 93% | 6.54% |  | 6.49% | 6.69% | 101% | 98%
LDB |  |  |  |  |  |  |  |  |  | 
0.26% | 0.28% | 0.44% | 113% | 100% | -0.02% |  | -0.05% | 0.35% | 99% | 100%
0.42% | 0.60% | 0.66% | 116% | 94% | 0.04% |  | -0.05% | 0.00% | 97% | 98%
-5.10% | -5.85% | -6.20% | 110% | 94% | 1.29% |  | 1.23% | 1.22% | 97% | 94%
-11.11% | -10.84% | -10.72% | 109% | 89% | 4.61% |  | 4.75% | 4.96% | 98% | 96%

## Slide 7: Supplemental results (4) – CPR area = current 64x64 VDPU
With 4 lines above and 4 left columns
CPR on, PLT off
CPR on, PLT on
 | AI |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 |  |  |  |  | Over VTM-3 + CPR on + PLT off |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | -0.12% | -0.20% | -0.21% | 130% | 104% | 0.16% | 0.19% | 0.12% | 96% | 102%
Class D | 0.02% | -0.02% | 0.17% | 131% | 106% | 0.13% | 0.22% | -0.05% | 96% | 108%
Class F | -9.37% | -9.40% | -9.41% | 146% | 108% | 3.65% | 3.51% | 3.59% | 94% | 108%
Class SCC | -29.45% | -28.41% | -28.65% | 141% | 102% | 12.44% | 12.67% | 12.72% | 99% | 108%
RA |  |  |  |  |  |  |  |  |  | 
Overall | 0.13% | 0.03% | 0.03% | 98% | 100% | 0.05% | 0.04% | -0.02% | 99% | 100%
Class D | 0.21% | -0.13% | 0.30% | 104% | 103% | 0.05% | 0.15% | 0.14% | 102% | 105%
Class F | -7.76% | -7.73% | -7.78% | 101% | 97% | 2.87% | 2.94% | 2.95% | 97% | 100%
Class SCC | -16.92% | -16.44% | -16.87% | 103% | 100% | 7.01% | 7.02% | 7.16% | 99% | 103%
LDB |  |  |  |  |  |  |  |  |  | 
Overall | 0.14% | 0.10% | -0.10% | 108% | 102% | 0.00% | -0.16% | -0.11% | 101% | 101%
Class D | 0.12% | 0.04% | 0.57% | 113% | 103% | -0.02% | 0.19% | -0.12% | 101% | 102%
Class F | -3.80% | -3.78% | -4.43% | 107% | 103% | 1.61% | 1.85% | 1.28% | 99% | 102%
Class SCC | -9.17% | -9.23% | -9.47% | 109% | 100% | 4.82% | 5.08% | 5.11% | 101% | 105%
AI |  |  |  |  |  |  |  |  |  | 
Over VTM-3.0 |  |  |  |  |  | Over VTM-3 + CPR on + PLT on |  |  |  | 
Y | U | V | EncT | DecT | Y |  | U | V | EncT | DecT
-0.03% | -0.10% | -0.10% | 136% | 105% | 0.16% |  | 0.16% | 0.16% | 95% | 101%
0.13% | 0.14% | 0.31% | 136% | 105% | 0.15% |  | 0.18% | 0.14% | 94% | 99%
-13.59% | -11.82% | -11.95% | 160% | 97% | 2.80% |  | 3.06% | 3.00% | 94% | 101%
-39.57% | -35.42% | -35.60% | 161% | 75% | 9.73% |  | 9.85% | 9.93% | 102% | 101%
RA |  |  |  |  |  |  |  |  |  | 
0.26% | 0.14% | 0.18% | 103% | 99% | 0.06% |  | 0.07% | -0.02% | 99% | 99%
0.42% | 0.08% | 0.46% | 110% | 103% | 0.00% |  | 0.13% | 0.50% | 100% | 102%
-10.43% | -10.06% | -10.23% | 109% | 97% | 2.11% |  | 2.43% | 2.49% | 98% | 98%
-21.98% | -20.79% | -21.02% | 106% | 93% | 5.32% |  | 5.20% | 5.34% | 99% | 98%
LDB |  |  |  |  |  |  |  |  |  | 
0.28% | 0.32% | 0.26% | 114% | 102% | -0.01% |  | -0.02% | 0.17% | 100% | 102%
0.39% | 0.74% | 0.87% | 121% | 102% | 0.00% |  | 0.09% | 0.21% | 102% | 105%
-5.13% | -6.05% | -6.52% | 114% | 101% | 1.25% |  | 0.98% | 0.84% | 100% | 102%
-11.92% | -11.70% | -11.63% | 112% | 94% | 3.62% |  | 3.71% | 3.87% | 101% | 101%

## Slide 8: Conclusions
Result of CE2.4.3 has been reported
Gain for AI and RA are reported without additional memory cost
Results of different CPR areas with VDPU have been reported