## Slide 1: Non-CE4: On Temporal Motion Buffer Compression (JVET-M0512)
F. Bossen, K. Misra, A. Segall

## Slide 2: Overview
Motivation
Proposed Solution
Experimental Results
Recommendations

## Slide 3: Motivation
 | Bits needed for motion vector storage | Bits needed for delta POC storage | Bits needed for long term flag storage | Motion information cell size (in luma samples) | Number of bits per 4x4 luma block
HEVC | 2 * 2 * 16 = 64 | 2 * 8 = 16 | 2 * 1 = 2 | 16 x 16 | (64+16+2)/16 = 5.125
VVC WD | 2 * 2 * 18 = 72 | 2 * 8 = 16 | 2 * 1 = 2 | 8 x 8 | (72+16+2)/4 = 22.5
Proposed | 2 * 2 * 10 = 40 | 0 | 2 * 1 = 2 | 8 x 8 | (40+2)/4 =10.5
Current VVC WD requires 22.5 bits of storage per 4x4 luma sample block for temporal motion buffer. This is more than 4x that needed for HEVC
It is proposed to reduce the required storage (to 10.5 bits) by:
Removing delta POC storage
Reducing MV storage

## Slide 4: Proposed Solution
Remove delta POC storage
  Scale MV during storage to a fixed delta POC (set to 4)
Reducing MV storage
  Use mantissa-exponent representation to store MV (6-bit signed mantissa, 4-bit unsigned exponent)

## Slide 5: Experimental Results
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.04% | 0.02% | 100% | 98%
Class A2 | 0.00% | -0.02% | 0.06% | 97% | 98%
Class B | -0.02% | 0.09% | -0.03% | 100% | 101%
Class C | 0.01% | -0.02% | 0.05% | 100% | 102%
Class E |  |  |  |  | 
Overall | 0.00% | 0.03% | 0.02% | 99% | 100%
Class D | 0.00% | -0.09% | -0.06% | 99% | 101%
Class F (optional) | -0.02% | -0.01% | -0.01% | 99% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.30% | -0.11% | 99% | 101%
Class C | -0.03% | 0.18% | 0.13% | 102% | 102%
Class E | 0.09% | 0.15% | -0.26% | 99% | 104%
Overall | 0.02% | -0.02% | -0.07% | 100% | 102%
Class D | 0.03% | 0.00% | 0.17% | 98% | 100%
Class F (optional) | 0.07% | 0.02% | -0.25% | 101% | 104%
Thank You LGE for providing crosscheck JVET-M0764
Changes to WD provided with contribution

## Slide 6: Recommendation
We propose an approach to reduce this buffer storage requirement to from 22.5 bits to 10.5 bits per 4x4 luma sample block
Average luma BD Rate 0.00% (RA), 0.02% (LDB)
It is recommended that the approach be adopted in the next version of the VVC WD and VTM.