## Slide 1: HEC with Pre-rotation + Adaptive Frame Packing (Test 4.2.a+4.1)
12 January 2019
Samsung Electronics Co. Ltd

## Slide 2: Introduction
In this test Pre-rotation + AFP is implemented on HEC + In-loop filter disabled
This test uses VTM3.0+ 360lib 8.0
This test was performed to check the gain of AFP with pre-rotation

## Slide 3: Results – TEST 13.4.1 + 13.4.2a vs 13.1.1a
 |  | Pre-rotation + AFP |  |  | AFP |  |  | Pre-rotation |  | 
 | Sequence | End-to-end WS-PSNR |  |  | End-to-end WS-PSNR |  |  | End-to-end WS-PSNR |  | 
 |  | Y | U | V | Y | U | V | Y | U | V
Class S1 | SkateboardInLot | -0.41% | 0.29% | 0.65% | -0.41% | 0.29% | 0.65% | -0.16% | -0.51% | 0.57%
 | ChairLift | -0.29% | 0.82% | -0.82% | -0.29% | 0.82% | -0.82% | -0.31% | -0.42% | -0.77%
 | KiteFlite | -0.03% | -0.13% | 0.65% | -0.16% | -0.08% | 0.43% | 0.20% | -0.20% | 1.19%
 | Harbor | -1.58% | -2.90% | -2.62% | -0.52% | -0.65% | -0.72% | -1.26% | -2.05% | -2.07%
 | Trolley | -0.36% | -0.99% | -0.69% | -0.63% | -0.84% | -0.87% | 0.19% | -0.17% | -0.05%
 | GasLamp | -2.78% | -6.13% | -8.72% | -0.74% | -0.95% | -0.81% | -2.59% | -6.22% | -8.51%
Class S2 | Balboa | -0.11% | 0.20% | -0.30% | -0.11% | 0.20% | -0.30% | 0.00% | 0.00% | 0.00%
 | Broadway | 0.06% | 1.31% | 0.41% | 0.06% | 1.31% | 0.41% | 0.00% | 0.00% | 0.00%
 | Landing2 | -0.03% | 0.44% | 0.18% | -0.03% | 0.44% | 0.18% | 0.00% | 0.00% | 0.00%
 | BranCastle2 | -0.17% | 0.43% | 0.04% | -0.17% | 0.43% | 0.04% | 0.00% | 0.00% | 0.00%
 | Class S1 | -0.91% | -1.51% | -1.93% | -0.46% | -0.23% | -0.36% | -0.66% | -1.59% | -1.61%
 | Class S2 | -0.06% | 0.59% | 0.08% | -0.06% | 0.59% | 0.08% | 0.00% | 0.00% | 0.00%
 | All | -0.57% | -0.67% | -1.12% | -0.30% | 0.10% | -0.18% | -0.39% | -0.96% | -0.96%

## Slide 4: Observations
Pre-rotation + AFP together provides 0.57% BD gain while AFP alone provides 0.3% gain and pre-rotation alone provides 0.39% gain
For Gaslamp achieved gain is maximum which is 2.78%
More gain is observed in case of 8k sequences

## Slide 5
Thank you