## Slide 1: CE4-related: Simplified coding of the MVP index
JVET-N0287
March. 2019
F. Le Léannec, Y. Chen, T. Poirier, A. Robert

## Slide 2: JVET-N0287
  VTM-4.0 AMVP mode
    2 MV prediction candidates are considered
    The MV predictors used for a CU are signaled by two flag: mvp_l0_flag and mvp_l1_flag
    mvp_l0_flag and mvp_l1_flag are context-based coded

## Slide 3: JVET-N0287
  Proposed
    Bypass coding of mvp_l0_flag and mvp_l1_flag
    Applied in AMVP, Affine AMVP and IBC AMVP

## Slide 4: JVET-N0287
  Results
    RA: 0.02%
    LDB: 0.02%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.11% | 0.04% | 100% | 99%
Class A2 | 0.00% | 0.04% | 0.04% | 100% | 100%
Class B | 0.03% | 0.00% | 0.02% | 101% | 100%
Class C | 0.02% | 0.01% | -0.12% | 101% | 102%
Class E |  |  |  |  | 
Overall | 0.02% | -0.01% | -0.01% | 101% | 100%
Class D | 0.00% | -0.06% | -0.08% | 100% | 101%
Class F (optional) | 0.09% | 0.04% | -0.07% | 100% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | 0.01% | 0.02% | 106% | 106%
Class C | -0.02% | 0.16% | -0.13% | 104% | 101%
Class E | 0.06% | -0.14% | 0.33% | 101% | 101%
Overall | 0.02% | 0.02% | 0.05% | 104% | 103%
Class D | -0.01% | -0.53% | -0.55% | 99% | 99%
Class F (optional) | -0.09% | -0.29% | 0.03% | 100% | 101%

## Slide 5: JVET-N0287
  Additional Results: combination with JVET-N0286 (simplified Gbi index coding)
    RA: 0.02%
    LDB: 0.03%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.12% | 0.01% | 102% | 101%
Class A2 | 0.00% | -0.03% | 0.08% | 103% | 101%
Class B | 0.02% | 0.01% | 0.00% | 101% | 101%
Class C | 0.04% | 0.03% | -0.13% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.02% | -0.02% | -0.02% | 101% | 101%
Class D | 0.01% | -0.03% | -0.06% | 100% | 101%
Class F (optional) | 0.09% | 0.05% | -0.10% | 102% | 104%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.02% | -0.09% | 0.04% | 107% | 108%
Class C | -0.01% | 0.19% | 0.02% | 102% | 99%
Class E | 0.11% | 0.29% | 0.03% | 102% | 101%
Overall | 0.03% | 0.10% | 0.03% | 104% | 103%
Class D | 0.03% | -0.01% | -0.32% | 103% | 103%
Class F (optional) | -0.05% | -0.36% | 0.09% | 102% | 101%

## Slide 6: JVET-N0287
  Conclusion
    Propose to code mvp_l0_flag and mvp_l1_flag elements in bypass mode
    Minor impact on coding efficiency
    Suggestion: Adopt in VTM-5
    We thank Qualcomm for cross-checking this contribution