## Slide 1: JVET-O0231: Non-CE7: Modified chroma coded block flag signalling
Semih Esenlik, Anand Meher Kotra, Biao Wang, Han Gao, Elena Alshina (Huawei)

## Slide 2
Introduction
tu_joint_cbcr_residual flag was introduced in VVC in 14th JVET Meeting. if tu_joint_cbcr_residual is equal to 1, residuals of Cr block are derived from Cb block:
resSamplesCr[ x ][ y ] = -resSamplesCb[ x ][ y ]
Chroma cbf syntax according to current VVC:
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex ) { | Descriptor
if( ( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_CHROMA ) { | 
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) ) ¦ ¦ ( IntraSubPartitionsSplitType != ISP_NO_SPLIT && ( subTuIndex = = NumIntraSubPartitions − 1 ) ) ) { | 
tu_cbf_cb[ x0 ][ y0 ] | ae(v)
tu_cbf_cr[ x0 ][ y0 ] | ae(v)
} | 
} | 
… | 
… | 
if( tu_cbf_cr[ x0 ][ y0 ] ) { | 
if( tu_cbf_cb[ x0 ][ y0 ] ) | 
tu_joint_cbcr_residual[ x0 ][ y0 ] | ae(v)
if( !tu_joint_cbcr_residual[ x0 ][ y0 ] ) | 
residual_coding( xC, yC, Log2( wC ), Log2( hC ), 2 ) | 
} | 
} | 

## Slide 3: Problem statement
The statistical analysis show that the following are the cases according to likelihood of occurrence:
  Both Cb and Cr residual are zero
  Both Cb and Cr has residual, tu_joint_cbcr_residual is equal to 1
  Both Cb and Cr has residual, tu_joint_cbcr_residual is equal to 0
  Only Cb has residual
  Only Cr has residual (almost same probability as 4)
  The binarization of chroma cbf can be improved.

## Slide 4: Proposed chroma cbf signalling
tu_cbf_cb_or_cr indicates at least one of Cb or Cr has residual.
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex ) { | Descriptor
if( ( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_CHROMA ) { | 
if( ( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !( cu_sbt_flag && ( ( subTuIndex = = 0 && cu_sbt_pos_flag ) ¦ ¦ ( subTuIndex = = 1 && !cu_sbt_pos_flag ) ) ) ) ¦ ¦ ( IntraSubPartitionsSplitType != ISP_NO_SPLIT && ( subTuIndex = = NumIntraSubPartitions − 1 ) ) ) { | 
tu_cbf_cb_or_cr[ x0 ][ y0 ] | ae(v)
if( tu_cbf_cb_or_cr[ x0 ][ y0 ] ) { | 
tu_joint_cbcr_residual[ x0 ][ y0 ] | ae(v)
if( !tu_joint_cbcr_residual[ x0 ][ y0 ] ) { | 
tu_cbf_cb_and_cr [ x0 ][ y0 ] | ae(v)
if( !tu_cbf_cb_and_cr[ x0 ][ y0 ] ) { | 
tu_cbf_cb [ x0 ][ y0 ] | ae(v)
tu_cbf_cr [ x0 ][ y0 ] = !tu_cbf_cb [ x0 ][ y0 ] | 
} | 
if (tu_cbf_cb_and_cr[ x0 ][ y0 ] ¦¦ tu_joint_cbcr_residual[ x0 ][ y0 ] { | 
tu_cbf_cr [ x0 ][ y0 ] = true | 
tu_cbf_cb [ x0 ][ y0 ] = true | 
} | 
} | 
} | 
else { | 
tu_cbf_cr [ x0 ][ y0 ] = false | 
tu_cbf_cb [ x0 ][ y0 ] = false | 
} | 
} | 
} | 
tu_joint_cbcr_residual indicates both Cb and Cr have residual and residuals are mirrored.
tu_cbf_cb_and_cr indicates both Cb and Cr have residual and residuals are not mirrored.
tu_cbf_cb_and_cr equal to 0 indicates only one of Cb or Cr has residual. tu_cbf_cb indicated which one (Cb or Cr).

## Slide 5: Context modelling
Number of contexts are reduced by 2.
Worst case number of context coded bins are unchanged (3 ctx per coding block).
Average number context coded bins are reduced (due to syntax more aligned with statistics and 1 bypass coded bin)
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
tu_cbf_cb[ ][ ][ ] | trDepth = = 0 ? 0 : 1 | na | na | na | na | na
tu_cbf_cr[ ][ ][ ] | tu_cbf_cb[ ][ ][ ] | na | na | na | na | na
tu_joint_cbcr_residual[ ][ ] | 0 | na | na | na | na | na
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
tu_cbf_cb[ ][ ][ ] | bypass | na | na | na | na | na
tu_cbf_cb_or_cr[ ][ ][ ] | 0 | na | na | na | na | na
tu_cbf_cb_and_cr[ ][ ] | 0 | na | na | na | na | na
tu_joint_cbcr_residual[ ][ ] | 0 | na | na | na | na | na
Proposed
VTM5.0

## Slide 6: Simulation results
 | All Intra Main10 |  |  |  |  | 
 | Over VTM 5.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | 0.16% | -1.53% | -0.41% | 101% | 100% | -0.12%
Class A2 | 0.20% | -2.17% | -0.40% | 101% | 101% | -0.17%
Class B | 0.11% | -0.81% | -1.80% | 101% | 100% | -0.24%
Class C | 0.11% | -0.90% | -1.33% | 101% | 101% | -0.20%
Class E | 0.09% | -0.89% | -1.69% | 101% | 100% | -0.25%
Overall | 0.13% | -1.19% | -1.21% | 101% | 100% | -0.20%
Class D | 0.10% | -0.86% | -0.92% | 101% | 101% | -0.15%
Class F | 0.10% | -0.61% | -0.83% | 101% | 101% | -0.10%
 | Random Access Main 10 |  |  |  |  | 
 | Over VTM 5.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 | 0.35% | -2.49% | -1.88% | 101% | 101% | -0.28%
Class A2 | 0.28% | -2.10% | -1.32% | 101% | 102% | -0.22%
Class B | 0.17% | -1.32% | -3.94% | 101% | 101% | -0.53%
Class C | 0.12% | -1.17% | -3.02% | 101% | 101% | -0.44%
Class E |  |  |  |  |  | 0.00%
Overall | 0.21% | -1.67% | -2.76% | 101% | 101% | -0.39%
Class D | 0.12% | -1.31% | -1.71% | 100% | 101% | -0.29%
Class F | 0.15% | -0.75% | -1.09% | 101% | 102% | -0.12%
 | Low delay B Main10 |  |  |  |  | 
 | Over VTM 5.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.16% | -0.31% | -4.91% | 102% | 104% | -0.54%
Class C | 0.17% | -0.64% | -3.61% | 101% | 101% | -0.40%
Class E | 0.02% | -0.17% | -1.58% | 101% | 103% | -0.21%
Overall | 0.13% | -0.38% | -3.65% | 101% | 103% | -0.41%
Class D | 0.14% | -0.32% | -1.58% | 100% | 101% | -0.14%
Class F | 0.21% | -0.67% | -1.52% | 101% | 102% | -0.12%
 | Low delay P Main10 |  |  |  |  | 
 | Over VTM 5.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | YUV
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.12% | -0.46% | -5.48% | 101% | 102% | -0.65%
Class C | 0.17% | -0.71% | -3.41% | 101% | 101% | -0.39%
Class E | 0.06% | 0.09% | -1.98% | 101% | 101% | -0.19%
Overall | 0.12% | -0.41% | -3.92% | 101% | 101% | -0.45%
Class D | 0.17% | -1.22% | -2.28% | 101% | 101% | -0.31%
Class F | 0.28% | -0.21% | -0.53% | 103% | 104% | 0.12%
  Proposal only modifies the signalling. Encoder logic is not changed.
  YUV gain according to (6Y+U+V)/8.

## Slide 7: Conclusion
A modified signalling for chroma coded block flags are proposed.
0.4% YUV gain in RA configuration.
Only signalling part is modified, no change in encoding logic.
Proposed to be adopted in next VVC draft.

## Slide 9: Average context coded bins
 | VTM5.0 tu_cbf_cb + tu_cbf_cr + tu_joint_cbcr_residual | Proposed tu_cbf_cb_or_cr + tu_cbf_cb_and_cr + tu_joint_cbcr_residual
Basketballpass QP 22, Intra Only | 96375 | 81213
BlowingBubbles QP 37, Intra Only | 51572 | 40365
BQSquare QP 32, Intra Only | 38435 | 28136
  Change in the number of total context coded bins: