## Slide 1: JVET-O0803: Non-CE5: Unified design for longer tap deblocking line buffer reduction
Anand Meher Kotra, Semih Esenlik, Biao Wang, Han Gao, Elena Alshina

## Slide 2: VTM-5.0 Luma and Chroma deblocking at horizontal CTU boundaries
Longer tap deblocking in VTM-5.0 changes 3 samples on either side of the edge (3 + 3) when the size of both blocks adjacent to the edge is >=8 samples
Due to line buffer restrictions of 2 lines, Chroma longer tap deblocking is completely switched off and only the weak filter (1 + 1) can be used, whereas for Luma deblocking longer tap asymmetric filter (3 + 7) is used.
For large blocks at the horizontal Chroma CTU boundaries, still sufficient blocking artifacts might still remain (especially for 4:2:2 and 4:4::4 content)

## Slide 3: Proposal
Proposal is to use an asymmetric longer tap filter (1 + 3) also at the Chroma CTU boundaries to more efficiently remove the blocking artifacts.

## Slide 4: Simple change to filtering decision
For the longer tap filter decision, the original filter equations are as follows:
dp0 = Abs( p2,0 − 2 * p1,0 + p0,0 ) (8‑1092)
dp1 = Abs( p2,1 − 2 * p1,1 + p0,1 ) (8‑1093)
dq0 = Abs( q2,0 − 2 * q1,0 + q0,0 ) (8‑1094)
dq1 = Abs( q2,1 − 2 * q1,1 + q0,1 ) (8‑1095)
At the horizontal CTU boundaries the modified longer tap filter decisions are as follows: (p2,0, p2,1 are simply replaced with p1,0 and p1,1), only dp0 and dp1 are changed
dp0 = Abs( p21,0 − 2 * p1,0 + p0,0 ) (8‑1092)
dp1 = Abs( p21,1 − 2 * p1,1 + p0,1 ) (8‑1093)

## Slide 5: Modified filtering equations
The original longer tap filtering equations for Chroma longer tap deblocking are as follows:
p0′ = Clip3( p0 − tC, p0 + tC, ( p3 + p2 + p1 + 2 * p0 + q0 + q1 + q2 + 4 ) >> 3 ) (8‑1151)
p1′ = Clip3( p1 − tC, p1 + tC, ( 2 * p3 + p2 + 2 * p1 + p0 + q0 + q1 + 4 ) >> 3 ) (8‑1152)
p2′ = Clip3( p2 − tC, p2 + tC, ( 3 * p3 + 2 * p2 + p1 + p0 + q0 + 4 ) >> 3 ) (8‑1153)
q0′ = Clip3( q0 − tC, q0 + tC, ( p2 + p1 + p0 + 2 * q0 + q1 + q2 + q3 + 4 ) >> 3 ) (8‑1154)
q1′ = Clip3( q1 − tC, q1 + tC, ( p1 + p0 + q0 + 2 * q1 + q2 + 2 * q3 + 4 ) >> 3 ) (8‑1155)
q2′= Clip3( q2 − tC, q2 + tC, ( p0 + q0 + q1 + 2 * q2 + 3 * q3 + 4 ) >> 3 ) (8‑1156)
At the horizontal CTU boundaries the modified longer tap deblocking equations are as follows:
p0′ = Clip3( p0 − tC, p0 + tC, ( p3 + p2 + 3 * p1 + 2 * p0 + q0 + q1 + q2 + 4 ) >> 3 ) (8‑1151)
p1′ = Clip3( p1 − tC, p1 + tC, ( 2 * p3 + p2 + 2 * p1 + p0 + q0 + q1 + 4 ) >> 3 ) (8‑1152)
p2′ = Clip3( p2 − tC, p2 + tC, ( 3 * p3 + 2 * p2 + p1 + p0 + q0 + 4 ) >> 3 ) (8‑1153)
q0′ = Clip3( q0 − tC, q0 + tC, ( p2 + 2 * p1 + p0 + 2 * q0 + q1 + q2 + q3 + 4 ) >> 3 ) (8‑1154)
q1′ = Clip3( q1 − tC, q1 + tC, ( p1 + p0 + q0 + 2 * q1 + q2 + 2 * q3 + 4 ) >> 3 ) (8‑1155)
q2′= Clip3( q2 − tC, q2 + tC, ( p0 + q0 + q1 + 2 * q2 + 3 * q3 + 4 ) >> 3 ) (8‑1156)

## Slide 6
VTM-5.0, ALF OFF, LDB, Candlelight 4:4:4, frame no: 123

## Slide 7
Proposal, LDB, Candlelight 4:4:4, frame no: 123

## Slide 8
CTC
ALF OFF

## Slide 9: Conclusion
Propose to switch on the longer tap filter ( 1+ 3) version at the horizontal Chroma CTB boundary.
No major BD-Rate impact.
Specification text changes are attached along with the contribution
Suggest to be adopted as it is a unification of deblocking design for Luma and Chroma
Thanks to MediaTek for crosscheck (JVET-O0809)

## Slide 10
Thank You
www.huawei.com