## Slide 1
JVET-P0486
CE8-related: Alignment of maximum transform-skip size with maximum transform block size
2019/10/3

## Slide 2
Problem statement
The PPS syntax log2_transform_skip_max_size_minus2 specifies the maximum block size used for TS mode, and is in the range of 0 to 3.
A decoder need to support all 4 possible values of log2_transform_skip_max_size_minus2.
It is asserted that given the maximum TB size can have only 2 values (32 or 64), this flexibility of maximum TS block size is unnecessary.

## Slide 3
Proposed Method 1: Remove max TS size signaling
Align maximum TS size with maximum TB size
If maximum TB size is 32, maximum TS size is 32. If maximum TB size is 64, maximum TS size is 64.
if( tu_cbf_luma[ x0 ][ y0 ] && treeType != DUAL_TREE_CHROMA && ( tbWidth <= 32 ) && ( tbHeight <= 32 ) && ( IntraSubPartitionsSplit[ x0 ][ y0 ] = = ISP_NO_SPLIT ) && ( !cu_sbt_flag ) ) { | 
if( sps_transform_skip_enabled_flag && !BdpcmFlag[ x0 ][ y0 ] && tbWidth <= MaxTsSize && tbHeight <= MaxTsSize ) | 
transform_skip_flag[ x0 ][ y0 ] | ae(v)
if( ( ( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTER && sps_explicit_mts_inter_enabled_flag ) ¦ ¦ ( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && sps_explicit_mts_intra_enabled_flag ) ) && ( !transform_skip_flag[ x0 ][ y0 ] ) && tbWidth <= 32 && tbHeight <= 32) | 
tu_mts_idx[ x0 ][ y0 ] | ae(v)
} | 
if( sps_bdpcm_enabled_flag && cbWidth <= MaxTsSize MaxTbSizeY && cbHeight <= MaxTsSize MaxTbSizeY) | 
intra_bdpcm_flag | ae(v)

## Slide 4
Proposed Method 2: allow 2 values of max TS size
An SPS flag is signaled to indicate if maximum TS size is either 32 or 64.
seq_parameter_set_rbsp( ) { | Descriptor
sps_max_luma_transform_size_64_flag | u(1)
. | 
. | 
sps_transform_skip_enabled_flag | u(1)
if( sps_transform_skip_enabled_flag){ | 
sps_bdpcm_enabled_flag | u(1)
if (sps_max_luma_transform_size_64_flag) | 
sps_max_transform_skip_size_64_flag | u(1)
} | 
} | 
The maximum value of width or height of the TS mode is computed as follows:
  MaxTsSize = sps_max_transform_skip_size_64_flag ? 64 : 32

## Slide 5
Proposed Method: Residual coding of large transform unit
VVC6 residual coding supports up-to 32x32 coefficient scanning
In order to re-use the existing VVC6 coefficient scanning, the proposed method divides a transform block into small residual unit (RU).
The maximum number of context coded bins are allocated based on RU.
Context model, Rice-parameter derivation, level mapping of one RU do not depend on other.
Figure 1: An illustration of RU (a) a 64x64 TB is divided into 4 32x32 RUs, (b) a 64x16 TB is divided into 2 32x16 RUs, (c) a 32x64 TB is divided into 2 32x32 RUs and (d) partition is not necessary since both the width and height are 32.

## Slide 6
Simulation results
In both tests, the maximum TS and BDPCM size are aligned with max TB which is 64 in CTC test condition.
  Test 1: Whole transform block scanning (i.e. maximum 64x64 coefficient scanning)
  Test 2: Divide TB to RU (max RU size 32x32, therefore, maximum 32x32 coefficient scanning)

## Slide 7
Simulation results : Test 1
CTC QP
Low QP
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.02% | 100% | 101%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 101%
Class B | 0.01% | 0.00% | -0.01% | 100% | 102%
Class C | 0.00% | 0.00% | -0.01% | 100% | 104%
Class E | 0.00% | -0.01% | -0.03% | 100% | 105%
Overall | 0.00% | 0.00% | -0.01% | 100% | 103%
Class D | 0.00% | 0.00% | 0.00% | 98% | 106%
Class F | -0.04% | -0.04% | -0.10% | 101% | 102%
Class SCC | -0.02% | -0.02% | -0.02% | 101% | 101%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.05% | -0.02% | 101% | 101%
Class A2 | 0.04% | -0.02% | 0.02% | 101% | 101%
Class B | -0.02% | 0.15% | 0.01% | 101% | 102%
Class C | 0.00% | 0.05% | -0.02% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.00% | 0.05% | 0.00% | 101% | 101%
Class D | -0.01% | 0.05% | -0.03% | 101% | 102%
Class F | -0.06% | -0.10% | -0.02% | 101% | 103%
Class SCC | -0.15% | -0.13% | -0.14% | 103% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | -0.06% | -0.22% | 101% | 101%
Class C | 0.01% | 0.13% | -0.07% | 102% | 104%
Class E | -0.02% | 0.38% | 0.89% | 102% | 103%
Overall | 0.01% | 0.11% | 0.11% | 102% | 103%
Class D | 0.04% | 0.42% | 0.03% | 101% | 108%
Class F | -0.06% | 0.35% | 0.26% | 102% | 103%
Class SCC | -0.12% | -0.09% | -0.06% | 104% | 105%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 100% | 101%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 101%
Class B | 0.00% | -0.01% | 0.00% | 99% | 101%
Class C | 0.00% | 0.00% | 0.00% | 98% | 102%
Class E | 0.00% | 0.00% | 0.00% | 100% | 101%
Overall | 0.00% | 0.00% | 0.00% | 99% | 101%
Class D | 0.00% | 0.00% | 0.00% | 100% | 105%
Class F | -0.01% | -0.04% | 0.03% | 100% | 99%
Class SCC | -0.02% | 0.00% | -0.02% | 99% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | -0.03% | 100% | 104%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 103%
Class B | 0.01% | 0.01% | 0.00% | 100% | 105%
Class C | 0.00% | -0.01% | 0.00% | 100% | 105%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.01% | 100% | 104%
Class D | 0.00% | 0.01% | 0.01% | 100% | 107%
Class F | -0.11% | -0.20% | -0.21% | 101% | 110%
Class SCC | -0.06% | -0.07% | -0.07% | 102% | 115%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 101% | 102%
Class C | 0.00% | 0.00% | -0.01% | 100% | 103%
Class E | 0.01% | -0.01% | 0.06% | 100% | 104%
Overall | 0.00% | 0.00% | 0.01% | 101% | 103%
Class D | 0.00% | -0.01% | -0.05% | 100% | 105%
Class F | 0.02% | -0.03% | -0.09% | 102% | 101%
Class SCC | -0.10% | -0.09% | 0.02% | 102% | 99%

## Slide 8
Simulation results : Test 2
CTC QP
Low QP
* RA results will be updated
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.03% | 100% | 100%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 100%
Class B | 0.01% | 0.00% | -0.01% | 100% | 102%
Class C | 0.00% | 0.00% | -0.01% | 100% | 104%
Class E | 0.00% | -0.01% | -0.03% | 101% | 104%
Overall | 0.00% | 0.00% | 0.00% | 100% | 102%
Class D | 0.00% | 0.00% | 0.00% | 99% | 106%
Class F | -0.05% | -0.05% | -0.13% | 101% | 99%
Class SCC | -0.02% | -0.02% | -0.01% | 101% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.05% | -0.03% | 102% | 100%
Class A2 | 0.04% | -0.02% | 0.03% | 101% | 100%
Class B | -0.02% | 0.15% | 0.01% | 101% | 101%
Class C | 0.00% | 0.05% | -0.02% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.05% | 0.00% | 101% | 100%
Class D | -0.01% | 0.05% | -0.01% | 101% | 101%
Class F | -0.07% | -0.11% | 0.01% | 101% | 100%
Class SCC | -0.13% | -0.16% | -0.17% | 102% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | 0.12% | -0.09% | 101% | 100%
Class C | 0.01% | 0.11% | 0.01% | 102% | 104%
Class E | 0.00% | 0.56% | 0.80% | 102% | 102%
Overall | 0.01% | 0.22% | 0.17% | 102% | 102%
Class D | 0.05% | 0.27% | 0.32% | 101% | 107%
Class F | 0.06% | -0.19% | 0.41% | 101% | 99%
Class SCC | -0.20% | -0.17% | -0.17% | 103% | 103%
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.01% | 0.00% | 100% | 98%
Class A2 | 0.00% | 0.00% | 0.00% | 100% | 98%
Class B | 0.00% | -0.01% | 0.00% | 100% | 98%
Class C | 0.00% | 0.00% | 0.00% | 98% | 100%
Class E | 0.00% | 0.00% | 0.00% | 99% | 98%
Overall | 0.00% | 0.00% | 0.00% | 99% | 98%
Class D | 0.00% | 0.00% | 0.00% | 100% | 103%
Class F | 0.03% | -0.03% | 0.01% | 100% | 99%
Class SCC | -0.01% | -0.02% | -0.02% | 99% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.01% | -0.02% | 100% | 99%
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.02% | 0.00% | 100% | 101%
Class C | 0.00% | -0.01% | 0.00% | 100% | 101%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.00% | 0.01% | 0.01% | 101% | 103%
Class F | -0.08% | -0.18% | -0.12% | 101% | 110%
Class SCC | -0.08% | -0.10% | -0.06% | 103% | 114%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.01% | -0.02% | 101% | 97%
Class C | 0.00% | 0.00% | -0.01% | 101% | 100%
Class E | 0.01% | -0.01% | 0.06% | 100% | 99%
Overall | 0.00% | 0.00% | 0.00% | 101% | 98%
Class D | 0.00% | -0.01% | -0.05% | 101% | 101%
Class F | -0.01% | -0.09% | 0.02% | 102% | 100%
Class SCC | -0.21% | -0.21% | -0.13% | 103% | 98%

## Slide 9
Conclusion
Summary results
  Test 1: -0.02% (AI), -0.15% (RA), -0.12% (LB) luma BD-rate
  Test 2: -0.02% (AI), -0.13% (RA), -0.20% (LB) luma BD-rate
Align max TS size to max TB size
Supports coefficient scanning of large ( > 32) TB using existing 32x32 coefficient scanning.