## Slide 1: CE4-related: On MVD derivation in PROF
Hongbin Liu, Li Zhang, Kai Zhang, Yang Wang, Jizheng Xu, Yue Wang

## Slide 2: Summary
Problem
  In PROF, position (x, y) and position (3 – x, 3 – y) have opposite MVD values in theory.
  However, unsymmetrical MVD clipping range [-32 31] breaks this behavior.
  Solution
  Modified MVD clipping range to be symmetrical
    From [-32, 31] to [-31 31]
    For both PROF and BDOF
Benefit
  Flexibility to use different ways for implementation
    Derive MVD using affine parameters (followed by rounding and clipping) for half positions, and use their opposite values for the other half positions directly
      Save computational complexity (MVD calculation/clipping) by 50%
    Or use current design, per sample calculation (identical results)
Figure 1: position pairs (e.g., positions with same color) having opposite MVD values.

## Slide 3: Simulation results
Anchor: CE4-2.1 (adopted in this meeting)
 | RA |  |  |  |  | LDB |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.01% | 0.04% | 100% | 99% |  |  |  |  | 
Class A2 | 0.02% | 0.10% | -0.04% | 100% | 102% |  |  |  |  | 
Class B | -0.01% | -0.03% | -0.10% | 100% | 100% | 0.01% | -0.06% | 0.50% | 101% | 101%
Class C | 0.00% | 0.01% | 0.01% | 100% | 101% | -0.05% | 0.06% | -0.36% | 100% | 100%
Class E |  |  |  |  |  | -0.06% | 0.11% | -0.54% | 99% | 101%
Overall | 0.00% | 0.01% | -0.03% | 100% | 100% | -0.02% | 0.02% | -0.05% | 100% | 101%
Class D | -0.06% | -0.04% | 0.01% | 99% | 99% | 0.04% | -0.01% | 0.27% | 101% | 104%
Class F | 0.00% | -0.01% | 0.01% | 100% | 100% | 0.03% | 0.05% | -0.04% | 100% | 101%

## Slide 4: Simulation results
Anchor: VTM-6.0
 | RA |  |  |  |  | LDB |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.07% | 0.04% | 99% | 99% |  |  |  |  | 
Class A2 | 0.03% | 0.04% | 0.00% | 99% | 99% |  |  |  |  | 
Class B | 0.00% | 0.05% | 0.06% | 100% | 100% | 0.00% | -0.22% | -0.03% | 100% | 100%
Class C | 0.00% | 0.02% | -0.01% | 100% | 100% | -0.06% | 0.15% | 0.06% | 100% | 96%
Class E |  |  |  |  |  | -0.03% | 0.29% | -0.21% | 100% | 99%
Overall | 0.01% | 0.02% | 0.03% | 100% | 100% | -0.03% | 0.03% | -0.05% | 100% | 98%
Class D | -0.04% | -0.08% | 0.01% | 100% | 100% | -0.04% | 0.15% | 0.37% | 100% | 97%
Class F | -0.01% | -0.01% | -0.02% | 100% | 99% | 0.08% | 0.00% | 1.10% | 100% | 99%

## Slide 5: Conclusions
MVD range of PROF and BDOF are changed to [-31 31]. Minor change of current design.
Can save the MVD derivation process for half of the positions.
Negligible impact on coding performance.
Thanks to Sharp for crosschecking this proposal! JVET-P0745