## Slide 1: JVET-P0532 CE4-related: Modified hpelIfIdx derivation for half-pel interpolation filter
Y. Kidani, K. Kawamura, K. Unno and S. Naito
KDDI Corp. (KDDI Research Inc.)

## Slide 2: Summary
In the previous meeting, half-pel interpolation filter (HPEL-IF) was adopted to improve coding gain.
In the current design, HPEL-IF is determined by hpelIfIdx and motion vector reference position (MV-pos.) which are inherited in merge mode.
MV-pos., however, may shift from half-pel position if pair-wise average merge mode, MMVD, or DMVR are used.
Modified hpelIfIdx derivation is proposed according to the MV-pos. if pair-wise average merge mode, MMVD or DMVR are used.
Results show overall luma BD-rate 0.02%/-0.01% for RA/LDB over VTM6.

## Slide 3: Problem Statement
HPEL-IF is applied when hpelIfIdx is valid and MV-pos. locates at half-pel.
In merge mode, hpelIfIdx and MV-pos. are inherited from existing CUs.
Even though hpelIfIdx is valid, MV-pos. may shift from half-pel positon if pair-wise average merge, MMVD or DMVR used.
This mismatch causes two problems as follows:
  The mismatch will drift to following CUs from the current CU.
  Different characteristic’s interpolation filters may be applied for bi-pred. inter blocks or in x and y directions.

## Slide 4: Proposal
Modified hpelfIdx derivation according to MV-Pos. is proposed.
  hpelIfIdx is modified from 1 to 0 if MV-pos. shifts from half-pel by pair-wise average merge, MMVD or DMVR.
It is noted that, in DMVR case, non-modified hpelIfIdx is inherited to following to avoid the dependency between blocks.

## Slide 5: Results
Proposal is implemented on top of VTM6.
 | RA over VTM6 |  |  |  |  | LDB over VTM5 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | -0.03% | 100% | 100% |  |  |  |  | 
Class A2 | 0.03% | 0.08% | 0.03% | 100% | 100% |  |  |  |  | 
Class B | 0.02% | 0.09% | 0.01% | 100% | 100% | 0.01% | 0.00% | -0.18% | 100% | 100%
Class C | 0.00% | 0.04% | -0.07% | 101% | 100% | -0.03% | -0.08% | -0.01% | 100% | 101%
Class E |  |  |  |  |  | -0.02% | 0.20% | 0.15% | 100% | 101%
Overall | 0.02% | 0.06% | -0.01% | 100% | 100% | -0.01% | 0.02% | -0.04% | 100% | 101%
Class D | -0.05% | -0.01% | 0.21% | 100% | 100% | -0.02% | -0.14% | 0.43% | 100% | 101%
Class F | -0.01% | 0.03% | -0.01% | 100% | 101% | 0.01% | 0.23% | 0.02% | 100% | 101%

## Slide 6: Conclusion
Modifed hpelIfIdx derivation according MV-Pos. is proposed.
Results show overall BD-rates and runtime are almost same as VTM6
    RA: BD-rate (Y/U/V) 0.02%/0.06%/-0.01%, Runtime (EncT/DecT) 100%/100%
    LDB: BD-rate (Y/U/V) -0.01%/0.02%/-0.04%, Runtime (EncT/DecT) 100%/101%
Suggest to adopt the proposal to WD/VTM.
Thanks for LGE cross checking.