## Slide 1
JVET-P0541
Non-CE4: Context modeling for inter prediction mode
October 2019
LG Electronics
Junghak Nam (junghak.nam@lge.com)

## Slide 2: Background
In current VVC draft, inter_pred_idc syntax is signaled up to 2 bits
  To specify inter prediction mode e.g. PRED_L0, PRED_L1, and PRED_BI
  5 context models
  Some context sharing between the first and the second bins
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
inter_pred_idc[ x0 ][ y0 ] | ( cbWidth + cbHeight ) != 12 ? 7 − ( ( 1 + Log2( cbWidth ) + Log2( cbHeight ) ) >> 1 ) : 4 | 4 | na | na | na | na
 |  | Width |  |  |  |  | 
 |  | 4 | 8 | 16 | 32 | 64 | 128
Height | 4 | N/A | x, 4 | 4, 4 | 3, 4 | 3, 4 | N/A
 | 8 | x, 4 | 4, 4 | 3, 4 | 3, 4 | 2, 4 | N/A
 | 16 | 4, 4 | 3, 4 | 3, 4 | 2, 4 | 2, 4 | N/A
 | 32 | 3, 4 | 3, 4 | 2, 4 | 2, 4 | 1, 4 | N/A
 | 64 | 3, 4 | 2, 4 | 2, 4 | 1, 4 | 1, 4 | 0, 4
 | 128 | N/A | N/A | N/A | N/A | 0, 4 | 0, 4

## Slide 3: Proposed method
Method 1
  Add a operation to prevent sharing context models
  or: ( cbWidth + cbHeight ) != 12 ? min(3, 7 − ( ( 1 + Log2( cbWidth ) + Log2( cbHeight ) ) >> 1 )) : 4
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
inter_pred_idc[ x0 ][ y0 ] | ( cbWidth + cbHeight ) != 12 ? Clip3(0, 3, 7 − ( ( 1 + Log2( cbWidth ) + Log2( cbHeight ) ) >> 1 )) : 4 | 4 | na | na | na | na
 |  | Width |  |  |  |  | 
 |  | 4 | 8 | 16 | 32 | 64 | 128
Height | 4 | N/A | x, 4 | 3, 4 | 3, 4 | 3, 4 | N/A
 | 8 | x, 4 | 3, 4 | 3, 4 | 3, 4 | 2, 4 | N/A
 | 16 | 3, 4 | 3, 4 | 3, 4 | 2, 4 | 2, 4 | N/A
 | 32 | 3, 4 | 3, 4 | 2, 4 | 2, 4 | 1, 4 | N/A
 | 64 | 3, 4 | 2, 4 | 2, 4 | 1, 4 | 1, 4 | 0, 4
 | 128 | N/A | N/A | N/A | N/A | 0, 4 | 0, 4

## Slide 4: Proposed method
Method 2
  Add a operation to prevent sharing context models
  Shifting selection of context model depending on block size
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
inter_pred_idc[ x0 ][ y0 ] | ( cbWidth + cbHeight ) != 12 ? max(0, 6 − ( ( Log2( cbWidth ) + Log2( cbHeight ) ) >> 1 )) : 4 | 4 | na | na | na | na
 |  | Width |  |  |  |  | 
 |  | 4 | 8 | 16 | 32 | 64 | 128
Height | 4 | N/A | x, 4 | 3, 4 | 3, 4 | 2, 4 | N/A
 | 8 | x, 4 | 3, 4 | 3, 4 | 2, 4 | 2, 4 | N/A
 | 16 | 3, 4 | 3, 4 | 2, 4 | 2, 4 | 1, 4 | N/A
 | 32 | 3, 4 | 2, 4 | 2, 4 | 1, 4 | 1, 4 | N/A
 | 64 | 2, 4 | 2, 4 | 1, 4 | 1, 4 | 0, 4 | 0, 4
 | 128 | N/A | N/A | N/A | N/A | 0, 4 | 0, 4

## Slide 5: Experimental results
Method 1
Method 2
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.10% | 0.00% | 102% | 102%
Class A2 | 0.02% | -0.01% | 0.00% | 103% | 102%
Class B | -0.01% | 0.07% | -0.07% | 100% | 101%
Class C | -0.04% | 0.06% | -0.03% | 97% | 98%
Class E |  |  |  |  | 
Overall | -0.01% | 0.02% | -0.03% | 100% | 100%
Class D | -0.07% | -0.07% | -0.10% | 96% | 93%
Class F | -0.02% | -0.04% | -0.01% | 98% | 99%
RA
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.07% | -0.44% | 99% | 99%
Class C | -0.07% | -0.03% | 0.01% | 99% | 101%
Class E | 0.02% | 0.37% | 0.35% | 99% | 101%
Overall | -0.02% | 0.05% | -0.09% | 99% | 100%
Class D | -0.10% | 0.64% | -0.03% | 99% | 98%
Class F | 0.01% | -0.15% | 1.15% | 99% | 101%
LD
RA
LD
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.07% | 0.00% | 100% | 102%
Class A2 | 0.00% | 0.04% | 0.03% | 101% | 102%
Class B | -0.01% | 0.07% | 0.01% | 100% | 101%
Class C | -0.04% | -0.03% | -0.01% | 99% | 100%
Class E |  |  |  |  | 
Overall | -0.02% | 0.01% | 0.01% | 100% | 101%
Class D | -0.06% | -0.09% | 0.00% | 100% | 102%
Class F | -0.03% | -0.03% | -0.01% | 100% | 101%
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.03% | -0.24% | 102% | 100%
Class C | -0.07% | -0.05% | -0.12% | 100% | 101%
Class E | -0.01% | -0.07% | -0.13% | 101% | 101%
Overall | -0.03% | -0.02% | -0.17% | 101% | 101%
Class D | -0.07% | -0.08% | 0.55% | 101% | 99%
Class F | -0.08% | 0.39% | 0.69% | 101% | 99%

## Slide 6: Conclusion
To remove sharing context modeling for inter_pred_idc syntax, two methods are proposed without changes a number of context model
  Test 1:
    RA: -0.01%, LD: -0.02%
  Test 2:
    RA: -0.02%, LD: -0.03%
It is recommended to adopt the next draft
Thanks Tencent for cross-checking