## Slide 1: AHG16/Non-CE5: On ALF boundary padding
Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2: Boundary padding for ALF in VVC draft 6
            1. Repetitive padding: Picture boundary, 360 boundaries not on CTU boundaries
            2. Mirrored padding: sub-picture/slice/tile/brick boundaries, 360 boundaries on CTU boundaries, virtual boundary for ALF line buffer reduction
            Unifications:
apply mirrored padding to 360 virtual boundaries and picture boundaries
apply repetitive padding for all boundaries excluding virtual boundaries for ALF line buffer reduction
apply repetitive padding for all boundaries

## Slide 3: Mirrored padding at picture boundaries
Anchor: VTM6.0
Test: VTM6.0 + applying mirrored padding at picture
boundaries
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.02% | 0.02% | 123% | 183%
Class A2 | 0.00% | 0.01% | 0.01% | 124% | 169%
Class B | 0.00% | 0.00% | -0.01% | 101% | 133%
Class C | 0.00% | 0.00% | 0.00% | 101% | 123%
Class E | 0.00% | 0.01% | 0.01% | 100% | 138%
Overall | 0.00% | 0.01% | 0.01% | 108% | 144%
Class D | 0.00% | 0.02% | 0.02% | 100% | 121%
Class F | 0.00% | 0.01% | 0.00% | 102% | 132%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | 0.01% | 0.03% | 128% | 186%
Class A2 | 0.01% | 0.07% | 0.01% | 128% | 178%
Class B | -0.01% | 0.08% | 0.05% | 101% | 141%
Class C | 0.00% | 0.06% | 0.00% | 100% | 133%
Class E |  |  |  |  | 
Overall | -0.01% | 0.06% | 0.03% | 110% | 154%
Class D | -0.02% | 0.09% | 0.03% | 98% | 126%
Class F | -0.03% | 0.01% | 0.02% | 101% | 126%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.06% | -0.41% | 100% | 146%
Class C | -0.03% | 0.03% | -0.03% | 101% | 138%
Class E | 0.00% | 0.63% | 0.12% | 100% | 132%
Overall | -0.01% | 0.14% | -0.15% | 100% | 140%
Class D | -0.01% | -0.07% | 0.49% | 101% | 133%
Class F | 0.02% | 0.02% | 1.09% | 102% | 139%

## Slide 4: Disabling loop filter at slice boundaries
Anchor: VTM6.0 + 4 slices in a picture
Test: VTM6.0 + 4 slices in a picture
+ disable loop filter at slice boundaries
+ applying mirrored padding at slice boundaries
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.08% | 0.08% | 101% | 143%
Class A2 | 0.04% | 0.04% | 0.04% | 101% | 137%
Class B | 0.03% | 0.07% | 0.07% | 101% | 135%
Class C | 0.05% | 0.08% | 0.11% | 100% | 124%
Class E | 0.05% | 0.13% | 0.14% | 100% | 143%
Overall | 0.04% | 0.08% | 0.09% | 101% | 135%
Class D | 0.06% | 0.17% | 0.23% | 100% | 120%
Class F | 0.03% | 0.07% | 0.08% | 101% | 126%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.09% | 0.03% | 101% | 148%
Class A2 | 0.05% | 0.07% | 0.09% | 101% | 143%
Class B | 0.04% | 0.01% | 0.17% | 100% | 137%
Class C | 0.07% | 0.14% | 0.05% | 100% | 131%
Class E |  |  |  |  | 
Overall | 0.04% | 0.07% | 0.10% | 100% | 138%
Class D | 0.05% | 0.03% | 0.06% | 100% | 124%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class C | 0.02% | 0.01% | 0.09% | 101% | 136%
Class E | 0.00% | 0.21% | 0.05% | 102% | 134%
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class D | 0.00% | 0.27% | -0.01% | 101% | 131%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 5: Repetitive padding at slice boundaries
Anchor: VTM6.0 + 4 slices in a picture
+ disable loop filter at slice boundaries
+ applying mirrored padding at slice boundaries
Test: VTM6.0 + 4 slices in a picture
+ disable loop filter at slice boundaries
+ applying repetitive padding at slice boundaries
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.05% | 0.05% | 100% | 69%
Class A2 | 0.02% | 0.02% | 0.02% | 100% | 73%
Class B | 0.02% | 0.03% | 0.04% | 100% | 76%
Class C | 0.02% | 0.07% | 0.09% | 101% | 81%
Class E | 0.04% | 0.04% | 0.03% | 101% | 71%
Overall | 0.02% | 0.04% | 0.05% | 100% | 75%
Class D | 0.04% | 0.09% | 0.12% | 101% | 88%
Class F | 0.01% | 0.04% | 0.03% | 101% | 89%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.04% | 0.07% | 99% | 67%
Class A2 | 0.00% | -0.03% | 0.04% | 99% | 70%
Class B | 0.01% | 0.04% | 0.00% | 100% | 73%
Class C | -0.01% | -0.02% | -0.06% | 100% | 77%
Class E |  |  |  |  | 
Overall | 0.00% | -0.01% | 0.01% | 100% | 72%
Class D | 0.02% | 0.14% | 0.05% | 99% | 78%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.04% | 0.15% | 0.18% | 99% | 71%
Class C | 0.05% | 0.22% | 0.21% | 99% | 73%
Class E | 0.07% | -0.16% | -0.03% | 99% | 75%
Overall | 0.05% | 0.10% | 0.14% | 99% | 73%
Class D | -0.01% | -0.48% | 0.37% | 100% | 78%
Class F | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!