## Slide 1: AHG18: on low level coding tool for lossless coding. (JVET-P0576)
Hyeongmun Jang

## Slide 2: Proposed
Proposed way for lossless coding for VVC.
  A flag(same as in HEVC) at CU level is transmitted to indicate whether lossless coded
Proposed constraint syntax signaling for lossless
  Disabling transform related coding tools and syntax signaling; MTS, LFNST, SBT and transform skip for lossless coded block. (same policy of HEVC)
  Disabling JointCbCr and the syntax signaling for lossless coded block
  Disabling LMCS in slice level and the syntax signaling
  Disabling sign data hiding for transform/quantization bypass block (same policy of HEVC)
Proposed decoding behavior to support lossless coding at CU level
  Bypass ALF processing for lossless coded block(same policy of HEVC).
  Support residual coding for Size MxN(M= 64 or N = 64) when MaxTbSize of 64 is signaled in SPS.
    Implicit TU tiling to 32 for lossless block
    Extend coefficient scanning
Notes:   The motivation of this contribution is here.

## Slide 3: Proposed decoding behavior
Bypass ALF processing for lossless coded block
  Case for sps_alf_enabled_flag is transmitted as 1 and lossless is allowed in CU level,
  ALF should be bypass with same policy of HEVC’s in-loop filter behavior for lossless
Subcluase 8.9.5.2 Coding tree block filtering process for luma samples The modified filtered reconstructed luma picture sample alfPictureL[ xCtb + x ][ yCtb + y ] is derived as follows: If pcm_loop_filter_disabled_flag and pcm_flag[ xCtb+ x ][ yCtb + y ] are both equal to 1, the following applies: alfPictureL[ xCtb + x ][ yCtb + y ] = recPictureL[ hx, vy ] (8‑1207) Othersiwe if cu_transquant_bypass_flag[ xCtb+ x ][ yCtb + y ] is equal to 1, the following applies: alfPictureL[ xCtb + x ][ yCtb + y ] = recPictureL[ hx, vy ] (8‑1207) … Subclause 8.8.5.4 Coding tree block filtering process for chroma samples The modified filtered reconstructed chroma picture sample alfPicture[ xCtbC + x ][ yCtbC + y ] is derived as follows: If pcm_loop_filter_disabled_flag and pcm_flag[ ( xCtbC + x ) * SubWidthC ][ ( yCtbC + y ) * SubHeightC ] are both equal to 1, the following applies: alfPicture[ xCtbC + x ][ yCtbC + y ] = recPicturec[ hx, vy ] (8‑1259) Otherwise, if cu_transquant_bypass_flag[ ( xCtbC + x ) * SubWidthC ][ ( yCtbC + y ) * SubHeightC ] is equal to 1, the following applies: alfPicture[ xCtbC + x ][ yCtbC + y ] = recPicturec[ hx, vy ] (8‑1259) …
Notes:   The motivation of this contribution is here.

## Slide 4: Proposed decoding behavior
Implicit TU tiling to prevent coefficient loss by zero-out at large CU
  Even if sps_max_luma_transform_size_64_flag is signaled as 1, lossless should be supported.
  But now, Coefficient Zero-out cause coefficient loss at large CU (64xN, Mx64)
  To support lossless coding for large CU. Implicit TU tiling is allowed to 32x32.
  Implicit TU tiling is already in VVC and it also support to 32x32.
transform_tree( x0, y0, tbWidth, tbHeight , treeType, chType ) { | Descriptor
InferTuCbfLuma = 1 | 
if( IntraSubPartitionsSplitType = = ISP_NO_SPLIT && !cu_sbt_flag ) { | 
if( tbWidth > implicitTuTileSize ¦ ¦ tbHeight > implicitTuTileSize) { | 
verSplitFirst = ( tbWidth > implicitTuTileSize && tbWidth > tbHeight ) ? 1 : 0 | 
trafoWidth = verSplitFirst ? (tbWidth / 2) : tbWidth | 
trafoHeight = !verSplitFirst ? (tbHeight / 2) : tbHeight | 
transform_tree( x0, y0, trafoWidth, trafoHeight, chType ) | 
if( verSplitFirst ) | 
transform_tree( x0 + trafoWidth, y0, trafoWidth, trafoHeight, treeType, chType ) | 
Else | 
transform_tree( x0, y0 + trafoHeight, trafoWidth, trafoHeight, treeType, chType ) | 
} else { | 
transform_unit( x0, y0, tbWidth, tbHeight, treeType, 0, chType ) | 
} | 
} | 
The variable of implicitTuTileSize is derive as follows:
mplicitTuTileSize = cu_transquant_bypass_flag[ x0 ][ y0 ] ? 32 : MaxTbSizeY
Notes:   The motivation of this contribution is here.

## Slide 5: Proposed decoding behavior
Intra prediction syntax signaling related implicit TU tiling for lossless CU
  Original design of IPS do not support implicit TU tiling. Hence, The ISP prediction should be allowed depend on allowed TU size for lossless
  Conceptually, MIP can support implicit TU tiling without any decoding process change. Hence in prediction level, up to 64x64 size can be allowed and the implicit TU tiling is applied for the lossless residual coding.
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) { | Descriptor
… | 
if ( sps_isp_enabled_flag && intra_luma_ref_idx[ x0 ][ y0 ] = = 0 && ( cbWidth <= implicitTuTileSize && cbHeight <= implicitTuTileSize) && ( cbWidth * cbHeight > MinTbSizeY * MinTbSizeY ) ) | 
intra_subpartitions_mode_flag[ x0 ][ y0 ] | ae(v)
if( intra_subpartitions_mode_flag[ x0 ][ y0 ] = = 1 ) | 
intra_subpartitions_split_flag[ x0 ][ y0 ] | ae(v)
} | 
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) { | Descriptor
… | 
if( sps_mip_enabled_flag && ( Abs( Log2( cbWidth ) − Log2( cbHeight ) ) <= 2 ) && cbWidth <= 64 && cbHeight <= 64 ) | 
intra_mip_flag[ x0 ][ y0 ] | ae(v)
} | 
Notes:   The motivation of this contribution is here.

## Slide 6: Proposed decoding behavior
Alternatively, Simply coefficient scanning extension can be considered to prevent coefficient loss at large TU(64xN, Mx64) for lossless coded block.
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) { | Descriptor
if( ( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbWidth > 4 ) | 
log2ZoTbWidth = 4 | 
Else | 
log2ZoTbWidth = Min( log2TbWidth, 5 + cu_transquant_bypass_flag[x0][y0]) | 
MaxCcbs = 2 * ( 1 << log2TbWidth ) * ( 1<< log2TbHeight ) | 
if( tu_mts_idx[ x0 ][ y0 ] > 0 ¦ ¦ ( cu_sbt_flag && log2TbWidth < 6 && log2TbHeight < 6 ) ) && cIdx = = 0 && log2TbHeight > 4 ) | 
log2ZoTbHeight = 4 | 
Else | 
log2ZoTbHeight = Min( log2TbHeight, 5 + cu_transquant_bypass_flag[x0][y0]) | 
Notes:   The motivation of this contribution is here.

## Slide 7: Test result for proposed method
 | All Intra |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM6 | 0 |  | VTM6 | 0 | 
Class A1 | 2.2 | 2.2 | -0.01% | 2.3 | 2.3 | 0.31%
Class A2 | 1.7 | 1.7 | 0.00% | 1.9 | 1.9 | 0.11%
Class B | 2.1 | 2.1 | -0.01% | 2.3 | 2.3 | 0.04%
Class C | 2.1 | 2.1 | 0.00% | 2.6 | 2.6 | 0.02%
Class D | 1.9 | 1.9 | -0.01% | 2.8 | 2.8 | 0.00%
Class E | 2.9 | 2.9 | 0.00% |  |  | 
Class F | 5.5 | 5.5 | -0.01% | 39.4 | 39.4 | 0.10%
TGM | 0.0 | 0.0 | 0.00% | 0.0 | 0.0 | 0.00%
Overall | 2.2 | 2.2 | 0.00% | 2.3 | 2.3 | 0.10%
Enc Time[%] | 40% |  |  | 54% |  | 
Dec Time[%] | 72% |  |  | 75% |  | 
Lossless VVC coding including below aspect and RDO process for LFNST/MTS is disabled in encoder side.
  Disabling transform related coding tools and syntax signaling; MTS, LFNST, SBT and transform skip for lossless coded block.
  Disabling JointCbCr and the syntax signaling for lossless coded block
  Disabling LMCS in slice level and the syntax signaling
  Disabling sign data hiding for transform/quantization bypass block.
Notes:   The motivation of this contribution is here.

## Slide 8: Test result for proposed method
Lossless VVC coding include below aspect and RDO process for LFNST/MTS is disabled in encoder side.
  Disabling transform related coding tools and syntax signaling; MTS, LFNST, SBT and transform skip for lossless coded block.
  Disabling JointCbCr and the syntax signaling for lossless coded block
  Disabling LMCS in slice level and the syntax signaling
  Disabling sign data hiding for transform/quantization bypass block.
  Implicit TU tiling to 32x32 for lossless CU with sps_max_luma_transform_size_64_flag(1)
 | All Intra |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM6 | 0 |  | VTM6 | 0 | 
Class A1 | 2.2 | 2.2 | -0.01% | 2.3 | 2.3 | 0.31%
Class A2 | 1.7 | 1.7 | 0.00% | 1.9 | 1.9 | 0.11%
Class B | 2.1 | 2.1 | -0.01% | 2.3 | 2.3 | 0.04%
Class C | 2.1 | 2.1 | 0.00% | 2.6 | 2.6 | 0.02%
Class D | 1.9 | 1.9 | -0.01% | 2.8 | 2.8 | 0.00%
Class E | 2.9 | 2.9 | 0.00% |  |  | 
Class F | 5.5 | 5.5 | -0.01% | 39.4 | 39.4 | 0.10%
TGM | 0.0 | 0.0 | 0.00% | 0.0 | 0.0 | 0.00%
Overall | 2.2 | 2.2 | 0.00% | 2.3 | 2.3 | 0.10%
Enc Time[%] | 40% |  |  | 55% |  | 
Dec Time[%] | 72% |  |  | 75% |  | 
Notes:   The motivation of this contribution is here.

## Slide 9: Test result for proposed method
 | All Intra |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM6 | 0 |  | VTM6 | 0 | 
Class A1 | 2.2 | 2.2 | -0.01% | 2.3 | 2.3 | 0.31%
Class A2 | 1.7 | 1.7 | 0.00% | 1.9 | 1.9 | 0.11%
Class B | 2.1 | 2.1 | -0.01% | 2.3 | 2.3 | 0.04%
Class C | 2.1 | 2.1 | 0.00% | 2.6 | 2.6 | 0.02%
Class D | 1.9 | 1.9 | -0.01% | 2.8 | 2.8 | 0.00%
Class E | 2.9 | 2.9 | 0.00% |  |  | 
Class F | 5.5 | 5.5 | -0.01% | 39.4 | 39.4 | 0.10%
TGM | 0.0 | 0.0 | 0.00% | 0.0 | 0.0 | 0.00%
Overall | 2.2 | 2.2 | 0.00% | 2.3 | 2.3 | 0.10%
Enc Time[%] | 40% |  |  | 54% |  | 
Dec Time[%] | 72% |  |  | 75% |  | 
Lossless VVC coding include below aspect and RDO process for LFNST/MTS is disabled in encoder side.
  Disabling transform related coding tools and syntax signaling; MTS, LFNST, SBT and transform skip for lossless coded block.
  Disabling JointCbCr and the syntax signaling for lossless coded block
  Disabling LMCS in slice level and the syntax signaling
  Disabling sign data hiding for transform/quantization bypass block.
  Locally bypass ALF process for lossless CU
Notes:   The motivation of this contribution is here.

## Slide 10: Additional test result
To prevent coefficient loss at large TU for lossless. It is test that coefficient scanning is extended up to 64x64.
 | All Intra |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM6 | 0 |  | VTM6 | 0 | 
Class A1 | 2.2 | 2.2 | -0.05% | 2.3 | 2.3 | -0.01%
Class A2 | 1.7 | 1.7 | 0.00% | 1.9 | 1.9 | -0.24%
Class B | 2.1 | 2.1 | 0.00% | 2.3 | 2.3 | -0.01%
Class C | 2.1 | 2.1 | 0.00% | 2.6 | 2.6 | 0.00%
Class D | 1.9 | 1.9 | 0.00% | 2.8 | 2.8 | 0.00%
Class E | 2.9 | 2.9 | 0.00% |  |  | 
Class F | 5.5 | 5.5 | 0.04% | 39.4 | 39.4 | 0.02%
TGM | 0.0 | 0.0 | -0.01% | 0.0 | 0.0 | -0.12%
Overall | 2.2 | 2.2 | -0.05% | 2.3 | 2.3 | -0.05%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 
Notes:   The motivation of this contribution is here.

## Slide 11: Additional rest result
Support implicit TU tiling for MIP for CTC.
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.03% | 0.00% | 89% | 97%
Class A2 | 0.00% | -0.08% | -0.02% | 91% | 91%
Class B | 0.00% | 0.02% | 0.04% | 80% | 88%
Class C | 0.00% | 0.01% | 0.00% | 95% | 87%
Class E | -0.05% | -0.02% | -0.16% | 108% | 84%
Overall | -0.02% | 0.00% | -0.02% | 91% | 89%
Class D | 0.00% | 0.00% | -0.01% | 82% | 86%
Class F | 0.02% | -0.02% | -0.06% | 93% | 84%
 | Random access Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | -0.20% | -0.33% | 101% | 88%
Class A2 | 0.00% | -0.10% | -0.03% | 102% | 96%
Class B | -0.01% | -0.12% | 0.00% | 95% | 87%
Class C | -0.02% | -0.06% | -0.01% | 102% | 89%
Class E |  |  |  |  | 
Overall | -0.03% | -0.11% | -0.08% | 99% | 90%
Class D | 0.00% | -0.07% | 0.01% | 101% | 94%
Class F | 0.02% | 0.13% | -0.06% | 104% | 94%
Notes:   The motivation of this contribution is here.

## Slide 12: Conclusion
It is proposed to adopt that cu_transquant_bypass_flag is transmitted to indicate whether lossless.
It is also proposed to adopt restriction the low-level coding tool with minor impact on current VVC design.