## Slide 1: JVET-P0634 CE6-related: Removal of LFNST for 4x4, 4xN and Nx4 blocks
Hilmi E. Egilmez, Ted Hsieh, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
LFNST consist of 16x16 and 16x48 transform shapes
16x16 non-separable: 4x4, Nx4 and 4xN
16x48 non-separable: larger sizes
4x4
N x 4
4 x N

## Slide 3: Issues
Transform process with LFNST has 2-stages
  latency
Latency critical for small blocks
4x4 TU is the worst-case in terms of latency
Latency for 4xN and Nx4 are worse compared to larger blocks (8x8, Nx8, 8xN)
4x4

## Slide 4: Propose: Remove LFNST for 4x4, 4xN and Nx4
Reduce latency for critical cases
  Small blocks
Memory reduction: 8KB  6KB
  No need for 16x16 matrices
  Only one transform shape (16x48) is supported
Coding efficiency: good trade-off
  0.16% AI loss with 10% encoder speed-up
  No luma loss on UHD sequences
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.41% | 0.39% | 91% | 100%
Class A2 | -0.01% | 0.99% | 1.22% | 90% | 101%
Class B | 0.13% | 0.98% | 0.93% | 89% | 101%
Class C | 0.36% | 0.91% | 1.33% | 89% | 103%
Class E | 0.28% | 0.43% | 0.40% | 91% | 101%
Overall | 0.16% | 0.78% | 0.89% | 90% | 101%
Class D | 0.34% | 1.20% | 1.35% | 85% | 98%
Class F | 0.31% | 0.61% | 0.86% | 92% | 99%
 | Random Access |  |  | 
Over VTM-6.0 |  |  |  | 
Y | U | V | EncT | DecT
0.02% | 0.52% | 0.29% | 99% | 100%
0.07% | 0.57% | 0.63% | 100% | 101%
0.07% | 1.07% | 1.09% | 98% | 100%
0.21% | 0.54% | 0.67% | 100% | 103%
0.10% | 0.72% | 0.72% | 99% | 101%
0.12% | 0.57% | 0.93% | 97% | 99%
0.16% | 0.27% | 0.45% | 98% | 99%

## Slide 5: Recommendation
To adopt the proposed simplification
Cross-checker: Santiago De-Luxán-Hernández (HHI)