## Slide 1: JVET-Q0167 Non-CE5: Multiplication simplification for ALF and CC-ALF
Jacob Ström, Zhi Zhang, Kenneth Andersson
Ericsson Research

## Slide 2: Background: Adaptive loop filtering (ALF)
ALF Classifies samples into 25 possible classes, and each can have a unique filter.
Most often these filters are merged, which is a form of quantization.
ALF filter support for luma

## Slide 3: Filter formula in VVC-ALF
The filter is formulated as the weighted differences to the center sample
signaled coefficient
difference value

## Slide 4: Filter formula in ALF
The filter is formulated as the weighted differences to the center sample
signaled coefficient
second difference value

## Slide 5: Full ALF equation (in VTM)

## Slide 6: Problem that we attack
In total there are 12 multiplications per sample.
Multiplications are expensive in hardware: (In software they are cheap.)

## Slide 7: Inspiration
In Geneva, Qualcomm described a simplification of CC-ALF where the multiplications were replaced by shifts. This can be tried also for ALF:

## Slide 8: Inspiration
In Geneva, Qualcomm described a simplification of CC-ALF where the multiplications were replaced by shifts. This can be tried also for ALF:

## Slide 9: Inspiration
In Geneva, Qualcomm described a simplification of CC-ALF where the multiplications were replaced by shifts. This can be tried also for ALF:

## Slide 10: Inspiration
In Geneva, Qualcomm described a simplification of CC-ALF where the multiplications were replaced by shifts. This can be tried also for ALF:

## Slide 11: Inspiration
In Geneva, Qualcomm described a simplification of CC-ALF where the multiplications were replaced by shifts. This can be tried also for ALF:
is replaced by
shift

## Slide 12: Implementation of pure power of two multiplication
<<
output
Possible outputs:

## Slide 13: Implementation of pure power of two multiplication
Possible outputs:
output
conditional negate
= sign of
<<

## Slide 14: Implementation of pure power of two multiplication
Possible outputs:
output
conditional negate
= sign of
conditional zero out
=
<<

## Slide 15: Implementation of pure power of two multiplication
Possible outputs:
output
conditional negate
= sign of
conditional zero out
=
cheap
cheap
cheap
<<

## Slide 16: However, BDR figures are not good.
BDR loss for Random Access is about 0.2%
Some sequences get BDR penalties of more than 0.4%

## Slide 17: Idea
Pure power of two coefficients too restrictive
Our idea is to allow more coefficients but still have low complexity hardware.

## Slide 18: Idea
Pure power of two coefficients too restrictive
Our idea is to allow more coefficients but still have low complexity hardware.
The best way to cut the distortion in the coefficients is to also have another allowed value between every allowed value
This happens if we includes not only but also .

## Slide 19: Idea
Pure power of two coefficients too restrictive
Our idea is to allow more coefficients but still have low complexity hardware.
The best way to cut the distortion in the coefficients is to also have another allowed value between every allowed value
This happens if we includes not only but also .
The next step to cut distances in half is to include also .

## Slide 20: Multiplication by 3 is very cheap
We can write as

## Slide 21: Multiplication by 3 is very cheap
We can write as
  And that is the same as

## Slide 22: Multiplication by 3 is very cheap
We can write as
  And that is the same as
0
input bits
output bits
is extremely cheap in hardware – no cost!

## Slide 23: Multiplication by 3 is very cheap
We can write as
  And that is the same as
0
input bits
output bits
is extremely cheap in hardware – no cost!

## Slide 24: Multiplication by 3 is very cheap
Possible outputs:

## Slide 25: Multiplication by 3 is very cheap
shift s0 steps
Possible outputs:

## Slide 26: Multiplication by 3 is very cheap
condi- tional zero out
shift s0 steps
Possible outputs:

## Slide 27: Multiplication by 3 is very cheap
condi- tional zero out
shift s0 steps
condi- tional zero out
Possible outputs:

## Slide 28: Multiplication by 3 is very cheap
Possible outputs:
condi- tional zero out
shift s0 steps
condi- tional zero out
condi- tional negate

## Slide 29: Multiplication by 3 or 5 is also very cheap
Possible outputs:
condi- tional zero out
shift s0 steps
condi- tional zero out
condi- tional negate

## Slide 30: Coding of coefficients
We only allow coefficients up to . (Larger coefficients are exceedingly rare.)
  Test 1:
  Test 2:
Simpler truncated binary coding can be used for the magnitude instead of Exponential Golomb 3 coding.
magnitude | index | index bits | sign bit | number of bits
0 | 0 | 000 |  | 3
1 | 1 | 001 | 0/1 | 4
2 | 2 | 010 | 0/1 | 4
3 | 3 | 0110 | 0/1 | 5
4 | 4 | 0111 | 0/1 | 5
6 | 5 | 1000 | 0/1 | 5
8 | 6 | 1001 | 0/1 | 5
12 | 7 | 1010 | 0/1 | 5
16 | 8 | 1011 | 0/1 | 5
24 | 9 | 1100 | 0/1 | 5
32 | 10 | 1101 | 0/1 | 5
48 | 11 | 1110 | 0/1 | 5
64 | 12 | 1111 | 0/1 | 5
magnitude | index | index bits | sign bit | number of bits
0 | 0 | 0000 |  | 4
1 | 1 | 0001 | 0/1 | 5
2 | 2 | 0010 | 0/1 | 5
3 | 3 | 0011 | 0/1 | 5
4 | 4 | 0100 | 0/1 | 5
5 | 5 | 0101 | 0/1 | 5
6 | 6 | 0110 | 0/1 | 5
8 | 7 | 0111 | 0/1 | 5
10 | 8 | 1000 | 0/1 | 5
12 | 9 | 1001 | 0/1 | 5
16 | 10 | 1010 | 0/1 | 5
20 | 11 | 1011 | 0/1 | 5
24 | 12 | 1100 | 0/1 | 5
32 | 13 | 1101 | 0/1 | 5
40 | 14 | 1110 | 0/1 | 5
48 | 15 | 11110 | 0/1 | 6
64 | 16 | 11111 | 0/1 | 6
Test 1
Test 2

## Slide 31: Specification changes (test 2)
Replacing Exponential-Golomb code 3 with truncated binary coding (and the same for chroma):
The decoding of the magnitude changes the following part of the specification text:
The variable filtCoeff[ sfIdx ][ j ] with sfIdx = 0..alf_luma_num_filters_signalled_minus1, j = 0..11 is initialized as follows:
filtCoeff[ sfIdx ][ j ] = AlfApsCoeffMap[ alf_luma_coeff_abs_idx[ sfIdx ][ j ] ] * (90) ( 1 − 2 * alf_luma_coeff_sign[ sfIdx ][ j ] )
AlfApsCoeffMap = { 0, 1, 2, 3, 4, 5, 6, 8, 10, 12, 16, 20, 24, 32, 40, 48, 64 }
for( sfIdx = 0; sfIdx <= alf_luma_num_filters_signalled_minus1; sfIdx++ ) { | 
for( j = 0; j < 12; j++ ) { | 
alf_luma_coeff_abs_idx[ sfIdx ][ j ] | uek(v) tb(v)
if( alf_luma_coeff_abs_idx[ sfIdx ][ j ] ) | 
alf_luma_coeff_sign[ sfIdx ][ j ] | u(1)
} | 
} | 

## Slide 32: Quantizing also the fixed filter table (test 2):
AlfFixFiltCoeff = (92)
{ { 0, 0, 2, −3, 1, −4, 1, 7, −1, 1, −1, 5}
{ 0, 0, 2, −3, 1, −4, 1, 6, −1, 1, −1, 5}
{ 0, 0, 0, 0, 0, −1, 0, 1, 0, 0, −1, 2}
{ 0, 0, 0, 0, 0, 0, 0, 1, 0, 0, 0, 0}
{ 0, 0, 0, 0, 0, 0, 0, 0, 0, 0, −1, 1}
{ 2, 2, −7, −3, 0, −5, 13, 22, 12, −3, −3, 17}
{ 2, 2, -6, -3, 0, -5, 12, 20, 12, -3, -3, 16}
{−1, 0, 6, −8, 1, −5, 1, 23, 0, 2, −5, 10}
{-1, 0, 6, -8, 1, -5, 1, 24, 0, 2, -5, 10}
{ 0, 0, −1, −1, 0, −1, 2, 1, 0, 0, −1, 4}
{ 0, 0, 3, −11, 1, 0, −1, 35, 5, 2, −9, 9}
{ 0, 0, 3, -10, 1, 0, -1, 32, 5, 2, -8, 8}
. . .
},

## Slide 33: Results
Test 1: Includes pure power of two plus (anchor is VTM-7.0 with unchanged ALF)
  AI: +0.02% (Y) -0.04% (U) -0.03% (V). YUV (8/1/1)= +0.01%
  RA: +0.02% (Y) -0.11% (U) -0.04% (V). YUV (8/1/1) = +0.01%
  LD: 0.00% (Y) -0.29% (U) -0.39% (V). YUV (8/1/1) = -0.07%
Test 2: Includes pure power of two plus and
  AI: 0.00% (Y) -0.05% (U) -0.05% (V). YUV (8/1/1)= -0.01%
  RA: 0.00% (Y) -0.12% (U) -0.06% (V). YUV (8/1/1) = -0.01%
  LD: -0.04% (Y) -0.21% (U) -0.28% (V). YUV (8/1/1) = -0.08%

## Slide 34: Why do we get zero BDR penalty?
Coefficients are very close to zero anyway.

## Slide 35: Why do we get zero BDR penalty?
Coefficients are very close to zero anyway.
Over 60% of coefficients are in [-6, 6] where test 2 has the same quantization step as the anchor.

## Slide 36: Why do we get zero BDR penalty?
Coefficients are very close to zero anyway.
Over 60% of coefficients are in [-6, 6] where test 2 has the same quantization step as the anchor.
Over 80% of the coefficients are in [-13, 13] where test 2 has a quantization step at most 2x that of the anchor.

## Slide 37: Why do we get zero BDR penalty?
Coefficients are very close to zero anyway.
Over 60% of coefficients are in [-6, 6] where test 2 has the same quantization step as the anchor.
Over 80% of the coefficients are in [-13, 13] where test 2 has a quantization step just 2x that of the anchor.
Merging two filters is also a form of quantization – one could argue that merging is a much harsher form of quantization.
Since the coefficients are now cheaper, less merging is necessary: 10% and 17% more filter sets are being signaled (test2).

## Slide 38: Combinations with CC-ALF (JVET-Q0165 which is a DC neutral version of CE5-2.1)
Test 3: Includes pure power of two plus in both ALF and CC-ALF. Anchor is CC-ALF anchor
  AI: 0.00% (Y) -0.13% (U) -0.29% (V). YUV (8/1/1)= -0.04%
  RA: 0.02% (Y) -0.34% (U) -0.41% (V). YUV (8/1/1) = -0.06%
  LD: 0.01% (Y) -0.76% (U) -0.87% (V). YUV (8/1/1) = -0.16%
Test 4: Includes pure power of two plus in ALF, only pure power of two in CC-ALF
  AI: -0.01% (Y) -0.04% (U) -0.22% (V). YUV (8/1/1)= -0.03%
  RA: 0.03% (Y) -0.33% (U) -0.35% (V). YUV (8/1/1) = -0.05%
  LD: 0.01% (Y) -0.83% (U) -0.72% (V). YUV (8/1/1) = -0.15%
Test 5: Includes pure power of two plus and in ALF, only pure power of two in CC-ALF
  AI: -0.03% (Y) -0.06% (U) -0.24% (V). YUV (8/1/1)= -0.05%
  RA: -0.01% (Y) -0.34% (U) -0.39% (V). YUV (8/1/1) = -0.08%
  LD: -0.01% (Y) -0.93% (U) -0.92% (V). YUV (8/1/1) = -0.19%

## Slide 39: Proposal: Adopt test 2
We propose restricting the ALF coefficients (luma and chroma) to {0, 1, 2, 3, 4, 5, 6 8, 10, 12, 16, 20, 24, 32, 40, 48, 64} (test2).
Features:
  Simplified multiplications, allowing for significant surface area savings in hardware implementations. Also reduces power consumption.
  No average loss in luma-BDR or chroma-BDR
  Exponential-Golomb-3 coding in HLS replaced by simpler truncated binary coding
Straightforward implementation – compatible with existing low-level processing implementations (new coefficients are a subset of previous coefficients).

## Slide 40: Test 1, All Intra
YUV BDR = 0.01%
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.00% | 0.04% | 100% | 100%
Class A2 | 0.04% | 0.03% | 0.03% | 100% | 99%
Class B | 0.02% | -0.07% | -0.06% | 100% | 100%
Class C | -0.02% | -0.07% | -0.07% | 99% | 100%
Class E | 0.05% | -0.05% | -0.05% | 101% | 98%
Overall | 0.02% | -0.04% | -0.03% | 100% | 100%
Class D | -0.02% | 0.09% | 0.05% | 101% | 102%
Class F | -0.02% | -0.09% | -0.08% | 100% | 99%

## Slide 41: Test 1, Random Access
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.16% | -0.03% | 101% | 101%
Class A2 | 0.05% | -0.01% | 0.01% | 101% | 99%
Class B | 0.04% | -0.06% | -0.06% | 100% | 100%
Class C | 0.00% | -0.20% | -0.06% | 98% | 99%
Class E |  |  |  |  | 
Overall | 0.02% | -0.11% | -0.04% | 100% | 100%
Class D | -0.03% | -0.30% | -0.06% | 98% | 99%
Class F | -0.06% | -0.19% | -0.10% | 98% | 100%
YUV BDR = 0.01%

## Slide 42: Test 1, Low delay B
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03% | -0.53% | -0.24% | 101% | 97%
Class C | -0.03% | -0.34% | -0.60% | 101% | 100%
Class E | -0.01% | 0.17% | -0.38% | 99% | 98%
Overall | 0.00% | -0.29% | -0.39% | 101% | 99%
Class D | -0.13% | 0.31% | 0.11% | 100% | 101%
Class F | -0.13% | -0.48% | -0.18% | 100% | 101%
YUV BDR = -0.07%

## Slide 43: Test 1, Low delay P
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.08% | -0.17% |  | 
Class C | 0.03% | -0.38% | -0.56% |  | 
Class E | -0.03% | -0.24% | -0.32% |  | 
Overall | 0.01% | -0.15% | -0.34% |  | 
Class D | -0.10% | -0.35% | 0.71% |  | 
Class F | -0.02% | -0.37% | 0.29% |  | 
YUV BDR = -0.04%

## Slide 44: Test 2, All Intra
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 102% | 99%
Class A2 | 0.02% | 0.01% | 0.00% | 102% | 97%
Class B | 0.00% | -0.08% | -0.07% | 100% | 100%
Class C | -0.03% | -0.09% | -0.09% | 101% | 101%
Class E | 0.00% | -0.06% | -0.06% | 102% | 101%
Overall | 0.00% | -0.05% | -0.05% | 101% | 100%
Class D | -0.02% | 0.04% | 0.00% | 100% | 100%
Class F | -0.03% | -0.09% | -0.12% | 100% | 101%
YUV BDR = -0.01%

## Slide 45: Test 2, Random Access
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | -0.02% | 98% | 100%
Class A2 | 0.01% | 0.05% | 0.05% | 97% | 100%
Class B | 0.01% | -0.16% | -0.02% | 99% | 100%
Class C | -0.01% | -0.27% | -0.23% | 98% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | -0.12% | -0.06% | 98% | 100%
Class D | -0.05% | -0.32% | -0.09% | 99% | 99%
Class F | -0.01% | -0.06% | -0.09% | 105% | 101%
YUV BDR = -0.01%

## Slide 46: Test 2, Low delay B
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.24% | -0.03% | 101% | 99%
Class C | 0.01% | -0.36% | -0.15% | 100% | 102%
Class E | -0.13% | 0.05% | -0.86% | 100% | 100%
Overall | -0.04% | -0.21% | -0.28% | 100% | 100%
Class D | 0.01% | -0.25% | -0.44% | 100% | 102%
Class F | -0.14% | -0.25% | -0.03% | 99% | 100%
YUV BDR = -0.08%

## Slide 47: Test 2, Low delay P
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | -0.02% |  | 
Class A2 | 0.01% | 0.05% | 0.05% |  | 
Class B | 0.01% | -0.16% | -0.02% |  | 
Class C | -0.01% | -0.27% | -0.23% |  | 
Class E |  |  |  |  | 
Overall | 0.00% | -0.12% | -0.06% |  | 
Class D | -0.05% | -0.32% | -0.09% |  | 
Class F | -0.01% | -0.06% | -0.09% |  | 
YUV BDR = -0.02%

## Slide 48: Test 3 vs CE5 anchor, All Intra
 | Over CE5 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | -0.13% | 101% | 99%
Class A2 | 0.04% | -0.55% | -0.40% | 98% | 101%
Class B | 0.01% | -0.04% | -0.12% | 101% | 100%
Class C | -0.06% | -0.17% | -0.25% | 95% | 102%
Class E | 0.03% | 0.06% | -0.72% | 98% | 97%
Overall | 0.00% | -0.13% | -0.29% | 99% | 100%
Class D | -0.02% | -0.13% | -0.44% | 96% | 101%
Class F | -0.06% | -0.12% | -0.16% | 100% | 100%
YUV BDR = -0.04%

## Slide 49: Test 3 vs CE5 anchor, Random Access
 | Over CE5 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.25% | -0.31% | 99% | 99%
Class A2 | 0.08% | -0.27% | -0.33% | 99% | 99%
Class B | 0.04% | -0.37% | -0.48% | 98% | 100%
Class C | -0.05% | -0.42% | -0.44% | 98% | 101%
Class E |  |  |  |  | 
Overall | 0.02% | -0.34% | -0.41% | 98% | 100%
Class D | -0.06% | -0.55% | -0.50% | 99% | 100%
Class F | -0.05% | -0.31% | -0.34% | 106% | 98%
YUV BDR = -0.06%

## Slide 50: Test 3 vs CE5 anchor, Low delay B
 | Over CE5 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.96% | -0.49% | 100% | 100%
Class C | 0.00% | -0.48% | -0.79% | 103% | 98%
Class E | 0.03% | -0.81% | -1.62% | 100% | 101%
Overall | 0.01% | -0.76% | -0.87% | 101% | 100%
Class D | -0.05% | -1.36% | -0.69% | 97% | 100%
Class F | -0.07% | -0.50% | 0.17% | 103% | 100%
YUV BDR = -0.16%

## Slide 51: Test 4 vs CE5 anchor, All Intra
 | Over CE5 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.03% | -0.05% | 99% | 100%
Class A2 | 0.04% | -0.42% | -0.29% | 97% | 100%
Class B | 0.00% | 0.06% | -0.01% | 98% | 101%
Class C | -0.07% | -0.15% | -0.22% | 91% | 102%
Class E | 0.01% | 0.25% | -0.67% | 91% | 101%
Overall | -0.01% | -0.04% | -0.22% | 95% | 101%
Class D | -0.02% | -0.15% | -0.48% | 93% | 101%
Class F | -0.07% | -0.02% | -0.04% | 99% | 100%
YUV BDR = -0.03%

## Slide 52: Test 4 vs CE5 anchor, Random Access
 | Over CE5 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | -0.26% | -0.27% | 97% | 99%
Class A2 | 0.08% | -0.20% | -0.24% | 99% | 102%
Class B | 0.05% | -0.36% | -0.36% | 97% | 98%
Class C | -0.04% | -0.45% | -0.47% | 98% | 101%
Class E |  |  |  |  | 
Overall | 0.03% | -0.33% | -0.35% | 98% | 100%
Class D | -0.06% | -0.54% | -0.42% | 99% | 101%
Class F | -0.03% | -0.22% | -0.33% | 108% | 101%
YUV BDR = -0.05%

## Slide 53: Test 4 vs CE5 anchor, Low delay B
 | Over CE5 anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.82% | -0.26% | 101% | 100%
Class C | 0.00% | -0.43% | -0.74% | 101% | 99%
Class E | 0.04% | -1.38% | -1.47% | 98% | 99%
Overall | 0.01% | -0.83% | -0.72% | 100% | 100%
Class D | -0.05% | -1.01% | -0.54% | 98% | 101%
Class F | -0.10% | -0.35% | -0.37% | 101% | 101%
YUV BDR = -0.15%

## Slide 54: Test 5 vs CE5 anchor, All Intra
 | Over CE5-anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.04% | -0.07% | 97% | 100%
Class A2 | 0.02% | -0.46% | -0.29% | 98% | 101%
Class B | -0.02% | 0.05% | -0.04% | 99% | 98%
Class C | -0.08% | -0.18% | -0.25% | 95% | 100%
Class E | -0.04% | 0.23% | -0.69% | 96% | 100%
Overall | -0.03% | -0.06% | -0.24% | 97% | 100%
Class D | -0.02% | -0.19% | -0.53% | 96% | 98%
Class F | -0.08% | -0.06% | -0.06% | 98% | 100%
YUV BDR = -0.05%

## Slide 55: Test 5 vs CE5 anchor, Random Access
 | Over CE5-anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.24% | -0.17% | 100% | 99%
Class A2 | 0.01% | -0.23% | -0.31% | 100% | 101%
Class B | 0.00% | -0.35% | -0.52% | 98% | 99%
Class C | -0.03% | -0.50% | -0.46% | 99% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | -0.34% | -0.39% | 99% | 100%
Class D | -0.05% | -0.55% | -0.31% | 99% | 100%
Class F | -0.04% | -0.19% | -0.32% | 107% | 97%
YUV BDR = -0.08%

## Slide 56: Test 5 vs CE5 anchor, Low delay B
 | Over CE5-anchor |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | -0.83% | -0.58% | 98% | 102%
Class C | 0.02% | -0.57% | -0.79% | 99% | 102%
Class E | -0.01% | -1.57% | -1.65% | 99% | 101%
Overall | -0.01% | -0.93% | -0.92% | 99% | 101%
Class D | -0.08% | -1.69% | -1.17% | 98% | 102%
Class F | -0.13% | -0.53% | -0.24% | 102% | 101%
YUV BDR = -0.19%

## Slide 57: Thank you!

## Slide 59: Combination with other standards
In AVS2, there is a form of ALF similar to the one in VVC.
Argument has been made that they have multipliers that can be reused.
However, these multipliers are smaller:
  AVS2: [-64, 63] x [0, 1023]
  VVC: [-127, 127] x [-2046, 2046] need about 140% of the area of a AVS2 multiplier
A multiplier in between can do both AVS2 and our solution:
  AVS2 / JVET-Q0167: [-64, 63] x [-2046, 2046]
  Including special case for a coefficient of +64 we need about 130% of the area of a AVS2 multiplier
Hence:
  Still saves area (from 140% to 130%)
  Also saves power (similar amount)

## Slide 60: Extracting parameters during decoding of coefficients (test 1)
Happens during decoding (max once per CTU):
  n = alf_luma_coeff_sign[ sfIdx ][ j ];
  idx = alf_luma_coeff_abs_idx[ sfIdx ][ j ];
  k_0 = idx & 1
  k_1 = (idx < 2 ? 0 : 1);
  s_1 = s_from_idx[idx >> 1];
where
  s_from_idx[17] = {0 0 1 2 3 4 5};
zero out
neg
zero out

## Slide 61: Extracting parameters during decoding of coefficients (test 2)
Happens during decoding (max once per CTU):
  n = alf_luma_coeff_sign[ sfIdx ][ j ];
  idx = alf_luma_coeff_abs_idx[ sfIdx ][ j ];
  k_0 = (idx < 2 ? idx : 1-thirdtab((idx-2) +1) );
  k_1 = (idx < 3 ? 0 : 1);
  s_0 = (idx < 2 ? 0 : thirdtab((idx-3) + 1) );
  s_1 = s_from_idx[idx];
where
  thirdtab[17] = {0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0};
  s_from_idx[17] = {0 0 1 0 1 0 1 2 1 2 3 2 3 4 3 4 5};
thirdtab = [0 0 1 0 0 1 0 0 1 0 0 1 0 0 1 0 0];
s_from_idx = [0 0 1 0 1 0 1 2 1 2 3 2 3 4 3 4 5];
zero out
neg
zero out

## Slide 62: Worst and best sequences (test2):
AI:
  Worst: Parkrunning +0.06%
  Best: BaskedballDrill -0.09%
RA:
  Worst: Parkrunning +0.05%
  Best: BaskedballPass: -0.15%
LD:
  Worst: RaceHorses (class D): +0.17%
  Best: Johnny: -0.27%