## Slide 1: JVET-Q0297: AHG16: Merge estimation region with constrain in HMVP update
Han Huang, Wei-Jung Chien, Ted Hsieh, Vadim Seregin, Chun-Chi Chen, Kevin Reuzé, Marta Karczewicz (Qualcomm)
Yu-Ling Hsiao, Chun-Chia Chen,Chih-Wei Hsu, Tzu-Der Chuang, Ching-Yeh Chen, Yu-Wen Huang,Shaw-Min Lei (MediaTek)

## Slide 2: Summary of proposal
Merge Estimation Region (MER) as in HEVC.
Encoder side constrain for BT/TT split to enable parallelization.
Normative change to HMVP updating process
  Method 1: Enabled if and only if both cbHeight and cbWidth are larger than or equal to 1 << Log2ParMrgLevel.
  Method 2: Enabled if and only if ( (xCb+cbWidth) >> Log2ParMrgLevel > (xCb >> Log2ParMrgLevel) and ( (yCb+cbHeight) >> Log2ParMrgLevel > (yCb >> Log2ParMrgLevel).

## Slide 3: Results
MER size | Method 1 |  |  |  |  | Method 2 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
128x128 | 4.15% | 4.12% | 4.40% | 112% | 97% | 3.79% | 3.76% | 3.99% | 110% | 97%
64x64 | 2.72% | 2.76% | 2.97% | 107% | 97% | 2.28% | 2.25% | 2.42% | 105% | 98%
32x32 | 2.64% | 2.86% | 3.08% | 70% | 98% | 2.39% | 2.54% | 2.73% | 70% | 99%
16x16 | 2.68% | 3.33% | 3.47% | 62% | 98% | 2.66% | 3.27% | 3.43% | 62% | 99%
8x8 | 1.26% | 1.72% | 1.85% | 79% | 98% | 1.27% | 1.72% | 1.82% | 80% | 98%
Random access Main 10, anchor is VTM-7.0

## Slide 4: Text change summary
A syntax element log2_parallel_merge_level_minus2 is added in PPS to specify the size of MER. The variable Log2ParMrgLevel is set equal to 2 + log2_parallel_merge_level_minus2
A spatial merge candidate (either in regular merge or subblock based merge) that is derived from location (xNb, yNb) is defined as unavailable if the xPb >> Log2ParMrgLevel is equal to xNb >> Log2ParMrgLevel and yPb >> Log2ParMrgLevel is equal to yNb >> Log2ParMrgLevel.
HMVP updating change
  Method 1: The updating process for the history-based motion vector predictor candidate list is enabled if and only if both cbHeight and cbWidth are larger than or equal to 1 << Log2ParMrgLevel.
  Method 2: The updating process for the history-based motion vector predictor candidate list is enabled if and only if ( (xCb+cbWidth) >> Log2ParMrgLevel > (xCb >> Log2ParMrgLevel) and ( (yCb+cbHeight) >> Log2ParMrgLevel > (yCb >> Log2ParMrgLevel).

## Slide 5: Encoder side constrain
R is equal to 1 << Log2ParMrgLevel
If cbWidth > R and cbHeight <= R, then horizontal BT split is disabled for current block.
If cbWidth <= R and cbHeight > R, then vertical BT split is disabled for current block.
If (cbWidth > R || cbHeight > R) and cbHeight <= 2 * R, then horizontal TT split is disabled for current block.
If cbWidth <= 2 * R and (cbWidth > R || cbHeight > R), then vertical TT split is disabled for current block.