## Slide 1: AHG11: picture/slice level deblocking control flag for IBC (JVET-Q0427)
X. Xu, G. Li, X. Li, S. Liu (Tencent)
2020/01

## Slide 2: Summary
Currently in VVC CD text/VTM-7.0, IBC deblocking behaves in a similar way as in inter MC:
  If either side is intra coded, BS=2
  Else, if both sides are IBC coded and
    BV difference <=1, BS=0
    BV difference > 1, BS=1
  Else, if one side is IBC coded and the other is not, BS=1
  Else, … (inter BS decisions)
It was argued that the use of deblocking for IBC is content dependent (good to turn off in some cases)
In this contribution, a picture/slice level flag is proposed to control the use of deblocking for IBC

## Slide 3: Problem statement
The usage of IBC deblocking is content dependent, no universal solution is available
  For some content (such as some natural content), IBC works and deblocking is necessary to smooth out blocking artifacts at the boundary
  For some content (such as screen content, low QP), deblocking may undesirably remove existing sharp edges at the boundary
The benefits of disabling IBC deblocking were previously discussed in JVET-P0611/JVET-M0336, no consensus reached

## Slide 4: Solutions
The suggested change is to add a high level control flag such that the encoder can optionally turned off deblocking filter for IBC, if that can help improve the visual quality
In this contribution, various solutions are proposed based on the above:
  Picture or slice level control flag
  Turn off deblocking for IBC if either or both sides are coded in IBC mode

## Slide 5: Solutions
Solution 1.1: a picture level flag to turn off IBC deblocking filter, turn off deblocking filter when either side of the edge is coded in IBC mode
Solution 1.2: a picture level flag to turn off IBC deblocking filter, turn off deblocking filter when both sides of the edge are coded in IBC mode
Solution 2.1: a slice level flag to turn off IBC deblocking filter, turn off deblocking filter when either side of the edge is coded in IBC mode
Solution 2.2: a slice level flag to turn off IBC deblocking filter, turn off deblocking filter when both sides of the edge are coded in IBC mode

## Slide 6: Conclusion
Deblocking filter behavior for IBC is content dependent
  No easy on/off decisions are available to solve all issues
Solutions are suggested to control the use of deblocking filters for edges containing IBC coded samples via a high level flag
It is argued that by adding such a flag, the encoder can optionally choose to turned off the deblocking filter for IBC when that can help improve visual quality