## Slide 1: JVET-R0083 AHG 14: Residual coding constraints for transform skip blocks
Alican Nalci, Hilmi Enes Egilmez, Muhammed Coban,
Vadim Seregin and Marta Karczewicz
  Qualcomm Inc.
Date: 04/09/2020
Teleconference

## Slide 2
Coefficient coding options for VTM-7.0:
In 17th JVET meeting, a slice level flag (slice_ts_residual_coding_disabled_flag) was adopted into VVC.
  Transform skip (TS) blocks can use transform or regular residual coding (RRC) in VTM-8.0.
Bugs: Ticket #981[SW], #859 [Spec] related to dependent quantization (DQ) and sign data hiding (SDH).
As discussed in these tickets, DQ and SDH can introduce undesired behavior for TS blocks:
  Encoder/decoder mismatch issues and encoder crashes when SDH is enabled (#981).
  Inconsistency: Though dequantization part of DQ is disabled in SW, context part is not disabled (#859).
  Coding losses for both lossy/lossless cases with DQ and SDH (several proposals).
  DQ and SDH are inherently lossy operations (issues for lossless coding).
Introduction
TS Flag = 1
VTM-7.0
Transform Skip
Residual Coding
Dependent Quantization (on spec), Sign Hiding, etc.
Uses RDOQTS
TS Flag = 0
Transform
Residual Coding
X
VTM-8.0

## Slide 3
In this proposal, 4 variants are discussed:
  Variant 1 : Both DQ and SDH are disabled for TS blocks (e.g. when TS flag is 1).
  Variants 2, 3 : DQ and SDH can be disabled for TS blocks independently.
  Variant 4 : Spec is aligned to VVC software, dequantization part of DQ is disabled in spec.
  Additionally: Encoder fixes for RDOQ is proposed
    This fixes currently broken encoder when TS blocks use RRC.
Summary of proposed variants:
7.3.10.11 Residual coding syntax
residual_coding( x0, y0, log2TbWidth, log2TbHeight, cIdx ) { | Descriptor
… | 
if( ph_dep_quant_enabled_flag && !transform_skip_flag[ x0 ][ y0 ][ cIdx ] ) | 
QState = QStateTransTable[ QState ][ AbsLevelPass1[ xC ][ yC ] & 1 ] | 
… | 
for( n = firstPosMode1; n >= 0; n− − ) { | 
xC = ( xS << log2SbW ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 0 ] | 
yC = ( yS << log2SbH ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 1 ] | 
… | 
if( ph_dep_quant_enabled_flag && !transform_skip_flag[ x0 ][ y0 ][ cIdx ] ) | 
QState = QStateTransTable[ QState ][ AbsLevel[ xC ][ yC ] & 1 ] | 
} | 
if(ph_dep_quant_enabled_flag ¦ ¦ !pic_sign_data_hiding_enabled_flag ¦ ¦ transform_skip_flag[ x0 ][ y0 ][ cIdx ] ) | 
signHidden = 0 | 
… | 
if( ph_dep_quant_enabled_flag && !transform_skip_flag[ x0 ][ y0 ][ cIdx ] ) { | 
QState = startQStateSb | 
for( n = numSbCoeff − 1; n >= 0; n− − ) { | 
… | 
QState = QStateTransTable[ QState ][ AbsLevel[ xC ][ yC ] & 1 ] | 
} else { | 
… | 
Variant 1 suggested Spec changes:
Yellow part is for disabling DQ.
Green part is for disabling SDH.

## Slide 4: Lossy Results
 | All Intra Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | 0.01% | 0.17% | 100% | 102%
Class A2 | 0.01% | -0.11% | -0.03% | 98% | 95%
Class B | -0.02% | -0.02% | 0.01% | 99% | 94%
Class C | -0.08% | -0.06% | -0.05% | 99% | 94%
Class E | 0.01% | -0.06% | -0.12% | 98% | 93%
Overall | -0.03% | -0.04% | 0.00% | 99% | 95%
Class D | -0.07% | 0.03% | 0.03% | 101% | 99%
Class F | -0.80% | -0.53% | -0.66% | 99% | 98%
Class SCC | -0.86% | -0.90% | -0.85% | 99% | 97%
 | Random access Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.07% | 100% | 100%
Class A2 | -0.02% | 0.12% | -0.14% | 96% | 97%
Class B | -0.01% | -0.05% | -0.11% | 99% | 99%
Class C | -0.10% | 0.03% | -0.06% | 96% | 91%
Class E |  |  |  |  | 
Overall | -0.03% | 0.02% | -0.07% | 98% | 97%
Class D | -0.20% | 0.26% | 0.19% | 99% | 99%
Class F | -0.70% | -0.40% | -0.44% | 99% | 99%
Class SCC | -0.86% | -0.61% | -0.74% | 99% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.01% | -0.30% | 91% | 84%
Class C | -0.16% | -0.24% | 0.23% | 97% | 89%
Class E | 0.08% | -0.19% | 1.03% | 95% | 91%
Overall | -0.04% | -0.13% | 0.21% | 94% | 87%
Class D | -0.29% | 0.24% | 0.49% | 99% | 94%
Class F | -1.02% | -0.28% | -0.24% | 99% | 98%
Class SCC | -1.32% | -0.90% | -1.11% | 94% | 86%
In the lossy results presented below (same for variants #1 and #2):
VTM-8.0 is used as the anchor on top of CTC configurations.
slice_ts_residual_coding_disabled_flag=1 is always enabled in both anchor and test cases.
Results below show BD-rate gains when DQ and SDH are both disabled for TS blocks.

## Slide 5: Lossy Results + Encoder Fixes
 | All Intra Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | 0.07% | 0.30% | 100% | 101%
Class A2 | 0.01% | -0.09% | -0.05% | 98% | 97%
Class B | -0.02% | -0.03% | 0.05% | 100% | 95%
Class C | -0.11% | -0.01% | -0.05% | 98% | 94%
Class E | -0.01% | 0.01% | -0.22% | 98% | 93%
Overall | -0.05% | -0.01% | 0.01% | 99% | 96%
Class D | -0.11% | 0.07% | 0.05% | 101% | 99%
Class F | -0.99% | -0.58% | -0.55% | 99% | 95%
Class SCC | -1.23% | -1.34% | -1.27% | 101% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.07% | 0.13% | 100% | 101%
Class A2 | 0.00% | 0.09% | -0.05% | 96% | 97%
Class B | -0.01% | -0.05% | -0.15% | 99% | 99%
Class C | -0.15% | -0.03% | 0.04% | 96% | 92%
Class E |  |  |  |  | 
Overall | -0.05% | 0.01% | -0.02% | 98% | 97%
Class D | -0.32% | 0.02% | -0.06% | 100% | 99%
Class F | -0.83% | -0.55% | -0.60% | 99% | 99%
Class SCC | -1.08% | -1.01% | -1.01% | 99% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.16% | 0.05% | 91% | 84%
Class C | -0.20% | -0.28% | -0.09% | 96% | 87%
Class E | -0.11% | 0.38% | 0.03% | 95% | 91%
Overall | -0.10% | -0.07% | 0.00% | 94% | 87%
Class D | -0.38% | -0.16% | 0.57% | 99% | 92%
Class F | -1.21% | 0.01% | -0.64% | 100% | 98%
Class SCC | -1.80% | -1.06% | -1.19% | 94% | 86%
Further encoder improvements are proposed as posted on Ticket #981.
TS blocks that use regular residual coding (RRC) with correct RDOQ function, parameters and contexts.
BDPCM blocks that use RRC use correct BDPCM residual in RDOQ (handling of scan order, etc).

## Slide 6: Lossless Results
 | All Intra |  |  | Random Access |  |  | Low Delay B |  | 
 | Compression Ratio |  | Bit-rate savings | Compression Ratio |  | Bit-rate savings | Compression Ratio |  | bit-rate savings
 | Anchor | Proposal |  | Anchor | Proposal |  | Anchor | Proposal | 
Class A1 | 2.4 | 2.4 | -0.10% | 2.4 | 2.4 | -0.11% |  |  | 
Class A2 | 1.8 | 1.8 | 0.00% | 1.9 | 1.9 | -0.02% |  |  | 
Class B | 2.3 | 2.3 | -0.14% | 2.5 | 2.5 | -0.18% | 2.4 | 2.4 | -0.18%
Class C | 2.1 | 2.1 | -0.23% | 2.6 | 2.6 | -0.32% | 2.6 | 2.6 | -0.33%
Class D | 2.1 | 2.1 | -0.29% | 2.9 | 2.9 | -0.42% | 2.9 | 2.9 | -0.41%
Class E | 3.1 | 3.1 | -0.32% |  |  |  | 3.4 | 3.4 | -0.36%
Class F | 5.8 | 5.8 | -0.47% | 35.2 | 35.4 | -0.56% | 51.4 | 51.9 | -0.65%
TGM | 12.3 | 12.4 | -0.47% | 108.3 | 109.0 | -0.57% | 122.1 | 122.8 | -0.60%
Overall | 2.3 | 2.3 | -0.16% | 2.4 | 2.4 | -0.17% | 2.7 | 2.7 | -0.28%
E. Time[%] | 99% |  |  | 100% |  |  | 100% |  | 
D. Time[%] | 99% |  |  | 99% |  |  | 100% |  | 
RGB | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-8.0 | Proposal |  | VTM-8.0 | Proposal |  | VTM-8.0 | Proposal | 
TGM 1080p | 10.8 | 10.9 | -0.22% | 21.6 | 21.7 | -0.49% | 31.3 | 31.4 | -0.41%
TGM 720p | 5.0 | 5.0 | -0.40% | 6.4 | 6.4 | -0.54% | 11.2 | 11.3 | -0.56%
A | 3.0 | 3.0 | -0.38% | 1.1 | 1.1 | -0.49% | 0.9 | 0.9 | -0.48%
M | 3.0 | 3.0 | -0.47% | 2.4 | 2.4 | -0.65% | 2.6 | 2.6 | -0.66%
CC | 0.9 | 0.9 | -0.03% | 0.1 | 0.1 | -0.05% | 0.1 | 0.1 | -0.04%
Overall | 5.2 | 5.2 | -0.32% | 7.7 | 7.7 | -0.48% | 11.3 | 11.3 | -0.46%
E. Time[%] | 100% |  |  | 101% |  |  | 100% |  | 
D. Time[%] | 99% |  |  | 100% |  |  | 100% |  | 
YUV 444 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
TGM 1080p | 10.7 | 10.7 | -0.26% | 21.8 | 21.8 | -0.36% | 31.5 | 31.6 | -0.41%
TGM 720p | 6.3 | 6.4 | -0.45% | 8.0 | 8.1 | -0.52% | 14.4 | 14.5 | -0.57%
A | 3.5 | 3.5 | -0.36% | 1.0 | 1.0 | -0.45% | 1.0 | 1.0 | -0.45%
M | 3.9 | 3.9 | -0.42% | 3.3 | 3.3 | -0.61% | 3.6 | 3.6 | -0.61%
CC | 1.0 | 1.0 | -0.05% | 0.1 | 0.1 | -0.08% | 0.1 | 0.1 | -0.08%
Overall | 5.8 | 5.8 | -0.33% | 8.3 | 8.3 | -0.43% | 12.4 | 12.4 | -0.46%
E. Time[%] | 100% |  |  | 100% |  |  | 99% |  | 
D. Time[%] | 100% |  |  | 101% |  |  | 98% |  | 
VTM-8.0 is used as the anchor with the appropriate “lossless.cfg” config file on top of the CTC configurations.
DepQuant:1 is enabled both for anchor and test simulations.
The fix in Ticket #988 is further applied for both anchor and test to avoid the reported encoder/decoder mismatch.
Coding gains observed both for YUV420, YUV444 and RGB sequences.

## Slide 7
Variant #4: Spec text is aligned to the VVC software for DQ part.
Only the dequantization part of DQ in spec is disabled for TS blocks as in VVC software.
No change in coding performance.
The following spec changes are proposed, where cyan highlighted text reflect the changes:
… | 
if( ph_dep_quant_enabled_flag ) { | 
QState = startQStateSb | 
for( n = numSbCoeff − 1; n >= 0; n− − ) { | 
xC = ( xS << log2SbW ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 0 ] | 
yC = ( yS << log2SbH ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 1 ] | 
if( AbsLevel[ xC ][ yC ] > 0 ) | 
TransCoeffLevel[ x0 ][ y0 ][ cIdx ][ xC ][ yC ] = ( (transform_skip_flag[ x0 ][ y0 ][ cIdx ] ? 1 : 2 ) * AbsLevel[ xC ][ yC ] − ( ( QState > 1 && transform_skip_flag[ x0 ][ y0 ][ cIdx ] )? 1 : 0 ) ) * ( 1 − 2 * coeff_sign_flag[ n ] ) | 
QState = QStateTransTable[ QState ][ AbsLevel[ xC ][ yC ] & 1 ] | 
} else { | 
sumAbsLevel = 0 | 
for( n = numSbCoeff − 1; n >= 0; n− − ) { | 
xC = ( xS << log2SbW ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 0 ] | 
yC = ( yS << log2SbH ) + DiagScanOrder[ log2SbW ][ log2SbH ][ n ][ 1 ] | 
if( AbsLevel[ xC ][ yC ] > 0 ) { | 
TransCoeffLevel[ x0 ][ y0 ][ cIdx ][ xC ][ yC ] = AbsLevel[ xC ][ yC ] * ( 1 − 2 * coeff_sign_flag[ n ] ) | 
… | 
} | 
} | 
} | 
… | 
7.3.10.11 Residual coding syntax

## Slide 8
It is proposed to disable dependent quantization (DQ) and sign data hiding (SDH) for TS blocks.
Identified following proposals which address the same problem:
  Disable DQ and SDH: JVET-R0141, JVET-R0144, JVET-R0153 (m3), JVET-R0325.
  Disable SDH: JVET-R0116 (m2.2)
Though DQ and SDH can be disabled individually, maximal benefits when observed disabling both.
  This fixes encoder crashes and decoder mismatch issues as reported in Ticket #981.
  Provides coding gains both for lossless and non-CTC lossy cases.
  Lossless coding is now possible in spec text.
  Design becomes more consistent.
Thanks to Canon for the crosscheck.
Conclusion

## Slide 9: Encoder Fixes Only
 | All Intra Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.04% | 0.06% | 99% | 101%
Class A2 | 0.01% | -0.08% | 0.00% | 99% | 99%
Class B | 0.00% | -0.01% | 0.02% | 101% | 96%
Class C | -0.01% | -0.02% | 0.06% | 98% | 95%
Class E | 0.00% | -0.02% | -0.05% | 98% | 92%
Overall | 0.00% | -0.02% | 0.02% | 99% | 96%
Class D | -0.01% | 0.07% | 0.17% | 100% | 98%
Class F | -0.17% | -0.04% | -0.02% | 101% | 103%
Class SCC | -0.39% | -0.48% | -0.45% | 100% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.06% | -0.03% | 99% | 100%
Class A2 | -0.01% | 0.03% | -0.08% | 97% | 99%
Class B | 0.01% | -0.04% | -0.04% | 99% | 100%
Class C | 0.00% | -0.02% | 0.05% | 96% | 92%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | -0.02% | 98% | 98%
Class D | 0.00% | -0.04% | 0.00% | 100% | 101%
Class F | -0.16% | -0.06% | -0.15% | 99% | 101%
Class SCC | -0.31% | -0.33% | -0.30% | 99% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | 0.05% | -0.10% | -0.20% | 97% | 90%
Class E | -0.15% | -0.13% | 0.36% | 96% | 93%
Overall |  |  |  |  | 
Class D | -0.19% | 0.49% | 0.65% | 99% | 97%
Class F | -0.25% | 0.41% | -0.01% | 99% | 99%
Class SCC | -0.41% | -0.27% | -0.30% | 100% | 99%
Results of only encoder improvements are proposed as posted on Ticket #981.