## Slide 1: AHG16: Cleanup of intra reference sample filter selection (JVET-R0280)
Jin Heo, Hyeongmun Jang, Jangwon Choi, Junghak Nam, Moonmo Koo,
Jaehyun Lim, and Seung Hwan Kim

## Slide 2: Summary
Motivation
  Reference sample filter and interpolation filter are determined based on the intra mode checking process
  Basically these two filtering processes do the same function for the intra mode with integer slope
    3-tap reference sample filter coefficient: [1 2 1]/4
    4-tap smoothing filter coefficient: [16 32 16 0]/64
  3-tap reference sample filter can be replaced by 4-tap smoothing filter
Proposed method
  Remove the intra mode checking process and replace reference sample filtering process with smoothing interpolation filtering process
    For clean-up
Experimental results (BD-rate) with VTM-8.0 anchor
  0.00% (AI), 0.00% (RA), and -0.05% (LD)

## Slide 3: Proposed method
Remove the intra mode checking process
Replace the reference sample filtering process with the smoothing interpolation filtering process

## Slide 4: Experimental Results
AI, RA, and LD

## Slide 5: Conclusion
It is proposed to remove intra mode checking process used for intra reference sample filter decision.
Experimental results
  0.00% (AI), 0.00% (RA), and -0.05% (LD)