## Slide 1
GEO with MMVD
JVET-R0282
Krit Panusopone, Seungwook Hong, Limin Wang

## Slide 2: Geometric Partitioning Merge Mode
Merge_gpm_partition_idx indicates split direction for GEO CU
Also determine location of partition 0 and 1
Merge_gpm_idx0/1 indicates merge candidate index that its MV is used as MV of GEO partition 0 and 1, respectively
GEO MV is limited to MV of merge candidates
Geo
gpm_idx0
gpm_idx1
partition

## Slide 3: GEO with MMVD extension
Reuse GEO syntax for split direction and base MV
Explicit signaling to indicate using MVD to refine base GEO MV
Distance and direction components used to calculate MVD
Same MMVD offset LUT as in VVC MMVD
GEO MV = base MV + MMVD offset
  GeoMmvdOffset = (GeoMmvdDistance << 2) * GeoMmvdSign

## Slide 4: GEO with MMVD signaling
Flexible, support one partition only, both partitions, and no refinement
2 flags, geo_mmvd_idx0_flag0/1, one for each GEO partition
4 syntax elements for MVD derivation
  geo_mmvd_distance_idx[0/1], geo_mmvd_direction_idx[0/1]
If (geo_mmvd_idx0_flag == true)
  GEO part 0 MV = base GEO part 0 MV + GEO MMVD part 0 offset
If (geo_mmvd_idx1_flag == true)
  GEO part 1 MV = base GEO part 1 MV + GEO MMVD part 1 offset

## Slide 5: Proposed syntax changes
if( !ciip_flag[ x0 ][ y0 ] ) { | 
merge_gpm_partition_idx[ x0 ][ y0 ] | ae(v)
merge_gpm_idx0[ x0 ][ y0 ] | ae(v)
if( MaxNumGpmMergeCand > 2 ) | 
merge_gpm_idx1[ x0 ][ y0 ] | ae(v)
geo_mmvd_idx0_flag[ x0 ][ y0 ] | ae(v)
geo_mmvd_idx1_flag[ x0 ][ y0 ] | ae(v)
if ( geo_mmvd_idx0_flag[ x0 ][ y0 ] ) { | 
geo_mmvd_distance_idx[ 0 ][ x0 ][ y0 ] | ae(v)
geo_mmvd_direction_idx[ 0 ][ x0 ][ y0 ] | ae(v)
} | 
if ( geo_mmvd_idx1_flag[ x0 ][ y0 ] ) { | 
geo_mmvd_distance_idx[ 1 ][ x0 ][ y0 ] | ae(v)
geo_mmvd_direction_idx[ 1 ][ x0 ][ y0 ] | ae(v)
} | 
} | 

## Slide 6: Simulation result
Proposed method
 | Random Access |  |  | Low Delay B |  | 
 | Y | U | V | Y | U | V
Class A1 | -0.15% | -0.26% | -0.43% |  |  | 
Class A2 | -0.26% | -0.41% | -0.32% |  |  | 
Class B | -0.16% | -0.24% | -0.36% | -0.32% | -0.35% | -0.82%
Class C | -0.42% | -0.53% | -0.83% | -0.77% | -1.32% | -1.25%
Class E |  |  |  | -0.47% | -0.28% | -0.85%
Overall | -0.25% | -0.36% | -0.49% | -0.51% | -0.66% | -0.97%
Class D | -0.41% | -0.57% | -0.81% | -0.68% | -1.55% | -1.32%
Class F | -0.07% | -0.18% | -0.24% | -0.25% | 0.12% | 0.02%

## Slide 7: Conclusions
Extend GEO to allow MVD for each GEO partition MV
Flexible syntax, support one partition only, both partitions, and no refinement
Minor changes in VVC decoding process
Luma BD-rate gains of -0.25% for RA and -0.51% for LB
Propose to adopt GEO extension to allow MMVD style refinement in VVC
Thanks to Qualcomm for crosschecking (JVET-R0407)

## Slide 9: Simulation result
Encoder complexity reduction
 | Random Access |  |  | Low Delay B |  | 
 | Y | U | V | Y | U | V
Class A1 | -0.11% | -0.17% | -0.19% |  |  | 
Class A2 | -0.19% | -0.24% | -0.21% |  |  | 
Class B | -0.09% | -0.23% | -0.15% | -0.17% | -0.25% | -0.14%
Class C | -0.30% | -0.30% | -0.43% | -0.50% | -0.68% | -0.57%
Class E |  |  |  | -0.21% | -0.37% | -0.29%
Overall | -0.17% | -0.24% | -0.24% | -0.29% | -0.43% | -0.32%
Class D | -0.29% | -0.45% | -0.51% | -0.45% | -1.05% | -0.78%
Class F | -0.01% | -0.07% | -0.05% | -0.11% | 0.59% | -0.47%