## Slide 1: JVET-R0366: Simplified disLut for GPM
Yanzhuo Ma, Qihong Ran, Ruipeng Qiu, Haixin Wang,
Junyan Huo, Shuai Wan, Fuzheng Yang,
Yuanfang Yu, Yang Liu
April. 2020

## Slide 2: Problem statement
In VVC Draft
The derivation of weight value for each pixel
0
weightIdx
wValue
8
16
24
-8
-16
-24
32
-32
weightIdx value occur
weightIdx value never occur
4
8
-40
idx | 0 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 11 | 12 | 13 | 14
disLut[idx] | 8 | 8 | 8 | 4 | 4 | 2 | 0 | −2 | −4 | −4 | −8 | −8
idx | 16 | 18 | 19 | 20 | 21 | 22 | 24 | 26 | 27 | 28 | 29 | 30
disLut[idx] | −8 | −8 | −8 | −4 | −4 | −2 | 0 | 2 | 4 | 4 | 8 | 8

## Slide 3: Proposed method
Changing each value to half
0
weightIdx
wValue
8
16
-8
-16
weightIdx value occur
4
8
4
12
-4
-12
20
-20
idx | 0 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 11 | 12 | 13 | 14
disLut[idx] | 4 | 4 | 4 | 2 | 2 | 1 | 0 | −1 | −2 | −2 | −4 | −4
idx | 16 | 18 | 19 | 20 | 21 | 22 | 24 | 26 | 27 | 28 | 29 | 30
disLut[idx] | −4 | −4 | −4 | −2 | −2 | −1 | 0 | 1 | 2 | 2 | 4 | 4

## Slide 4: Experimental results
 |  |  | Random Access |  | 
 | Over VTM8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 97% | 95%
Class A2 | 0.00% | 0.00% | 0.00% | 97% | 97%
Class B | 0.00% | 0.00% | 0.00% | 100% | 98%
Class C | 0.00% | 0.00% | 0.00% | 98% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | 0.00% | 0.00% | 98% | 97%
Class D | 0.00% | 0.00% | 0.00% | 97% | 96%
Class F | 0.00% | 0.00% | 0.00% | 98% | 96%
 |  |  | Low Delay B |  | 
 | Over VTM8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 102% | 97%
Class C | 0.00% | 0.00% | 0.00% | 102% | 96%
Class E | 0.00% | 0.00% | 0.00% | 93% | 93%
Overall | 0.00% | 0.00% | 0.00% | 100% | 96%
Class D | 0.00% | 0.00% | 0.00% | 100% | 98%
Class F | 0.00% | 0.00% | 0.00% | 93% | 92%

## Slide 5: Spec text changes
idx | 0 | 2 | 3 | 4 | 5 | 6 | 8 | 10 | 11 | 12 | 13 | 14
disLut[idx] | 84 | 84 | 84 | 42 | 42 | 21 | 0 | −21 | −42 | −42 | −84 | −84
idx | 16 | 18 | 19 | 20 | 21 | 22 | 24 | 26 | 27 | 28 | 29 | 30
disLut[idx] | −84 | −84 | −84 | −42 | −42 | −21 | 0 | 21 | 42 | 42 | 84 | 84
(1046)
(1047)
(1059)
Table 37 ‑ Specification of the geometric partitioning distance array disLut.
…
…
(1045)

## Slide 6: Conclusion
Proposed to change each value in the disLut to half.
  1 bit could be saved for each value
Coding performance:
RA: 0.00% 0.00% 0.00%, 98% 97%
    LDB: 0.00% 0.00% 0.00%, 100% 96%
  No change on performance and enc./dec. time.
Recommend to adopt into VVC.
Thanks for crosschecking by Kwai.

## Slide 7
Thank you