## Slide 1: AHG10: Deblocking filter setting for VTM JVET-X0063
Han Zhang, Xiang Li, Shan Liu
Tencent

## Slide 2: Summary
Motivation
  In ECM-2.0, the DBF control parameters BetaOffset_div2 and TcOffset_div2 vary with the temporal layer
  But two new syntax elements - pps_beta_offset_div2_num_minus1 and pps_beta_Tc_div2_num_minus1 are also signaled
  In VTM, these parameters are set to the same value
Proposed
  Use temporal layer dependent DBF control parameters in VTM
  Only encoder cfg files changed
  No new syntax elements

## Slide 3: Proposed Method
Temporal layer dependent DBF control parameters in VTM
In line with ECM-2.0 parameters
Only modifying the DBF related parameters in the configuration files
Tid Parameter | I slice | 0 | 1 | 2 | 3 | 4 | 5
BetaOffset_div2 | -2 | -2 | -2 | -2 | -2 | -2 | -2
TcOffset_div2 | -5 | -4 | -3 | -2 | -1 | 0 | 0
Tid Parameter | I slice | 0
BetaOffset_div2 | -3 | -3
TcOffset_div2 | -3 | -3
Tid Parameter | I slice
BetaOffset_div2 | -2
TcOffset_div2 | -5
DBF parameters for LD
DBF parameters for AI
DBF parameters for RA

## Slide 4: Test Results
Anchor is VTM-14.0
 |  |  | All Intra Main10 |  | 
 |  |  | Over VTM-14.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.87% | -0.76% | 0.26% | 100% | 101%
Class A2 | -0.77% | -0.83% | -0.72% | 97% | 98%
Class B | -0.89% | -0.66% | -0.58% | 100% | 100%
Class C | -0.56% | -0.99% | -1.01% | 100% | 97%
Class E | -0.56% | -0.15% | 0.15% | 100% | 101%
Overall | -0.74% | -0.69% | -0.44% | 99% | 99%
Class D | -0.48% | -0.73% | -0.71% | 100% | 101%
Class F | -0.39% | -1.06% | -1.49% | 100% | 98%
 |  |  | Random access Main10 |  | 
 |  |  | Over VTM-14.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.21% | -0.19% | -0.01% | 101% | 101%
Class A2 | -0.42% | -0.27% | -0.36% | 100% | 101%
Class B | -0.39% | -0.67% | -0.54% | 100% | 100%
Class C | -0.23% | -1.00% | -0.94% | 100% | 98%
Class E |  |  |  |  | 
Overall | -0.32% | -0.58% | -0.50% | 100% | 100%
Class D | 0.03% | -0.91% | -0.62% | 101% | 104%
Class F | -0.19% | -1.37% | -1.74% | 101% | 101%
 |  |  | Low delay B Main10 |  | 
 |  |  | Over VTM-14.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.52% | -0.27% | 0.14% | 100% | 99%
Class C | -0.38% | -0.65% | -0.05% | 100% | 100%
Class E | -1.11% | -0.30% | -0.06% | 100% | 102%
Overall | -0.62% | -0.41% | 0.02% | 100% | 100%
Class D | -0.21% | 0.17% | 0.44% | 100% | 101%
Class F | -0.70% | -0.89% | -0.69% | 100% | 96%
 |  |  | Low delay P Main10 |  | 
 |  |  | Over VTM-14.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.36% | -0.34% | 0.01% | 100% | 100%
Class C | -0.23% | -0.48% | -0.07% | 100% | 98%
Class E | -0.45% | 0.17% | -0.29% | 100% | 101%
Overall | -0.34% | -0.26% | -0.09% | 100% | 100%
Class D | -0.22% | -0.29% | 0.67% | 100% | 101%
Class F | -0.44% | -0.64% | -0.73% | 100% | 97%

## Slide 5: Conclusion
Encoder only settings on DBF control parameters for VTM is presented
Coding gains are achieved with similar encoding and decoding time
Propose to adopt the cfg changes into the next version of VTM
Thanks Kwai for crosscheck

## Slide 6: Thanks